3810: Computer Organization
Lecture 10: Memory
Anton Burtsev
October, 2022

---
Datapath With Control
MIPS Datapath
Chapter 4 — The Processor —
[Speaker Notes: Morgan Kaufmann Publishers 26 October 2022 Chapter 4 — The Processor]

---
Designing a Latch
An S-R latch: set-reset latch
When Set is high, a 1 is stored
When Reset is high, a 0 is stored
When both are low, the previous state is preserved (hence,
known as a storage or memory element)
Both are high – this set of inputs is not allowed
Verify the above behavior!
Source: H&P textbook

---
D Latch
Incorporates a clock
The value of the input D signal (data) is stored only when the clock
is high – the previous state is preserved when the clock is low
Source: H&P textbook

---
D Flip Flop
Terminology:
Latch: outputs can change any time the clock is high (asserted)
Flip flop: outputs can change only on a clock edge
Two D latches in series – ensures that a value is stored only on
the falling edge of the clock
Source: H&P textbook

---
Register file
- Two read ports
- One write port

---
Register file (read ports)
- Build from D-flops
- Read ports
  - Multiplexors
  - N-to-1, 32bit wide

---
Common Logic Blocks – Multiplexor
Multiplexor or selector: one of N inputs is reflected on the
output depending on the value of the log2N selector bits
2-input mux
Source: H&P textbook

---
Register file (write ports)
Decoder

---
Common Logic Blocks – Decoder
Takes in N inputs and activates one of 2N outputs
I0 I1 I2 O0 O1 O2 O3 O4 O5 O6 O7
0 0 0 1 0 0 0 0 0 0 0
0 0 1 0 1 0 0 0 0 0 0
0 1 0 0 0 1 0 0 0 0 0
0 1 1 0 0 0 1 0 0 0 0
1 0 0 0 0 0 0 1 0 0 0
1 0 1 0 0 0 0 0 1 0 0
1 1 0 0 0 0 0 0 0 1 0
1 1 1 0 0 0 0 0 0 0 1
3-to-8
Decoder
I0-2
O0-7

---
Register file (write ports)
- What if we read and write the register in the same cycle?
  - add $s0, $s0, $s1

---
MIPS Datapath
Chapter 4 — The Processor —
[Speaker Notes: Morgan Kaufmann Publishers 26 October 2022 Chapter 4 — The Processor]

---
SRAM and DRAM

---
SRAM (Static Random Access Memory)
- Chip select to enable read or write
- Output enable to read

---
Register file vs memory
32-to-1 multiplexor

---
Three-state buffer
- 64K to 1 multiplexors are not practical
- Shared bit line instead
- Output
  - Asserted, deasserted or high-impedance

---
4 x 2 SRAM

---
4M x 8 SRAM
Array of 4K x 1024 arrays

---
DRAM
- SRAM
  - 4-6 transistors
- DRAM
  - 1 transistor

---
DRAM cell

---
4M x 1 DRAM cell
2048 x 2048 array

---
Error correction
- Parity code
  - Counts number of 1s in a word
  - Parity bit (1 for odd, 0 for even)
  - Detects 1 bit error
  - Hence error detection code (EDC)
- Error correction codes are also used
  - 7-8 bits for every 128 bits of data
  - Correct 2-bit errors