CS/EE 3810: Computer Organization
Lecture 13: Branch Prediction &
Out-of-order execution
Anton Burtsev
November, 2022

---
Branch prediction

---
Control Hazards
Simple techniques to handle control hazard stalls:
for every branch, introduce a stall cycle (note: every
    6th instruction is a branch!)
assume the branch is not taken and start fetching the
    next instruction – if the branch is taken, need hardware
    to cancel the effect of the wrong-path instruction
fetch the next instruction (branch delay slot) and
    execute it anyway – if the instruction turns out to be
    on the correct path, useful work was done – if the
    instruction turns out to be on the wrong path,
    hopefully program state is not lost
make a smarter guess and fetch instructions from the
     expected target

---
Branch Delay Slots
Source: H&P textbook

---
Pipeline without Branch Predictor
PC
IF (br)
Reg Read
Compare
Br-target
PC + 4
In the 5-stage pipeline, a branch completes in two cycles 
If the branch went the wrong way, one incorrect instr is fetched 
One stall cycle per incorrect branch

---
Pipeline with Branch Predictor
PC
IF (br)
Reg Read
Compare
Br-target
Branch
Predictor
In the 5-stage pipeline, a branch completes in two cycles 
If the branch went the wrong way, one incorrect instr is fetched 
One stall cycle per incorrect branch

---
1-Bit Bimodal Prediction
For each branch, keep track of what happened last time
and use that outcome as the prediction
What are prediction accuracies for branches 1 and 2 below:
while (1) {
for (i=0;i<10;i++) { branch-1
…
}
for (j=0;j<20;j++) { branch-2
…
}
}

---
2-Bit Bimodal Prediction
For each branch, maintain a 2-bit saturating counter:
if the branch is taken: counter = min(3,counter+1)
if the branch is not taken: counter = max(0,counter-1)
If (counter >= 2), predict taken, else predict not taken
Advantage: a few atypical branches will not influence the
prediction (a better measure of “the common case”)
Especially useful when multiple branches share the same
counter (some bits of the branch PC are used to index
into the branch predictor)
Can be easily extended to N-bits (in most processors, N=2)

---
Bimodal Predictor
Table of
16K entries
of 2-bit
saturating
counters
14 bits
Branch PC

---
Multicycle Instructions
Multiple parallel pipelines – each pipeline can have a different
   number of stages
Instructions can now complete out of order – must make sure
   that writes to a register happen in the correct order

---
An Out-of-Order Processor Implementation
Reorder Buffer (ROB)
Branch prediction
and instr fetch
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Register File
R1-R32
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Decode &
Rename
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
ALU
ALU
ALU
Instr Fetch Queue
Results written to
ROB and tags
broadcast to IQ
Issue Queue (IQ)

---
Example Code
Completion times with in-order with ooo
ADD R1, R2, R3 5 5
ADD R4, R1, R2 6 6
LW R5, 8(R4) 7 7
ADD R7, R6, R5 9 9
ADD R8, R7, R5 10 10
LW R9, 16(R4) 11 7
ADD R10, R6, R9 13 9
ADD R11, R10, R9 14 10

---
An Out-of-Order Processor Implementation
Reorder Buffer (ROB)
Branch prediction
and instr fetch
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Register File
R1-R32
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Decode &
Rename
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
ALU
ALU
ALU
Instr Fetch Queue
Results written to
ROB and tags
broadcast to IQ
Issue Queue (IQ)

---
Design Details - I
Instructions enter the pipeline in order
No need for branch delay slots if prediction happens in time
Instructions leave the pipeline in order – all instructions
that enter also get placed in the ROB – the process of an
instruction leaving the ROB (in order) is called commit –
an instruction commits only if it and all instructions before
it have completed successfully (without an exception)
To preserve precise exceptions, a result is written into the
register file only when the instruction commits – until then,
the result is saved in a temporary register in the ROB

---
Design Details - II
Instructions get renamed and placed in the issue queue –
some operands are available (T1-T6; R1-R32), while
others are being produced by instructions in flight (T1-T6)
As instructions finish, they write results into the ROB (T1-T6)
and broadcast the operand tag (T1-T6) to the issue queue –
instructions now know if their operands are ready
When a ready instruction issues, it reads its operands from
T1-T6 and R1-R32 and executes (out-of-order execution)
Can you have WAW or WAR hazards? By using more
names (T1-T6), name dependences can be avoided

---
Design Details - III
If instr-3 raises an exception, wait until it reaches the top
of the ROB – at this point, R1-R32 contain results for all
instructions up to instr-3 – save registers, save PC of instr-3,
and service the exception
If branch is a mispredict, flush all instructions after the
branch and start on the correct path – mispredicted instrs
will not have updated registers (the branch cannot commit
until it has completed and the flush happens as soon as the
branch completes)
Potential problems: ?

---
Alpha 21264 Out-of-Order Implementation

---
The Alpha 21264 Out-of-Order Implementation
Reorder Buffer (ROB)
Branch prediction
and instr fetch
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Committed
Reg Map
R1P1
R2P2
Register File
P1-P64
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Decode &
Rename
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
ALU
ALU
ALU
Speculative
Reg Map
R1P36
R2P34
Instr Fetch Queue
Results written to
regfile and tags
broadcast to IQ
Issue Queue (IQ)

---
Logical and physical registers

---
Managing Register Names
Temporary values are stored in the register file and not the ROB
Logical
Registers
R1-R32
Physical
Registers
P1-P64
At the start, R1-R32 can be found in P1-P32
Instructions stop entering the pipeline when P64 is assigned
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
What happens on commit?

---
The Commit Process
On commit, no copy is required
The register map table is updated – the “committed” value
of R1 is now in P33 and not P1 – on an exception, P33 is
copied to memory and not P1
An instruction in the issue queue need not modify its
input operand when the producer commits
When instruction-1 commits, we no longer have any use
for P1 – it is put in a free pool and a new instruction can
now enter the pipeline  for every instr that commits, a
new instr can enter the pipeline  number of in-flight
instrs is a constant = number of extra (rename) registers

---
Additional Details
When does the decode stage stall? When we either run
out of registers, or ROB entries, or issue queue entries
Issue width: the number of instructions handled by each
stage in a cycle. High issue width  high peak ILP
Window size: the number of in-flight instructions in the
pipeline. Large window size  high ILP
No more WAR and WAW hazards because of rename
registers – must only worry about RAW hazards

---
The Alpha 21264 Out-of-Order Implementation
Reorder Buffer (ROB)
Branch prediction
and instr fetch
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Committed
Reg Map
R1P1
R2P2
Register File
P1-P64
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Decode &
Rename
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
ALU
ALU
ALU
Speculative
Reg Map
R1P36
R2P34
Instr Fetch Queue
Results written to
regfile and tags
broadcast to IQ
Issue Queue (IQ)

---
Additional Details
When does the decode stage stall? When we either run
out of registers, or ROB entries, or issue queue entries
Issue width: the number of instructions handled by each
stage in a cycle. High issue width  high peak ILP
Window size: the number of in-flight instructions in the
pipeline. Large window size  high ILP
No more WAR and WAW hazards because of rename
registers – must only worry about RAW hazards

---
The Alpha 21264 Out-of-Order Implementation
Reorder Buffer (ROB)
Branch prediction
and instr fetch
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Committed
Reg Map
R1P1
R2P2
Register File
P1-P64
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Decode &
Rename
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
ALU
ALU
ALU
Speculative
Reg Map
R1P36
R2P34
Instr Fetch Queue
Results written to
regfile and tags
broadcast to IQ
Issue Queue (IQ)

---
Thank you!