cs5460/6460: Operating Systems
Midterm recap, sample questions
Anton Burtsev
February, 2023

---
Describe the x86 address translation pipeline (draw figure), explain stages.

---
Address translation

---
What is the linear address? What address is in the registers, e.g., in %eax?

---
Logical and linear addresses
Segment selector (16 bit) + offset (32 bit)

---
What segments do the following instructions use? push, jump, mov

---
Programming model
- Segments for: code, data, stack, “extra”
  - A program can have up to 6 total segments
  - Segments identified by registers: cs, ds, ss, es, fs, gs
- Prefix all memory accesses with desired segment:
  - mov eax, ds:0x80 (load offset 0x80 from data into eax)
  - jmp cs:0xab8 (jump execution to code offset 0xab8)
  - mov ss:0x40, ecx (move ecx to stack offset 0x40)

---
Segmented programming (not real)
static int x = 1;
int y; // stack
if (x) {
    y = 1;
    printf (“Boo”);
} else
    y = 0;
ds:x = 1; // data
ss:y; // stack
if (ds:x) {
   ss:y = 1;
   cs:printf(ds:“Boo”);
} else
   ss:y = 0;

---
Describe the linear to physical address translation with the paging mechanism (use provided diagram, mark and explain the steps).

---
Page translation

---
Page translation

---
Page directory entry (PDE)
- 20 bit address of the page table
  - Pages 4KB each, we need 1M to cover 4GB
- R/W – writes allowed?
  - To a 4MB region controlled by this entry
- U/S – user/supervisor
  - If 0 – user-mode access is not allowed
- A – accessed

---
Page translation

---
Page table entry (PTE)
- 20 bit address of the 4KB page
  - Pages 4KB each, we need 1M to cover 4GB
- R/W – writes allowed?
  - To a 4KB page
- U/S – user/supervisor
  - If 0 user-mode access is not allowed
- A – accessed
- D – dirty – software has written to this page

---
Page translation

---
Consider the following 32-bit x86 page table setup.
%cr3 holds 0x00001000.
The Page Directory Page at physical address 0x00001000:
PDE 0: PPN=0x00002, PTE_P, PTE_U, PTE_W
PDE 1: PPN=0x00003, PTE_P, PTE_U, PTE_W
PDE 2: PPN=0x00002, PTE_P, PTE_U, PTE_W
... all other PDEs are zero
The Page Table Page at physical address 0x00002000 (which is PPN 0x00002):
PTE 0: PPN=0x00005, PTE_P, PTE_U, PTE_W
PTE 1: PPN=0x00006, PTE_P, PTE_U, PTE_W
... all other PTEs are zero
The Page Table Page at physical address 0x00003000:
PTE 0: PPN=0x00005, PTE_P, PTE_U, PTE_W
PTE 1: PPN=0x00005, PTE_P, PTE_U, PTE_W
... all other PTEs are zero
List all virtual addresses that map to physical address 0x00005555

---
Consider the following 32-bit x86 page table setup.
%cr3 holds 0x00001000.
The Page Directory Page at physical address 0x00001000:
PDE 0: PPN=0x00002, PTE_P, PTE_U, PTE_W
PDE 1: PPN=0x00003, PTE_P, PTE_U, PTE_W
PDE 2: PPN=0x00002, PTE_P, PTE_U, PTE_W
... all other PDEs are zero
The Page Table Page at physical address 0x00002000 (which is PPN 0x00002):
PTE 0: PPN=0x00005, PTE_P, PTE_U, PTE_W
PTE 1: PPN=0x00006, PTE_P, PTE_U, PTE_W
... all other PTEs are zero
The Page Table Page at physical address 0x00003000:
PTE 0: PPN=0x00005, PTE_P, PTE_U, PTE_W
PTE 1: PPN=0x00005, PTE_P, PTE_U, PTE_W
... all other PTEs are zero
List all virtual addresses that map to physical address 0x00005555
Answer: 0x00000555, 0x00400555, 0x00401555, 0x00800555

---
What's on the stack? Describe layout of a stack and how it changes during function invocation?

---
Example stack
: :
| 10 | [ebp + 16] (3rd function argument)
| 5 | [ebp + 12] (2nd argument)
| 2 | [ebp + 8] (1st argument)
| RA | [ebp + 4] (return address)
| FP | [ebp] (old ebp value)
| | [ebp - 4] (1st local variable)
: :
: :
| | [ebp - X] (esp - the current stack pointer)

---
Thank you!