## Slide 1: cs5460/6460 Operating Systems Lecture 03: x86 instruction set
Anton Burtsev
January, 2024

## Slide 2
How do CPUs work internally?

## Slide 3: CPU execution loop
CPU repeatedly reads instructions from memory
Executes them
Example
ADD EDX, EAX
// EDX = EAX + EDX

## Slide 5
What are those instructions?
(a brief introduction to x86 instruction set)
This part is based on David Evans’ x86 Assembly Guide
http://www.cs.virginia.edu/~evans/cs216/guides/x86.html
and Yale FLINT’s group version of the same manual converted to GNU ASM syntax
https://flint.cs.yale.edu/cs421/papers/x86-asm/asm.html

## Slide 6: Note
We’ll be talking about 32bit x86 instruction set
  The version of xv6 we will be using in this class is a 32bit operating system
  You’re welcome to take a look at the 64bit port

## Slide 7: x86 instruction set
The full x86 instruction set is large and complex
  But don’t worry, the core part is simple
  The rest are various extensions (often you can guess what they do, or quickly look it up in the manual)

## Slide 8: x86 instruction set
Three main groups
  Data movement (from memory and between registers)
  Arithmetic operations (addition, subtraction, etc.)
  Control flow (jumps, function calls)

## Slide 9: General registers
8 general registers
  32bits each
Two (ESP and EBP) have a special role
Others are more or less general
  Used in arithmetic instructions, control flow decisions, passing arguments to functions, etc.

## Slide 10: BTW, where are these registers?

## Slide 11: Registers and Memory

## Slide 12
Global (static) variables

## Slide 13: Declaring static data regions
Data declarations are preceded by the .DATA directive
DB (declare byte)
DW (declare two byte location aka word)
DD (declare four byte locattion aka double word)
.DATA
var DB 64 ; Declare a byte, referred to as location var,
; containing the value 64
var2 DB ? ; Declare an uninitialized byte,
; referred to as location var2
DB 10 ; Declare a byte with no label, containing the value 10
; Its location is var2 + 1
X DW ? ; Declare a 2-byte uninitialized value, location X
Y DD 30000 ; Declare a 4-byte value, location Y, initialized to 30000

## Slide 14: Arrays
Simply a number of cells in memory
Z DD 1, 2, 3 ; Declare three 4-byte values, initialized to
; 1, 2, and 3. The value of location Z + 8 is 3
DUP – duplicate expression a given number of times
bytes DB 10 DUP(?) ; Declare 10 uninitialized bytes starting at
; location bytes
arr DD 100 DUP(0) ; Declare 100 4-byte words starting at location
; arr, all initialized to 0
String literals
str DB 'hello',0 ; Declare 6 bytes starting at the address str,
; initialized to the ASCII character values for
; hello and the null (0) byte

## Slide 15
Data movement instructions

## Slide 16: We use the following notation
<reg32> Any 32-bit register (EAX,EBX,ECX,EDX,ESI,EDI,ESP,EBP)
<reg16> Any 16-bit register (AX, BX, CX, or DX)
<reg8> Any 8-bit register (AH, BH, CH, DH, AL, BL, CL, DL)
<reg> Any register
<mem> A memory address (e.g., [eax], [var + 4],
or dword ptr [eax+ebx])
<con32> Any 32-bit constant
<con16> Any 16-bit constant
<con8> Any 8-bit constant
<con> Any 8-, 16-, or 32-bit constant

## Slide 17: mov instruciton
Copies the data item referred to by its second operand (i.e. register contents, memory contents, or a constant value) into the location referred to by its first operand (i.e. a register or memory).
  Register-to-register moves are possible
  Direct memory-to-memory moves are not
Syntax
mov <reg>,<reg>
mov <reg>,<mem>
mov <mem>,<reg>
mov <reg>,<const>
mov <mem>,<const>

## Slide 18: mov examples
mov eax, ebx ; copy the value in ebx into eax
mov byte ptr [var], 5 ; store 5 into the byte at location var
mov eax, [ebx] ; Move the 4 bytes in memory at the address
; contained in EBX into EAX
mov [var], ebx ; Move the contents of EBX into the 4 bytes
; at memory address var.
; (Note, var is a 32-bit constant).
mov eax, [esi-4] ; Move 4 bytes at memory address ESI + (-4)
; into EAX
mov [esi+eax], cl ; Move the contents of CL into the byte at
; address ESI+EAX

## Slide 19: mov: access to data structures
struct point {
int x; // x coordinate (4 bytes)
int y; // y coordinate (4 bytes)
}
struct point points[128]; // array of 128 points
// load y coordinate of i-th point into y
int y = points[i].y;
; ebx is address of the points array, eax is i
mov edx, [ebx + 8*eax + 4] ; Move y of the i-th
; point into edx

## Slide 20: lea load effective address
The lea instruction places the address specified by its second operand into the register specified by its first operand
  The contents of the memory location are not loaded, only the effective address is computed and placed into the register
  This is useful for obtaining a pointer into a memory region

## Slide 21: lea vs mov access to data structures
mov
// load y coordinate of i-th point into y
int y = points[i].y;
; ebx is address of the points array, eax is i
mov edx, [ebx + 8*eax + 4] ; Move y of the i-th point into edx
lea
// load the address of the y coordinate of the i-th point into p
int *p = &points[i].y;
; ebx is address of the points array, eax is i
lea esi, [ebx + 8*eax + 4] ; Move address of y of the i-th point
; into esi

## Slide 22: lea is often used instead of add
Compared to add, lea can
perform addition with either two or three operands
  store the result in any register; not just one of the source operands.
  Examples
LEA EAX, [ EAX + EBX + 1234567 ]
; EAX = EAX + EBX + 1234567 (three operands)
LEA EAX, [ EBX + ECX ] ; EAX = EBX + ECX
; Add without overriding EBX or ECX with the result
LEA EAX, [ EBX + N * EBX ] ; multiplication by constant
; (limited set, by 2, 3, 4, 5, 8, and 9 since N is
; limited to 1,2,4, and 8).

## Slide 23
Arithmetic and logic instructions

## Slide 24: add Integer addition
The add instruction adds together its two operands, storing the result in its first operand
  Both operands may be registers
  At most one operand may be a memory location
Syntax
add <reg>,<reg>
add <reg>,<mem>
add <mem>,<reg>
add <reg>,<con>
add <mem>,<con>

## Slide 25: add examples
add eax, 10 ; EAX ← EAX + 10
add BYTE PTR [var], 10 ; add 10 to the
; single byte stored at
; memory address var

## Slide 26: sub Integer subtraction
The sub instruction stores in the value of its first operand the result of subtracting the value of its second operand from the value of its first operand.
Examples
sub al, ah ; AL ← AL - AH
sub eax, 216 ; subtract 216 from the value
; stored in EAX

## Slide 27: inc, dec Increment, decrement
The inc instruction increments the contents of its operand by one
The dec instruction decrements the contents of its operand by one
Examples
dec eax ; subtract one from the contents
; of EAX
inc DWORD PTR [var] ; add one to the 32-
; bit integer stored at
; location var

## Slide 28: and, or, xor Bitwise logical and, or, and exclusive or
These instructions perform the specified logical operation (logical bitwise and, or, and exclusive or, respectively) on their operands, placing the result in the first operand location
Examples
and eax, 0fH ; clear all but the last 4
; bits of EAX
xor edx, edx ; set the contents of EDX to
; zero

## Slide 29: shl, shr shift left, shift right
These instructions shift the bits in their first operand's contents left and right, padding the resulting empty bit positions with zeros
The shifted operand can be shifted up to 31 places. The number of bits to shift is specified by the second operand, which can be either an 8-bit constant or the register CL
  In either case, shifts counts of greater then 31 are performed modulo 32.
Examples
shl eax, 1 ; Multiply the value of EAX by 2
; (if the most significant bit is 0)
shr ebx, cl ; Store in EBX the floor of result of dividing
; the value of EBX by 2^n
; where n is the value in CL.

## Slide 30: More instructions… (similar)
Multiplication imul
imul eax, [var] ; multiply the contents of EAX by the
; 32-bit contents of the memory
; location var. Store result in EAX
imul esi, edi, 25 ; ESI ← EDI * 25
Division idiv
not - bitvise logical not (flips all bits)
neg - negation
  neg eax ; EAX ← - EAX

## Slide 31: This is enough to do arithmetic

## Slide 32: Poll Q1: What is inside ebx?
After we execute the mov instruction?
; eax = 2
; ebx = 3
mov ebx, eax
; what is the value of eax here?

## Slide 33
Notes: Do not modify the notes in this section to avoid tampering with the Poll Everywhere activity. More info at polleverywhere.com/support What is inside ebx?
https://www.polleverywhere.com/multiple_choice_polls/lrCccnGm68FB3B7E5O6Sj?state=opened&flow=Default&onscreen=persist

## Slide 34: Poll Q2: What is this instruction doing?
mov ebx, [eax]
; Is it writing memory? Or reading it?

## Slide 35
Notes: Do not modify the notes in this section to avoid tampering with the Poll Everywhere activity. More info at polleverywhere.com/support What is this instruciton mov ebx, [eax] doing?
https://www.polleverywhere.com/multiple_choice_polls/Nu5xKXhHLrsm0NopeA8pm?state=opened&flow=Default&onscreen=persist

## Slide 36: Poll Q3: Is this a legal instruction
mov [ebx], [eax]

## Slide 37
Notes: Do not modify the notes in this section to avoid tampering with the Poll Everywhere activity. More info at polleverywhere.com/support Is this a legal x86 instruction? mov [eax], [ebx]
https://www.polleverywhere.com/multiple_choice_polls/kDWvtqhRVLbMKc48fwMVg?state=opened&flow=Default&onscreen=persist

## Slide 38
Control flow instructions

## Slide 40: EIP instruction pointer
EIP is a 32bit value indicating the location in memory where the current instruction starts (i.e., memory address of the instruction)
EIP cannot be changed directly
  Normally, it increments to point to the next instruction in memory
  But it can be updated implicitly by provided control flow instructions

## Slide 41: Labels
<label> refers to a labeled location in the program text (code).
Labels can be inserted anywhere in x86 assembly code text by entering a label name followed by a colon
Examples
mov esi, [ebp+8]
begin: xor ecx, ecx
mov eax, [esi]

## Slide 42: jump: jump
Transfers program control flow to the instruction at the memory location indicated by the operand.
Syntax
jmp <label>
Example
begin: xor ecx, ecx
...
jmp begin ; jump to instruction labeled
; begin

## Slide 43: jcondition: conditional jump
Jumps only if a condition is true
  The status of a set of condition codes that are stored in a special register (EFLAGS)
  EFLAGS stores information about the last arithmetic operation performedm for example,
    Bit 6 of EFLAGS indicates if the last result was zero
    Bit 7 indicates if the last result was negative
Based on these bits, different conditional jumps can be performed
  For example, the jz instruction performs a jump to the specified operand label if the result of the last arithmetic operation was zero
  Otherwise, control proceeds to the next instruction in sequence

## Slide 44: Conditional jumps
Most conditional jump follow the comparison instruction (cmp, we’ll cover it below)
Syntax
je <label> (jump when equal)
jne <label> (jump when not equal)
jz <label> (jump when last result was zero)
jg <label> (jump when greater than)
jge <label> (jump when greater than or equal to)
jl <label> (jump when less than)
jle <label> (jump when less than or equal to)
Example: if EAX is less than or equal to EBX, jump to the label done. Otherwise, continue to the next instruction
cmp eax, ebx
jle done

## Slide 45: cmp: compare
Compare the values of the two specified operands, setting the condition codes in EFLAGS
  This instruction is equivalent to the sub instruction, except the result of the subtraction is discarded instead of replacing the first operand.
Syntax
cmp <reg>,<reg>
cmp <reg>,<mem>
cmp <mem>,<reg>
cmp <reg>,<con>
Example: if the 4 bytes stored at location var are equal to the 4-byte integer constant 10, jump to the location labeled loop.
cmp DWORD PTR [var], 10
jeq loop

## Slide 46
Stack and procedure calls

## Slide 47
What is stack?

## Slide 48: Stack
It's just a region of memory
  Pointed by a special register ESP
You can change ESP
  Get a new stack

## Slide 49
Why do we need stack?

## Slide 50: Calling functions
// some code...
foo();
// more code..
Stack contains information for how to return from a subroutine
  i.e., from foo()
Functions can be called from different places in the program
if (a == 0) {
foo();
…
} else {
foo();
…
}

## Slide 51: Stack
Main purpose:
  Store the return address for the current procedure
  Caller pushes return address on the stack
  Callee pops it and jumps

## Slide 52: Stack
Main purpose:
  Store the return address for the current procedure
  Caller pushes return address on the stack
  Callee pops it and jumps

## Slide 53: Call/return
CALL instruction
  Makes an unconditional jump to a subprogram and pushes the address of the next instruction on the stack
push eip + sizeof(CALL) ; save return
; address
jmp _my_function
RET instruction
  Pops off an address and jumps to that address

## Slide 54: Stack
Other uses:
  Local data storage
  Parameter passing
  Evaluation stack
    Register spill

## Slide 55: Manipulating stack
ESP register
  Contains the memory address of the topmost element in the stack
PUSH instruction
push 0xBAR
  Subtract 4 from ESP
  Insert data on the stack

## Slide 56: Manipulating stack
POP instruction
pop EAX
  Removes data from the stack
  Saves in register or memory
  Adds 4 to ESP

## Slide 57: Some examples

## Slide 58
Thank you!