## Slide 1: How can Computational Geometry help Mobile Networks: Geometry in Wireless Sensor Networks
Jie Gao
Stony Brook University
CG Week 2012
Algorithms in the Field Workshop

## Slide 2: A generic sensor node
CPU.
On-board flash memory or external memory
Sensors: thermometer, camera, motion, light sensor, etc.
Wireless radio.
Battery.

## Slide 3: Sensor Networks

## Slide 4: Applications
Initially: Scientific Monitoring
  High-resolution data collection and monitoring.
  Deploy sensors in a remote region, collect data to a base station.
Examples
  Habitat monitoring of animal behaviors
  Environment monitoring (redwoods, golden gate bridge, tunnels, etc)

## Slide 5: Applications
Later: Cyber Physical Systems (CPS), Internet of Things (IoT)
  Real-time data acquisition.
  Situation understanding.
  Event response and control.
Examples:
  Health monitoring
  Smart buildings; green buildings
  SmartGrid
Sensing
Control
Environment

## Slide 6: Applications
Emerging: Participatory Sensing
  Sensors on cellular phones (GPS, microphone, cameras…)
  “Crowdsourcing”
  Devices are available, charged & maintained.
Applications
  Social activities (foursquare)
  Traffic monitoring (waze)

## Slide 7: Where is the geometry?
Sensor locations
  Points in the plane
  Points on a terrain
  Points in 3D
  Mobile sensors

## Slide 8: Where is the geometry?
Sensor communication models
  Short-range communication (for reducing energy consumption/interference)
  E.g. Unit disk graph model (UDG)

## Slide 9: Where is the geometry?
Sensing models
  Isotropic: point, disk.
  Non-isotropic: camera, laser.

## Slide 10: Where is the geometry?
Sensor data
  Spatial & temporal correlation in most physical phenomena

## Slide 11: Model is important
Captures important properties
Simple enough s.t. interesting results can be proved.
Multiple interesting models & solutions.

## Slide 12: Two case study
Network localization
Geometric routing

## Slide 13: Network Localization
Given a network of sensors, find their (absolute or relative) positions.
Input:
  Network connectivity.
  (optional) noisy edge length.
  (optional) noisy angles.

## Slide 14: Unit disk graph realization
Given a graph, can you realize it as a unit disk graph in R2?
?

## Slide 15: Unit disk graph realization
Given a graph, can you realize it as a unit disk graph in R2?
NP-complete [Breu, Kirkpatrick’98]
NP-hard to approx. within √1.5 [Kuhn, Moscibroda, Wattenhofer’04]
NP-complete w. edge lengths [Aspnes, Goldenberg, Yang’04; Bâdoiu, Demaine, Hajiaghayi, Indyk’04]
NP-complete w. angles [Bruck, Gao, Jiang’05]
NP-complete w. noisy edge length & angles [Basu, Gao, Mitchell, Sabhnani’06]

## Slide 16: Unit disk graph realization
Approximation?
Known: O(log2.5 n log log n) on ratio of longest edge/ shortest non-edge [Kuhn, Moscibroda, Wattenhofer’04]
Open question: O(1)-approximation?
Given a combinatorial UDG, embed all neighbors to be within distance 1, and all non-neighbors at least α apart, for a constant α.

## Slide 17: Why is UDG realization so hard?
Intuitively,
AC, BC is an edge  |AC| ≤ 1; |BC| ≤ 1
AB is not an edge  |AB| >1
Not convex!
Packing disjoint disks rep. independent set!
Formally, all proofs use reduction from 3-SAT.
A
B
C

## Slide 18
Unit disk graph recognition is NP-hard, Breu & Kirkpatrick, 1998.
Truth setting gadget
Independent set
cage

## Slide 19: 2nd challenge: flip ambiguity
Given two triangles with fixed edge length, one can flip one triangle relative to the other.
Incorrect global flip.

## Slide 20: Rigidity and global rigidity
Rigidity: no continuous deformation
Global rigidity: unique embedding in R2
Rigid, not globally rigid
Globally rigid
Not rigid

## Slide 21: 2D rigidity is well understood!
A graph is rigid in 2D if and only if it contains a Laman graph on its vertices.
A Laman graph has n vertices, 2n-3 edges and any subset of k vertices spans at most 2k-3 edges.

## Slide 22: Global rigidity
A graph is globally rigid in 2D iff it is 3-connected and redundantly rigid (rigid upon the removal of an edge).
Rigid, not globally rigid
Globally rigid
[Berg, Jordan 2003] [Hendrickson 1992]

## Slide 23: Recognizing rigidity is easy
Pebble game: test whether a graph is generically rigid in time O(nm), n=|V|, m=|E|.
Testing global rigidity?
  Test redundant rigidity
  Test 3-connectivity.
D. J. Jacobs and B. Hendrickson, An Algorithm for two dimensional rigidity percolation: The pebble game. J. Comput. Phys., 137:346-365, 1997.

## Slide 24: But finding an embedding is hard!
Given a graph with edge lengths specified, finding a valid graph realization in Rd for a fixed dimension d is NP-complete.
Rank constraint is non-convex.
1st idea: embed in Rn and project down to R2 – multi-dimensional scaling.
2nd idea: poly time algorithm for special families of graphs.
What about dense graphs?

## Slide 25: A detour
Look at a different model of the network.

## Slide 26
Local view

## Slide 27
obstacles
Global view

## Slide 28: Large-scale sensor field
large-scale, dense deployment.
  Sufficient sensor coverage.
w/ holes/obstacles.
Prominent feature: shape of the network.

## Slide 29: Graph abstraction of sensor networks
The “graph” view of a sensor network depends very much on the network connectivity, which is not stable: links come and go, nodes fail…
Dynamic graph problems, in general, are difficult problems.

## Slide 30: Geometric View of Sensor Networks
The global geometry/ topology is stable
We know how to handle shapes
obstacle

## Slide 31: Network Localization
Large, dense sensor field with complex geometry.
Nearby nodes are able to communicate.
Use connectivity information only.
Recover the relative positioning.
Surface reconstruction?

## Slide 32: The algorithm
Select landmarks on the boundary.
Landmark Voronoi diagram:
Nodes identify closest landmark under network distance
Combinatorial Delaunay complex:
Neighboring landmarks connected by an edge
[Lederer, Wang, Gao, 2008].

## Slide 33: The algorithm, cont
Embed the combinatorial Delaunay complex
  Edge length = network hop count
  Glue adjacent triangles side by side.

## Slide 34: No flip ambiguity for Delaunay triangles
Recall: we want to embed as a simplicial complex.
  Intersection of two simplices is empty or is a common face.
good
bad

## Slide 35: Algorithm, cont
Embed the rest of the nodes.
  Each node embeds itself with hop-count distances to nearby 3 landmarks.

## Slide 36: Are we done?
How to select landmarks?
Make sure the Delaunay complex is rigid.

## Slide 37: Landmark selection condition
If the Voronoi diagram (Voronoi edges and vertices) is connected in R, then the Delaunay graph is rigid.
Sampling criterion:
Each boundary point p
has a landmark
within LFS(p).

## Slide 38: Two case study
Network localization
Geometric routing

## Slide 39: Greedy Routing in Sensor Networks
Assign coordinates to nodes
Message moves to neighbor closest to destination
Simple, compact, scalable

## Slide 40: Greedy routing may get stuck
Can get stuck
Lake
Find a different embedding so that greedy routing does not get stuck!

## Slide 41: Greedy embedding
Given a graph G, find an embedding of the vertices in Rd, s.t. for each pair of nodes s, t, there is a neighbor of s closer to t than s itself.
Q: how to compute?
s
t
C. H. Papadimitriou and D. Ratajczak. On a conjecture related to geometric routing. Theor. Comput. Sci., 344(1):3–14, 2005.

## Slide 42: Greedy embedding does not always exist
≤π/3
A star with ≥ 6 leaves does not have a greedy embedding in R2
Not the longest distance in Δab2b3
Source
Destination

## Slide 43: Conjecture [Papadimitriou, Ratajczak]
Any planar 3-connected graph has a greedy embedding R2.
Any 3-connected planar graph is the edge graph of a 3D convex polytope, with edges tangent to a sphere. [Steinitz 1922].

## Slide 44: Polyhedral routing
Distance is a linear function  single global minimum.
For destination v, d(u, v) is minimum if u=v.
No stuck point due to convexity.
Theorem: Greedy routing with the distance function d(u, v) = - e(u)e(v) guarantees delivery.

## Slide 45: Progress on the conjecture
Dhandapani proved that any triangulation admits a greedy embedding (SODA’08).
Leighton and Moitra proved the conjecture (FOCS’08).
Independently, Angelini et al. also proved it (Graph Drawing’08).

## Slide 46: Leighton and Moitra’s Proof
All 3-connected planar graphs contain a spanning Christmas Cactus graph.
All Christmas Cactus graphs admit a greedy embedding in the plane.

## Slide 47: A Christmas Cactus

## Slide 48: Christmas cactus graph
A cactus graph is connected, each edge is in at most one simple cycle.
A Christmas Cactus graph is a cactus graph for which the removal of any node disconnects it into at most 2 pieces.
“Tree of cycles”

## Slide 49: How does the embedding look like?
Requires high resolution!
Ω(n log n) bit size coordinates! [Eppstein, Goodrich’08]
Leighton and Moitra

## Slide 50: Succinct greedy drawing
Goal: o(n log n) bit size coordinates.
But this is in general impossible. [Battista, Frati, Angelini, 2009].
Notice: no need to store exact coordinates, only need comparison.
Goldrich and Strash show compressed representation of “Christmas cactus embedding” using O(log n) size storage.

## Slide 51: Greedy drawing
Very nice theory
In practice: links go up and down.
Maintaining the greedy drawing is non-trivial.
Switch to the geometric view.

## Slide 52: Greedy routing get stuck at “holes”
Can get stuck
x
y
z
Lake

## Slide 53: Deform the holes to be circular
Greedy routing does not get stuck at circular holes. [Sarkar, Yin, Gao, Luo, Gu, 2009]

Conformal map!

## Slide 54: Conformal map for greedy routing
Curvature flow (Ricci flow) is a natural distributed algorithm.
Deform a complex shape to a simple one, making it easy to explore the space of paths.
  Multi-path routing
  Recover from link failure
  Find routes of different homotopy types

## Slide 55: Möbius Transform
Möbius transform
  Conformal: maps circles to circles
a, b, c, d are 4 complex numbers, ad ≠ bc


## Slide 56: Recover from link failure
Apply a Möbius transformation & route in an alternative embedding. [Jiang, Ban, Goswami, Zeng, Gao, Gu, 2011]

## Slide 57: Embed into hyperbolic plane
Greedy routing on the universal covering space finds paths of different homotopy types. [Zeng, Sarkar, Luo, Gu, Gao, 2010]

## Slide 58: Conclusion
Many nice geometric problems
Modeling the problem is important
“All models are wrong, but some are useful.” [George E. P. Box]
Unit disk graph model
In reality,

## Slide 59: Questions and Comments
http://www.cs.sunysb.edu/~jgao
jgao@cs.sunysb.edu
Jie Gao and Leo Guibas, Geometric Algorithms for Sensor Networks, Philosophical Transactions of the Royal Society A, 2012.