## Slide 1
Lecture 5: More Instructions, Procedure Calls
Today’s topics:
  Memory layout, numbers, control instructions
  Procedure calls
  Recaps: cycle time and frequency, addr/value

## Slide 2
Example
Convert to assembly:
C code: d[3] = d[2] + a;
Assembly (same assumptions as previous example):
lw $s0, 0($gp) # a is brought into $s0
lw $s1, 20($gp) # d[2] is brought into $s1
add $t1, $s0, $s1 # the sum is in $t1
sw $t1, 24($gp) # $t1 is stored into d[3]
Assembly version of the code continues to expand!

## Slide 3
Memory Organization
The space allocated on stack by a procedure is termed the activation
record (includes saved values and data local to the procedure) – frame
pointer points to the start of the record and stack pointer points to the
end – variable addresses are specified relative to $fp as $sp may
change during the execution of the procedure
$gp points to area in memory that saves global variables
Dynamically allocated storage (with malloc()) is placed on the heap
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)

## Slide 4
Recap – Numeric Representations
Decimal 3510 = 3 x 101 + 5 x 100
Binary 001000112 = 1 x 25 + 1 x 21 + 1 x 20
Hexadecimal (compact representation)
0x 23 or 23hex = 2 x 161 + 3 x 160
0-15 (decimal)  0-9, a-f (hex)
Dec Binary Hex
0 0000 00
1 0001 01
2 0010 02
3 0011 03
Dec Binary Hex
4 0100 04
5 0101 05
6 0110 06
7 0111 07
Dec Binary Hex
8 1000 08
9 1001 09
10 1010 0a
11 1011 0b
Dec Binary Hex
12 1100 0c
13 1101 0d
14 1110 0e
15 1111 0f

## Slide 5
Instruction Formats
Instructions are represented as 32-bit numbers (one word),
broken into 6 fields
R-type instruction add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
op rs rt rd shamt funct
opcode source source dest shift amt function
I-type instruction lw $t0, 32($s3)
6 bits 5 bits 5 bits 16 bits
opcode rs rt constant

## Slide 6
Logical Operations
Logical ops C operators Java operators MIPS instr
Shift Left << << sll
Shift Right >> >>> srl
Bit-by-bit AND & & and, andi
Bit-by-bit OR | | or, ori
Bit-by-bit NOT ~ ~ nor

## Slide 7
Control Instructions
Conditional branch: Jump to instruction L1 if register1
equals register2: beq register1, register2, L1
Similarly, bne and slt (set-on-less-than)
Unconditional branch:
j L1
jr $s0 (useful for big jumps and procedure returns)
Convert to assembly:
if (i == j)
f = g+h;
else
f = g-h;

## Slide 8
Control Instructions
Conditional branch: Jump to instruction L1 if register1
equals register2: beq register1, register2, L1
Similarly, bne and slt (set-on-less-than)
Unconditional branch:
j L1
jr $s0 (useful for big jumps and procedure returns)
Convert to assembly:
if (i == j) bne $s3, $s4, Else
f = g+h; add $s0, $s1, $s2
else j Exit
f = g-h; Else: sub $s0, $s1, $s2
Exit:

## Slide 9
Example
Convert to assembly:
while (save[i] == k)
i += 1;
Values of i and k are in $s3 and
$s5 and base of array save[] is
in $s6

## Slide 10
Example
Convert to assembly:
while (save[i] == k)
i += 1;
Values of i and k are in $s3
and $s5 and base of array
save[] is in $s6
Loop: sll $t1, $s3, 2
add $t1, $t1, $s6
lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3, 1
j Loop
Exit:
sll $t1, $s3, 2
add $t1, $t1, $s6
Loop: lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3, 1
addi $t1, $t1, 4
j Loop
Exit:

## Slide 11
Registers
The 32 MIPS registers are partitioned as follows:
  Register 0 : $zero always stores the constant 0
  Regs 2-3 : $v0, $v1 return values of a procedure
  Regs 4-7 : $a0-$a3 input arguments to a procedure
  Regs 8-15 : $t0-$t7 temporaries
  Regs 16-23: $s0-$s7 variables
  Regs 24-25: $t8-$t9 more temporaries
  Reg 28 : $gp global pointer
  Reg 29 : $sp stack pointer
  Reg 30 : $fp frame pointer
  Reg 31 : $ra return address

## Slide 12
Procedures
Local variables, AR, $fp, $sp
Scratchpad and saves/restores
Arguments and returns
jal and $ra