## Slide 1
Lecture 10: Division, Floating Point
Today’s topics:
  Division
  IEEE 754 representations

## Slide 2
Division
1001ten Quotient
Divisor 1000ten | 1001010ten Dividend
-1000
10
101
1010
-1000
10ten Remainder
At every step,
  shift divisor right and compare it with current dividend
  if divisor is larger, shift 0 as the next bit of the quotient
  if divisor is smaller, subtract to get new dividend and shift 1
  as the next bit of the quotient

## Slide 3
Division
1001ten Quotient
Divisor 1000ten | 1001010ten Dividend
0001001010 0001001010 0000001010 0000001010
100000000000  0001000000 00001000000000001000
Quo: 0 000001 0000010 000001001
At every step,
  shift divisor right and compare it with current dividend
  if divisor is larger, shift 0 as the next bit of the quotient
  if divisor is smaller, subtract to get new dividend and shift 1
  as the next bit of the quotient

## Slide 4
Divide Example
Divide 7ten (0000 0111two) by 2ten (0010two)
Iter | Step | Quot | Divisor | Remainder
0 | Initial values |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 

## Slide 5
Divide Example
Divide 7ten (0000 0111two) by 2ten (0010two)
Iter | Step | Quot | Divisor | Remainder
0 | Initial values | 0000 | 0010 0000 | 0000 0111
1 | Rem = Rem – Div Rem < 0  +Div, shift 0 into Q Shift Div right | 0000 0000 0000 | 0010 0000 0010 0000 0001 0000 | 1110 0111 0000 0111 0000 0111
2 | Same steps as 1 | 0000 0000 0000 | 0001 0000 0001 0000 0000 1000 | 1111 0111 0000 0111 0000 0111
3 | Same steps as 1 | 0000 | 0000 0100 | 0000 0111
4 | Rem = Rem – Div Rem >= 0  shift 1 into Q Shift Div right | 0000 0001 0001 | 0000 0100 0000 0100 0000 0010 | 0000 0011 0000 0011 0000 0011
5 | Same steps as 4 | 0011 | 0000 0001 | 0000 0001

## Slide 6
Hardware for Division
A comparison requires a subtract; the sign of the result is
examined; if the result is negative, the divisor must be added back
Similar to multiply, results are placed in Hi (remainder) and Lo (quotient)
Source: H&P textbook

## Slide 7
Efficient Division
Source: H&P textbook

## Slide 8
Divisions involving Negatives
Simplest solution: convert to positive and adjust sign later
Note that multiple solutions exist for the equation:
Dividend = Quotient x Divisor + Remainder
+7 div +2 Quo = Rem =
-7 div +2 Quo = Rem =
+7 div -2 Quo = Rem =
-7 div -2 Quo = Rem =

## Slide 9
Divisions involving Negatives
Simplest solution: convert to positive and adjust sign later
Note that multiple solutions exist for the equation:
Dividend = Quotient x Divisor + Remainder
+7 div +2 Quo = +3 Rem = +1
-7 div +2 Quo = -3 Rem = -1
+7 div -2 Quo = -3 Rem = +1
-7 div -2 Quo = +3 Rem = -1
Convention: Dividend and remainder have the same sign
Quotient is negative if signs disagree
These rules fulfil the equation above

## Slide 10
Floating Point
Normalized scientific notation: single non-zero digit to the
left of the decimal (binary) point – example: 3.5 x 109
1.010001 x 2-5two = (1 + 0 x 2-1 + 1 x 2-2 + … + 1 x 2-6) x 2-5ten
A standard notation enables easy exchange of data between
machines and simplifies hardware algorithms – the
IEEE 754 standard defines how floating point numbers
are represented

## Slide 11
Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
More exponent bits  wider range of numbers (not necessarily more
numbers – recall there are infinite real numbers)
More fraction bits  higher precision
Register value = (-1)S x F x 2E
Since we are only representing normalized numbers, we are
guaranteed that the number is of the form 1.xxxx..
Hence, in IEEE 754 standard, the 1 is implicit
Register value = (-1)S x (1 + F) x 2E

## Slide 12
Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
Largest number that can be represented:
Smallest number that can be represented:

## Slide 13
Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
Largest number that can be represented: 2.0 x 2128 = 2.0 x 1038
Smallest number that can be represented: 1.0 x 2-127 = 2.0 x 10-38
Overflow: when representing a number larger than the one above;
Underflow: when representing a number smaller than the one above
Double precision format: occupies two 32-bit registers:
Largest: Smallest:
Sign Exponent Fraction
1 bit 11 bits 52 bits
S
E
F

## Slide 14
Details
The number “0” has a special code so that the implicit 1 does not
get added: the code is all 0s
(it may seem that this takes up the representation for 1.0, but
given how the exponent is represented, that’s not the case)
(see discussion of denorms (pg. 222) in the textbook)
The largest exponent value (with zero fraction) represents +/- infinity
The largest exponent value (with non-zero fraction) represents
NaN (not a number) – for the result of 0/0 or (infinity minus infinity)
Note that these choices impact the smallest and largest numbers
that can be represented

## Slide 15
Exponent Representation
To simplify sort, sign was placed as the first bit
For a similar reason, the representation of the exponent is also
modified: in order to use integer compares, it would be preferable to
have the smallest exponent as 00…0 and the largest exponent as 11…1
This is the biased notation, where a bias is subtracted from the
exponent field to yield the true exponent
IEEE 754 single-precision uses a bias of 127 (since the exponent
must have values between -127 and 128)…double precision uses
a bias of 1023
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)

## Slide 16
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
Double: (1 + 11 + 52)
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000

## Slide 17
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
1 0111 1110 1000…000
Double: (1 + 11 + 52)
1 0111 1111 110 1000…000
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
-5.0

## Slide 18
FP Addition
Consider the following decimal example (can maintain
only 4 decimal digits and 2 exponent digits)
9.999 x 101 + 1.610 x 10-1
Convert to the larger exponent:
9.999 x 101 + 0.016 x 101
Add
10.015 x 101
Normalize
1.0015 x 102
Check for overflow/underflow
Round
1.002 x 102
Re-normalize

## Slide 19
FP Addition
Consider the following decimal example (can maintain
only 4 decimal digits and 2 exponent digits)
9.999 x 101 + 1.610 x 10-1
Convert to the larger exponent:
9.999 x 101 + 0.016 x 101
Add
10.015 x 101
Normalize
1.0015 x 102
Check for overflow/underflow
Round
1.002 x 102
Re-normalize
If we had more fraction bits,
these errors would be minimized