## Slide 1
Lecture 20: Branches, OOO
Today’s topics:
  Branch prediction
  Out-of-order execution
Mute yourself
Raise your hand if you have a question
I’ll call on you
Mute again after the conversation ends
Feel free to chat among yourselves (keep it technical), but I’ll only see it at the end

## Slide 2
Control Hazards
Simple techniques to handle control hazard stalls:
  for every branch, introduce a stall cycle (note: every
  6th instruction is a branch!)
  assume the branch is not taken and start fetching the
  next instruction – if the branch is taken, need hardware
  to cancel the effect of the wrong-path instruction
  fetch the next instruction (branch delay slot) and
  execute it anyway – if the instruction turns out to be
  on the correct path, useful work was done – if the
  instruction turns out to be on the wrong path,
  hopefully program state is not lost
  make a smarter guess and fetch instructions from the
  expected target

## Slide 3
Branch Delay Slots
Source: H&P textbook

## Slide 4
Pipeline without Branch Predictor
IF (br)
PC
Reg Read
Compare
Br-target
PC + 4

## Slide 5
Pipeline with Branch Predictor
IF (br)
PC
Reg Read
Compare
Br-target
Branch
Predictor

## Slide 6
Bimodal Predictor
Branch PC
14 bits
Table of
16K entries
of 2-bit
saturating
counters

## Slide 7
2-Bit Prediction
For each branch, maintain a 2-bit saturating counter:
if the branch is taken: counter = min(3,counter+1)
if the branch is not taken: counter = max(0,counter-1)
… sound familiar?
If (counter >= 2), predict taken, else predict not taken
The counter attempts to capture the common case for
each branch
Indexing functions
Multiple branch predictors
History, trade-offs

## Slide 8
Slowdowns from Stalls
Perfect pipelining with no hazards  an instruction
completes every cycle (total cycles ~ num instructions)
 speedup = increase in clock speed = num pipeline stages
With hazards and stalls, some cycles (= stall time) go by
during which no instruction completes, and then the stalled
instruction completes
Total cycles = number of instructions + stall cycles

## Slide 9
Multicycle Instructions
Multiple parallel pipelines – each pipeline can have a different
number of stages
Instructions can now complete out of order – must make sure
that writes to a register happen in the correct order

## Slide 10
An Out-of-Order Processor Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 11
Example Code
Completion times with in-order with ooo
ADD R1, R2, R3 5 5
ADD R4, R1, R2 6 6
LW R5, 8(R4) 7 7
ADD R7, R6, R5 9 9
ADD R8, R7, R5 10 10
LW R9, 16(R4) 11 7
ADD R10, R6, R9 13 9
ADD R11, R10, R9 14 10