## Slide 1
Lecture 22: Cache Hierarchies
Today’s topics:
  Cache access details
  Examples

## Slide 2
Locality
Why do caches work?
  Temporal locality: if you used some data recently, you
  will likely use it again
  Spatial locality: if you used some data recently, you
  will likely access its neighbors
No hierarchy: average access time for data = 300 cycles
32KB 1-cycle L1 cache that has a hit rate of 95%:
average access time = 0.95 x 1 + 0.05 x (301)
= 16 cycles

## Slide 3
Accessing the Cache
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique location in cache
8 words: 3 index bits
Byte address
Data array
Sets
Offset

## Slide 4
The Tag Array
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array

## Slide 5
Example Access Pattern
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 68, 73, 78, 83, 88, 4, 7, 10…

## Slide 6
Increasing Line Size
32-byte cache
line size or
block size
10100000
Byte address
Tag
Data array
Tag array
Offset
A large cache line size  smaller tag array,
fewer misses because of spatial locality

## Slide 7
Associativity
10100000
Byte address
Tag
Data array
Tag array
Set associativity  fewer conflicts; wasted power
because multiple data and tags are read
Way-1
Way-2
Compare

## Slide 8
Associativity
10100000
Byte address
Tag
Data array
Tag array
How many offset/index/tag bits if the cache has
64 sets,
each set has 64 bytes,
4 ways
Way-1
Way-2
Compare

## Slide 9
Example 1
32 KB 4-way set-associative data cache array with 32
byte line sizes
How many sets?
How many index bits, offset bits, tag bits?
How large is the tag array?

## Slide 10
Example 1
32 KB 4-way set-associative data cache array with 32
byte line sizes
cache size = #sets x #ways x block size
How many sets? 256
How many index bits, offset bits, tag bits?
8 5 19
How large is the tag array?
tag array size = #sets x #ways x tag size
= 19 Kb = 2.375 KB

## Slide 11
Example 2
A pipeline has CPI 1 if all loads/stores are L1 cache hits
40% of all instructions are loads/stores
85% of all loads/stores hit in 1-cycle L1
50% of all (10-cycle) L2 accesses are misses
Memory access takes 100 cycles
What is the CPI?

## Slide 12
Example 2
A pipeline has CPI 1 if all loads/stores are L1 cache hits
40% of all instructions are loads/stores
85% of all loads/stores hit in 1-cycle L1
50% of all (10-cycle) L2 accesses are misses
Memory access takes 100 cycles
What is the CPI?
Start with 1000 instructions
1000 cycles (includes all 400 L1 accesses)
+ 400 (ld/st) x 15% x 10 cycles (the L2 accesses)
+ 400 x 15% x 50% x 100 cycles (the mem accesses)
= 4,600 cycles
CPI = 4.6

## Slide 13
Example 3
00010000
Byte address
Tag
Data array
Tag array
8-byte blocks
Way-1
Way-2
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 24, 36, 4, 48, 64, 4, 36, 64, 4

## Slide 14
Example 3
00010000
Byte address
Tag
Data array
Tag array
8-byte blocks
Way-1
Way-2
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 24, 36, 4, 48, 64, 4, 36, 64, 4
M H M H M M M H M M H M M M

## Slide 15
Cache Misses
On a write miss, you may either choose to bring the block
into the cache (write-allocate) or not (write-no-allocate)
On a read miss, you always bring the block in (spatial and
temporal locality) – but which block do you replace?
  no choice for a direct-mapped cache
  randomly pick one of the ways to replace
  replace the way that was least-recently used (LRU)
  FIFO replacement (round-robin)

## Slide 16
Writes
When you write into a block, do you also update the
copy in L2?
  write-through: every write to L1  write to L2
  write-back: mark the block as dirty, when the block
  gets replaced from L1, write it to L2
Writeback coalesces multiple writes to an L1 block into one
L2 write
Writethrough simplifies coherency protocols in a
multiprocessor system as the L2 always has a current
copy of data

## Slide 17
Types of Cache Misses
Compulsory misses: happens the first time a memory
word is accessed – the misses for an infinite cache
Capacity misses: happens because the program touched
many other words before re-touching the same word – the
misses for a fully-associative cache
Conflict misses: happens because two words map to the
same location in the cache – the misses generated while
moving from a fully-associative to a direct-mapped cache