## Slide 1
3810 Review Session
Spring 2020

## Slide 2
Unpipelined processor
CPI:
Clock speed:
Throughput:
Pipelined processor
CPI:
Clock speed:
Throughput:
Circuit Assumptions
Length of full circuit:
Length of each stage:
No hazards
Pipeline Performance

## Slide 3
Data Hazards
No Bypassing
Point of production: always RW middle
Point of consumption: always D/R middle
Bypassing
Point of production:
add, sub, etc.: end of ALU
lw: end of DM
Point of consumption:
add, sub, lw: start of ALU
sw $1, 8($2): start of ALU for $2,
start of DM for $1
* PoP
I1 add: IF DR AL DM RW
I2 add: IF DR DR DR AL DM RW
* PoC
* PoP
I1 add: IF DR AL DM RW
I2 add: IF DR AL DM RW
* PoC

## Slide 4
Control Hazards
Assumptions
100 instructions
20 branches
14 Not-Taken, 6 Taken
Branch resolved in 6th cycle (penalty of 5)
Approach 1: Panic and wait
Approach 2: Fetch-next-instr
Approach 3: Branch Delay Slot
Option A: always useful
Option B: useful when the branch
goes along common fork
Option C: useful when the branch
goes along uncommon fork
Option D: no-op, always non-useful
Approach 4: Branch predictor
Accuracy of 90%
Option A
Branch
Slot
NTaken Taken
Option B Option C

## Slide 5
Out of Order Processor
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 6
Cache Latency
Assumptions
1000 instructions, 1000 cycles, no stalls with L1 hits
# loads/stores:
% of loads/stores that show up at L2:
% of loads/stores that show up at L3:
% of loads/stores that show up at mem:
L2 acc = 10 cyc, L3 acc = 25 cyc, mem acc = 200 cyc

## Slide 7
Cache Size
Assumptions
512KB cache, 8-way set-associative, 64-byte blocks, 32-bit addresses
Data array size = #sets x #ways x blocksize
Tag array size = #sets x #ways x tagsize
Offset bits = log(blocksize)
Index bits = log(#sets)
Tag bits + index bits + offset bits = addresswidth

## Slide 8
Cache Hits/Misses
Assumptions
16 sets, 1 way, 32-byte blocks
Access pattern: 4 40 400 480 512 520 1032 1540
Set #:
Block:

## Slide 10
Security

## Slide 11
Virtual Memory

## Slide 12
Synchronization, GPUs