## Slide 1
Lecture 18: Pipelining
Today’s topics:
  5-stage pipeline
  Hazards
  Data dependence handling with bypassing
  Data dependence examples

## Slide 2
A 5-Stage Pipeline
Source: H&P textbook

## Slide 3
Hazards
Structural hazards: different instructions in different stages
(or the same stage) conflicting for the same resource
Data hazards: an instruction cannot continue because it
needs a value that has not yet been generated by an
earlier instruction
Control hazard: fetch cannot continue because it does
not know the outcome of an earlier branch – special case
of a data hazard – separate category because they are
treated in different ways

## Slide 4
Conflicts/Problems
I-cache and D-cache are accessed in the same cycle – it
helps to implement them separately
Registers are read and written in the same cycle – easy to
deal with if register read/write time equals cycle time/2
Instructions can’t skip the DM stage, else conflict for RW
Consuming instruction may have to wait for producer
Branch target changes only at the end of the second stage
-- what do you do in the meantime?

## Slide 5
Structural Hazards
Example: a unified instruction and data cache 
stage 4 (MEM) and stage 1 (IF) can never coincide
The later instruction and all its successors are delayed
until a cycle is found when the resource is free  these
are pipeline bubbles
Structural hazards are easy to eliminate – increase the
number of resources (for example, implement a separate
instruction and data cache, add more register ports)

## Slide 6
Data Hazards
An instruction produces a value in a given pipeline stage
A subsequent instruction consumes that value in a pipeline
stage
The consumer may have to be delayed so that the time
of consumption is later than the time of production

## Slide 7
Example 1 – No Bypassing
D/R
ALU
DM
RW
IF
CYC-1
D/R
ALU
DM
RW
IF
CYC-2
D/R
ALU
DM
RW
IF
CYC-3
D/R
ALU
DM
RW
IF
CYC-4
D/R
ALU
DM
RW
IF
CYC-5
D/R
ALU
DM
RW
IF
CYC-6
D/R
ALU
DM
RW
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9

## Slide 8
Example 1 – No Bypassing
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I2
ALU
DM
I1
RW
IF
I3
CYC-4
D/R
I2
ALU
DM
RW
I1
IF
I3
CYC-5
D/R
I3
ALU
I2
DM
RW
IF
I4
CYC-6
D/R
I4
ALU
I3
DM
I2
RW
IF
I5
CYC-7
D/R
ALU
DM
I3
RW
I2
IF
CYC-8
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9

## Slide 9
Example 2 – Bypassing
D/R
ALU
DM
RW
IF
CYC-1
D/R
ALU
DM
RW
IF
CYC-2
D/R
ALU
DM
RW
IF
CYC-3
D/R
ALU
DM
RW
IF
CYC-4
D/R
ALU
DM
RW
IF
CYC-5
D/R
ALU
DM
RW
IF
CYC-6
D/R
ALU
DM
RW
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.

## Slide 10
Example 2 – Bypassing
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I3
ALU
I2
DM
I1
RW
IF
I4
CYC-4
D/R
I4
ALU
I3
DM
I2
RW
I1
IF
I5
CYC-5
D/R
ALU
DM
I3
RW
I2
IF
CYC-6
D/R
ALU
DM
RW
I3
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
L3 L3 L4 L3 L5 L3

## Slide 11
Problem 1
add $1, $2, $3
lw $4, 8($1)
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW

## Slide 12
Problem 2
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
lw $4, 8($1)

## Slide 13
Problem 3
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
sw $1, 8($3)