## Slide 1
Lecture 7: Examples, MARS
Today’s topics:
  More examples
  MARS intro

## Slide 2
Dealing with Characters
Instructions are also provided to deal with byte-sized
and half-word quantities: lb (load-byte), sb, lh, sh
These data types are most useful when dealing with
characters, pixel values, etc.
C employs ASCII formats to represent characters – each
character is represented with 8 bits and a string ends in
the null character (corresponding to the 8-bit number 0);
A is 65, a is 97

## Slide 3
Example 3 (pg. 108)
Convert to assembly:
void strcpy (char x[], char y[])
{
int i;
i=0;
while ((x[i] = y[i]) != `\0’)
i += 1;
}
strcpy:
addi $sp, $sp, -4
sw $s0, 0($sp)
add $s0, $zero, $zero
L1: add $t1, $s0, $a1
lb $t2, 0($t1)
add $t3, $s0, $a0
sb $t2, 0($t3)
beq $t2, $zero, L2
addi $s0, $s0, 1
j L1
L2: lw $s0, 0($sp)
addi $sp, $sp, 4
jr $ra
Notes:
Temp registers not saved.

## Slide 4
Large Constants
Immediate instructions can only specify 16-bit constants
The lui instruction is used to store a 16-bit constant into
the upper 16 bits of a register… combine this with an
OR instruction to specify a 32-bit constant
The destination PC-address in a conditional branch is
specified as a 16-bit constant, relative to the current PC
A jump (j) instruction can specify a 26-bit constant; if more
bits are required, the jump-register (jr) instruction is used

## Slide 5
Starting a Program
C Program
Assembly language program
Object: machine language module
Object: library routine (machine language)
Executable: machine language program
Memory
Compiler
Assembler
Linker
Loader
x.c
x.s
x.o
x.a, x.so
a.out

## Slide 6
Role of Assembler
Convert pseudo-instructions into actual hardware
instructions – pseudo-instrs make it easier to program
in assembly – examples: “move”, “blt”, 32-bit immediate
operands, labels, etc.
Convert assembly instrs into machine instrs – a separate
object file (x.o) is created for each C file (x.c) – compute
the actual values for instruction labels – maintain info
on external references and debugging information

## Slide 7
Role of Linker
Stitches different object files into a single executable
  patch internal and external references
  determine addresses of data and instruction labels
  organize code and data modules in memory
Some libraries (DLLs) are dynamically linked – the
executable points to dummy routines – these dummy
routines call the dynamic linker-loader so they can
update the executable to jump to the correct routine

## Slide 8
Full Example – Sort in C (pg. 133)
Allocate registers to program variables
Produce code for the program body
Preserve registers across procedure invocations
void sort (int v[ ], int n)
{
int i, j;
for (i=0; i<n; i+=1) {
for (j=i-1; j>=0 && v[j] > v[j+1]; j-=1) {
swap (v,j);
}
}
}
void swap (int v[ ], int k)
{
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}

## Slide 9
The swap Procedure
Register allocation: $a0 and $a1 for the two arguments, $t0 for the
temp variable – no need for saves and restores as we’re not using
$s0-$s7 and this is a leaf procedure (won’t need to re-use $a0 and $a1)
swap: sll $t1, $a1, 2
add $t1, $a0, $t1
lw $t0, 0($t1)
lw $t2, 4($t1)
sw $t2, 0($t1)
sw $t0, 4($t1)
jr $ra
void swap (int v[], int k)
{
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}

## Slide 10
The sort Procedure
Register allocation: arguments v and n use $a0 and $a1, i and j use
$s0 and $s1; must save $a0 and $a1 before calling the leaf procedure
The outer for loop looks like this: (note the use of pseudo-instrs)
move $s0, $zero # initialize the loop
loopbody1: bge $s0, $a1, exit1 # will eventually use slt and beq
… body of inner loop …
addi $s0, $s0, 1
j loopbody1
exit1:
for (i=0; i<n; i+=1) {
for (j=i-1; j>=0 && v[j] > v[j+1]; j-=1) {
swap (v,j);
}
}

## Slide 11
The sort Procedure
The inner for loop looks like this:
addi $s1, $s0, -1 # initialize the loop
loopbody2: blt $s1, $zero, exit2 # will eventually use slt and beq
sll $t1, $s1, 2
add $t2, $a0, $t1
lw $t3, 0($t2)
lw $t4, 4($t2)
ble $t3, $t4, exit2
… body of inner loop …
addi $s1, $s1, -1
j loopbody2
exit2:
for (i=0; i<n; i+=1) {
for (j=i-1; j>=0 && v[j] > v[j+1]; j-=1) {
swap (v,j);
}
}

## Slide 12
Saves and Restores
Since we repeatedly call “swap” with $a0 and $a1, we begin
“sort” by copying its arguments into $s2 and $s3 – must update
the rest of the code in “sort” to use $s2 and $s3 instead of
$a0 and $a1
Must save $ra at the start of “sort” because it will get
over-written when we call “swap”
Must also save $s0-$s3 so we don’t overwrite something that
belongs to the procedure that called “sort”

## Slide 13
Saves and Restores
sort: addi $sp, $sp, -20
sw $ra, 16($sp)
sw $s3, 12($sp)
sw $s2, 8($sp)
sw $s1, 4($sp)
sw $s0, 0($sp)
move $s2, $a0
move $s3, $a1
…
move $a0, $s2 # the inner loop body starts here
move $a1, $s1
jal swap
…
exit1: lw $s0, 0($sp)
…
addi $sp, $sp, 20
jr $ra
9 lines of C code  35 lines of assembly

## Slide 14
MARS
MARS is a simulator that reads in an assembly program
and models its behavior on a MIPS processor
Note that a “MIPS add instruction” will eventually be
converted to an add instruction for the host computer’s
architecture – this translation happens under the hood
To simplify the programmer’s task, it accepts
pseudo-instructions, large constants, constants in
decimal/hex formats, labels, etc.
The simulator allows us to inspect register/memory
values to confirm that our program is behaving correctly

## Slide 15
MARS Intro
Directives, labels, global pointers, system calls

## Slide 16
MARS Intro

## Slide 17
MARS Intro
Read the google doc on the class webpage for details!

## Slide 18
Example Print Routine
.data
str: .asciiz “the answer is ”
.text
li $v0, 4 # load immediate; 4 is the code for print_string
la $a0, str # the print_string syscall expects the string
# address as the argument; la is the instruction
# to load the address of the operand (str)
syscall # MARS will now invoke syscall-4
li $v0, 1 # syscall-1 corresponds to print_int
li $a0, 5 # print_int expects the integer as its argument
syscall # MARS will now invoke syscall-1
(see the detailed solution in Section 7 of the “MARS notes”
on the class webpage)

## Slide 19
Example
Write an assembly program to prompt the user for two
numbers and print the sum of the two numbers

## Slide 20
Example
.data
str1: .asciiz “Enter 2 numbers:”
.text str2: .asciiz “The sum is ”
li $v0, 4
la $a0, str1
syscall
li $v0, 5
syscall
add $t0, $v0, $zero
li $v0, 5
syscall
add $t1, $v0, $zero
li $v0, 4
la $a0, str2
syscall
li $v0, 1
add $a0, $t1, $t0
syscall