## Slide 1
Lecture 15: Review Session
Today’s topics:
  Midterm review session
  Midterm rules:
  Students are allowed to bring 3 A4/letter-sized sheets of paper with anything written/printed on both sides. In addition, you may bring the ``green sheet''. You may also bring a phone/calculator that can be used for any numeric calculations (but it's also ok to write a mathematical term, say 1.4/2.2 GHz without doing the calculation). You may of course not use your phone to surf the web or consult with others during the test. You may also not use the MARS simulator or other calculators/tools for numeric conversions. If necessary, make reasonable assumptions and clearly state them. The only clarifications you may ask for during the exam are definitions of terms. You will receive partial credit if you show your steps and explain your line of thinking, so attempt every question even if you can't fully solve it. Complete your answers in the space provided (including the back-side of each page). Confirm that you have 14 questions on 8 pages, followed by a blank page. Turn in your answer sheets before 10:35am. The test is worth 100 points and you have about 90 minutes, so allocate time accordingly.

## Slide 2
Modern Trends
Historical contributions to performance:
  Better processes (faster devices) ~20%
  Better circuits/pipelines ~15%
  Better organization/architecture ~15%
Today, annual improvement is closer to 20%; this is primarily
because of slowly increasing transistor count and more cores.
Need multi-thread parallelism and accelerators to boost
performance every year.

## Slide 3
Performance Measures
Performance = 1 / execution time
Speedup = ratio of performance
Performance improvement = speedup -1
Execution time = clock cycle time x CPI x number of instrs
Program takes 100 seconds on ProcA and 150 seconds on ProcB
Speedup of A over B = 150/100 = 1.5
Performance improvement of A over B = 1.5 – 1 = 0.5 = 50%
Speedup of B over A = 100/150 = 0.66 (speedup less than 1 means
performance went down)
Performance improvement of B over A = 0.66 – 1 = -0.33 = -33%
or Performance degradation of B, relative to A = 33%
If multiple programs are executed, the execution times are combined
into a single number using AM, weighted AM, or GM

## Slide 4
Performance Equations
CPU execution time = CPU clock cycles x Clock cycle time
CPU clock cycles = number of instrs x avg clock cycles
per instruction (CPI)
Substituting in previous equation,
Execution time = clock cycle time x number of instrs x avg CPI
If a 2 GHz processor graduates an instruction every third cycle,
how many instructions are there in a program that runs for
10 seconds?

## Slide 5
Power Consumption
Dyn power a activity x capacitance x voltage2 x frequency
Capacitance per transistor and voltage are decreasing,
but number of transistors and frequency are increasing at
a faster rate
Leakage power is also rising and will soon match dynamic
power
Power consumption is already around 100W in
some high-performance processors today

## Slide 6
Example Problem
A 1 GHz processor takes 100 seconds to execute a CPU-bound
program, while consuming 70 W of dynamic power and 30 W of
leakage power. Does the program consume less energy in
Turbo boost mode when the frequency is increased to 1.2 GHz?
Normal mode energy = 100 W x 100 s = 10,000 J
Turbo mode energy = (70 x 1.2 + 30) x 100/1.2 = 9,500 J
Note:
Frequency only impacts dynamic power, not leakage power.
We assume that the program’s CPI is unchanged when
frequency is changed, i.e., exec time varies linearly
with cycle time.

## Slide 7
Basic MIPS Instructions
lw $t1, 16($t2)
add $t3, $t1, $t2
addi $t3, $t3, 16
sw $t3, 16($t2)
beq $t1, $t2, 16
blt is implemented as slt and bne
j 64
jr $t1
sll $t1, $t1, 2
Convert to assembly:
while (save[i] == k)
i += 1;
i and k are in $s3 and $s5 and
base of array save[] is in $s6
Loop: sll $t1, $s3, 2
add $t1, $t1, $s6
lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3, 1
j Loop
Exit:

## Slide 8
Registers
The 32 MIPS registers are partitioned as follows:
  Register 0 : $zero always stores the constant 0
  Regs 2-3 : $v0, $v1 return values of a procedure
  Regs 4-7 : $a0-$a3 input arguments to a procedure
  Regs 8-15 : $t0-$t7 temporaries
  Regs 16-23: $s0-$s7 variables
  Regs 24-25: $t8-$t9 more temporaries
  Reg 28 : $gp global pointer
  Reg 29 : $sp stack pointer
  Reg 30 : $fp frame pointer
  Reg 31 : $ra return address

## Slide 9
Memory Organization
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)
Proc A’s values
Proc B’s values
Proc C’s values
…
High address
Low address
Stack grows
this way
$fp
$sp
$gp

## Slide 10
Procedure Calls/Returns
procA (int i)
{
int j;
j = …;
i = call procB(j);
… = i;
}
procB (int j)
{
int k;
… = j;
k = …;
return k;
}
procA:
$s0 = … # value of j
$t0 = … # some tempval
$a0 = $s0 # the argument
…
jal procB
…
… = $v0
procB:
$t0 = … # some tempval
… = $a0 # using the argument
$s0 = … # value of k
$v0 = $s0;
jr $ra

## Slide 11
Saves and Restores
Caller saves:
  $ra, $a0, $t0, $fp (if reqd)
Callee saves:
  $s0
procA:
$s0 = … # value of j
$t0 = … # some tempval
$a0 = $s0 # the argument
…
jal procB
…
… = $v0
procB:
$t0 = … # some tempval
… = $a0 # using the argument
$s0 = … # value of k
$v0 = $s0;
jr $ra
As every element is saved on stack,
the stack pointer is decremented

## Slide 12
Example 2
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}
fact:
addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1:
addi $a0, $a0, -1
jal fact
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
Notes:
The caller saves $a0 and $ra
in its stack space.
Temps are never saved.

## Slide 13
Recap – Numeric Representations
Decimal 3510 = 3 x 101 + 5 x 100
Binary 001000112 = 1 x 25 + 1 x 21 + 1 x 20
Hexadecimal (compact representation)
0x 23 or 23hex = 2 x 161 + 3 x 160
0-15 (decimal)  0-9, a-f (hex)
Dec Binary Hex
0 0000 00
1 0001 01
2 0010 02
3 0011 03
Dec Binary Hex
4 0100 04
5 0101 05
6 0110 06
7 0111 07
Dec Binary Hex
8 1000 08
9 1001 09
10 1010 0a
11 1011 0b
Dec Binary Hex
12 1100 0c
13 1101 0d
14 1110 0e
15 1111 0f

## Slide 14
2’s Complement
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
…
0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
1000 0000 0000 0000 0000 0000 0000 0000two = -231
1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
…
1111 1111 1111 1111 1111 1111 1111 1110two = -2
1111 1111 1111 1111 1111 1111 1111 1111two = -1
Note that the sum of a number x and its inverted representation x’ always
equals a string of 1s (-1).
x + x’ = -1
x’ + 1 = -x … hence, can compute the negative of a number by
-x = x’ + 1 inverting all bits and adding 1
This format can directly undergo addition without any conversions!
Each number represents the quantity
x31 -231 + x30 230 + x29 229 + … + x1 21 + x0 20

## Slide 15
Multiplication Example
Multiplicand 1000ten
Multiplier x 1001ten
---------------
1000
0000
0000
1000
----------------
Product 1001000ten
In every step
  multiplicand is shifted
  next bit of multiplier is examined (also a shifting step)
  if this bit is 1, shifted multiplicand is added to the product

## Slide 16
Division
1001ten Quotient
Divisor 1000ten | 1001010ten Dividend
-1000
10
101
1010
-1000
10ten Remainder
At every step,
  shift divisor right and compare it with current dividend
  if divisor is larger, shift 0 as the next bit of the quotient
  if divisor is smaller, subtract to get new dividend and shift 1
  as the next bit of the quotient

## Slide 17
Division
1001ten Quotient
Divisor 1000ten | 1001010ten Dividend
0001001010 0001001010 0000001010 0000001010
100000000000  0001000000 00001000000000001000
Quo: 0 000001 0000010 000001001
At every step,
  shift divisor right and compare it with current dividend
  if divisor is larger, shift 0 as the next bit of the quotient
  if divisor is smaller, subtract to get new dividend and shift 1
  as the next bit of the quotient

## Slide 18
Binary FP Numbers
20.45 decimal = ? Binary
20 decimal = 10100 binary
0.45 x 2 = 0.9 (not greater than 1, first bit after binary point is 0)
0.90 x 2 = 1.8 (greater than 1, second bit is 1, subtract 1 from 1.8)
0.80 x 2 = 1.6 (greater than 1, third bit is 1, subtract 1 from 1.6)
0.60 x 2 = 1.2 (greater than 1, fourth bit is 1, subtract 1 from 1.2)
0.20 x 2 = 0.4 (less than 1, fifth bit is 0)
0.40 x 2 = 0.8 (less than 1, sixth bit is 0)
0.80 x 2 = 1.6 (greater than 1, seventh bit is 1, subtract 1 from 1.6)
… and the pattern repeats
10100.011100110011001100…
Normalized form = 1.0100011100110011… x 24

## Slide 19
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
Double: (1 + 11 + 52)
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
Remember:
True exponent Exponent in register
+127
-127

## Slide 20
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
1 0111 1110 1000…000
Double: (1 + 11 + 52)
1 0111 1111 110 1000…000
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
-5.0

## Slide 21
Example 2
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent 36.90625ten in single-precision format
36 / 2 = 18 rem 0
18 / 2 = 9 rem 0
9 / 2 = 4 rem 1
4 / 2 = 2 rem 0
2 / 2 = 1 rem 0
1 / 2 = 0 rem 1
36 is 100100
0.90625 x 2 = 1.81250
0.8125 x 2 = 1.6250
0.625 x 2 = 1.250
0.25 x 2 = 0.50
0.5 x 2 = 1.00
0.0 x 2 = 0.0
0.90625 is 0.1110100…0

## Slide 22
Example 2
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
We’ve calculated that 36.90625ten = 100100.1110100…0 in binary
Normalized form = 1.001001110100…0 x 25
(had to shift 5 places to get only one bit left of the point)
The sign bit is 0 (positive number)
The fraction field is 001001110100…0 (the 23 bits after the point)
The exponent field is 5 + 127 (have to add the bias) = 132,
which in binary is 10000100
The IEEE 754 format is 0 10000100 001001110100…..0
sign exponent 23 fraction bits

## Slide 23
0 00..0 00…0
Value 0
Value 1
0 127 00…0
Value inf
Value NAN
Highest value ~2 x 2127
0 255 00…0
0 255 xx….x
0 254 11….1
Smallest Norm ~2 x 2-126
Largest Denorm ~1 x 2-126
Smallest Denorm ~2-149
0 0..01 00…0
0 0..00 11…1
0 0..00 00…1
Same rules as above, but the sign bit is 1
Same magnitudes as above, but negative numbers
Exponent field < 127, i.e., after
subtracting bias, they are negative
exponents, representing numbers < 1
2 special cases up top that use the
reserved exponent field of 255
Special case with exponent field 0, used to
represent denorms, that help us gradually approach 0

## Slide 24
FP Addition – Binary Example
Consider the following binary example
1.010 x 21 + 1.100 x 23
Convert to the larger exponent:
0.0101 x 23 + 1.1000 x 23
Add
1.1101 x 23
Normalize
1.1101 x 23
Check for overflow/underflow
Round
Re-normalize
IEEE 754 format: 0 10000010 11010000000000000000000

## Slide 25
Boolean Algebra
A B C E
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 0
(A . B . C) + (A . C . B) + (C . B . A)
Can also use “product of sums”
Any equation can be implemented
with an array of ANDs, followed by
an array of ORs
A + B = A . B
A . B = A + B
Any truth table can be expressed
as a sum of products

## Slide 26
Adder Implementations
Ripple-Carry adder – each 1-bit adder feeds its carry-out to next stage –
simple design, but we must wait for the carry to propagate thru all bits
Carry-Lookahead adder – each bit can be represented by an equation
that only involves input bits (ai, bi) and initial carry-in (c0) -- this is a
complex equation, so it’s broken into sub-parts
For bits ai, bi,, and ci, a carry is generated if ai.bi = 1 and a carry is
propagated if ai + bi = 1
Ci+1 = gi + pi . Ci
Similarly, compute these values for a block of 4 bits, then for a block
of 16 bits, then for a block of 64 bits….Finally, the carry-out for the
64th bit is represented by an equation such as this:
C4 = G3+ G2.P3 + G1.P2.P3 + G0.P1.P2.P3 + C0.P0.P1.P2.P3
Each of the sub-terms is also a similar expression

## Slide 27
32-bit ALU
Source: H&P textbook

## Slide 28
Control Lines
What are the values
of the control lines
and what operations
do they correspond to?
Ai Bn Op
AND 0 0 00
OR 0 0 01
Add 0 0 10
Sub 0 1 10
NOR 1 1 00
NAND 1 1 01
SLT 0 1 11
BEQ 0 1 10 (xx)
Source: H&P textbook