## Slide 1
Lecture 19: Pipelining
Today’s topics:
  Data hazards and instruction scheduling
  Control hazards

## Slide 2
Example 2 – Bypassing
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I3
ALU
I2
DM
I1
RW
IF
I4
CYC-4
D/R
I4
ALU
I3
DM
I2
RW
I1
IF
I5
CYC-5
D/R
ALU
DM
I3
RW
I2
IF
CYC-6
D/R
ALU
DM
RW
I3
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
L3 L3 L4 L3 L5 L3

## Slide 3
Problem 0
add $1, $2, $3
add $5, $1, $4
Without bypassing:
add $1, $2, $3: IF DR AL DM RW
add $5, $1, $4: IF DR DR DR AL DM RW
With bypassing:
add $1, $2, $3: IF DR AL DM RW
add $5, $1, $4: IF DR AL DM RW
Point of Production
Point of Consumption

## Slide 4
Problem 1
add $1, $2, $3
lw $4, 8($1)
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW

## Slide 5
Problem 1
add $1, $2, $3
lw $4, 8($1)
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW

## Slide 6
Problem 2
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
lw $4, 8($1)

## Slide 7
Problem 2
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
lw $4, 8($1)

## Slide 8
Problem 3
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
sw $1, 8($3)

## Slide 9
Problem 3
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
sw $1, 8($3)

## Slide 10
Problem 4
IF
Dec
ALU
DM
RW
ALU
DM
RW
lw $1, 8($2)
add $4, $1, $3
IF
Dec
RR
A 7 or 9 stage pipeline, RR and RW take an entire stage

## Slide 11
Problem 4
IF
Dec
ALU
DM
RW
ALU
DM
RW
lw $1, 8($2)
add $4, $1, $3
IF
Dec
RR
A 7 or 9 stage pipeline, RR and RW take an entire stage

## Slide 12
Problem 4
IF
Dec
ALU
DM
RW
ALU
DM
RW
lw $1, 8($2)
add $4, $1, $3
IF
Dec
RR
Without bypassing: 4 stalls
IF:IF:DE:DE:RR:AL:DM:DM:RW
IF: IF :DE:DE:DE:DE: DE :DE:RR:AL:RW
With bypassing: 2 stalls
IF:IF:DE:DE:RR:AL:DM:DM:RW
IF: IF :DE:DE:DE:DE: RR :AL:RW

## Slide 13
Control Hazards
Simple techniques to handle control hazard stalls:
  for every branch, introduce a stall cycle (note: every
  6th instruction is a branch!)
  assume the branch is not taken and start fetching the
  next instruction – if the branch is taken, need hardware
  to cancel the effect of the wrong-path instruction
  fetch the next instruction (branch delay slot) and
  execute it anyway – if the instruction turns out to be
  on the correct path, useful work was done – if the
  instruction turns out to be on the wrong path,
  hopefully program state is not lost
  make a smarter guess and fetch instructions from the
  expected target

## Slide 14
Control Hazards
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW

## Slide 15
Branch Delay Slots
Source: H&P textbook