## Slide 1
Lecture 11: Floating Point, Digital Design
Today’s topics:
  FP formats, arithmetic
  Intro to Boolean functions

## Slide 2
0 00..0 00…0
Value 0
Value 1
0 127 00…0
Value inf
Value NAN
Highest value ~2 x 2127
0 255 00…0
0 255 xx….x
0 254 11….1
Smallest Norm ~2 x 2-126
Largest Denorm ~1 x 2-126
Smallest Denorm ~2-149
0 0..01 00…0
0 0..00 11…1
0 0..00 00…1
Same rules as above, but the sign bit is 1
Same magnitudes as above, but negative numbers
Exponent field < 127, i.e., after
subtracting bias, they are negative
exponents, representing numbers < 1
2 special cases up top that use the
reserved exponent field of 255
Special case with exponent field 0, used to
represent denorms, that help us gradually approach 0

## Slide 3
Example 2
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent 36.90625ten in single-precision format
36 / 2 = 18 rem 0
18 / 2 = 9 rem 0
9 / 2 = 4 rem 1
4 / 2 = 2 rem 0
2 / 2 = 1 rem 0
1 / 2 = 0 rem 1
36 is 100100
0.90625 x 2 = 1.81250
0.8125 x 2 = 1.6250
0.625 x 2 = 1.250
0.25 x 2 = 0.50
0.5 x 2 = 1.00
0.0 x 2 = 0.0
0.90625 is 0.1110100…0

## Slide 4
Example 2
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
We’ve calculated that 36.90625ten = 100100.1110100…0 in binary
Normalized form = 1.001001110100…0 x 25
(had to shift 5 places to get only one bit left of the point)
The sign bit is 0 (positive number)
The fraction field is 001001110100…0 (the 23 bits after the point)
The exponent field is 5 + 127 (have to add the bias) = 132,
which in binary is 10000100
The IEEE 754 format is 0 10000100 001001110100…..0
sign exponent 23 fraction bits

## Slide 5
Remember:
True exponent Exponent in register
+127
-127

## Slide 6
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
Double: (1 + 11 + 52)
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
Remember:
True exponent Exponent in register
+127
-127

## Slide 7
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
1 0111 1110 1000…000
Double: (1 + 11 + 52)
1 0111 1111 110 1000…000
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
-5.0

## Slide 8
FP Addition
Consider the following decimal example (can maintain
only 4 decimal digits and 2 exponent digits)
9.999 x 101 + 1.610 x 10-1
Convert to the larger exponent:
9.999 x 101 + 0.016 x 101
Add
10.015 x 101
Normalize
1.0015 x 102
Check for overflow/underflow
Round
1.002 x 102
Re-normalize

## Slide 9
FP Addition
Consider the following decimal example (can maintain
only 4 decimal digits and 2 exponent digits)
9.999 x 101 + 1.610 x 10-1
Convert to the larger exponent:
9.999 x 101 + 0.016 x 101
Add
10.015 x 101
Normalize
1.0015 x 102
Check for overflow/underflow
Round
1.002 x 102
Re-normalize
If we had more fraction bits,
these errors would be minimized

## Slide 10
FP Addition – Binary Example
Consider the following binary example
1.010 x 21 + 1.100 x 23
Convert to the larger exponent:
0.0101 x 23 + 1.1000 x 23
Add
1.1101 x 23
Normalize
1.1101 x 23
Check for overflow/underflow
Round
Re-normalize
IEEE 754 format: 0 10000010 11010000000000000000000

## Slide 11
FP Multiplication
Similar steps:
  Compute exponent (careful!)
  Multiply significands (set the binary point correctly)
  Normalize
  Round (potentially re-normalize)
  Assign sign

## Slide 12
MIPS Instructions
The usual add.s, add.d, sub, mul, div
Comparison instructions: c.eq.s, c.neq.s, c.lt.s….
These comparisons set an internal bit in hardware that
is then inspected by branch instructions: bc1t, bc1f
Separate register file $f0 - $f31 : a double-precision
value is stored in (say) $f4-$f5 and is referred to by $f4
Load/store instructions (lwc1, swc1) must still use
integer registers for address computation

## Slide 13
Code Example
float f2c (float fahr)
{
return ((5.0/9.0) * (fahr – 32.0));
}
(argument fahr is stored in $f12)
lwc1 $f16, const5
lwc1 $f18, const9
div.s $f16, $f16, $f18
lwc1 $f18, const32
sub.s $f18, $f12, $f18
mul.s $f0, $f16, $f18
jr $ra

## Slide 14
Fixed Point
FP operations are much slower than integer ops
Fixed point arithmetic uses integers, but assumes that
every number is multiplied by the same factor
Example: with a factor of 1/1000, the fixed-point
representations for 1.46, 1.7198, and 5624 are
respectively 1460, 1720, and 5624000
More programming effort and possibly lower precision
for higher performance

## Slide 15
Subword Parallelism
ALUs are typically designed to perform 64-bit or 128-bit
arithmetic
Some data types are much smaller, e.g., bytes for pixel
RGB values, half-words for audio samples
Partitioning the carry-chains within the ALU can convert
the 64-bit adder into 4 16-bit adders or 8 8-bit adders
A single load can fetch multiple values, and a single
add instruction can perform multiple parallel additions,
referred to as subword parallelism

## Slide 16
Digital Design Basics
Two voltage levels – high and low (1 and 0, true and false)
Hence, the use of binary arithmetic/logic in all computers
A transistor is a 3-terminal device that acts as a switch
V
V
0
0
Conducting
0
V
0
V
Non-conducting

## Slide 17
Logic Blocks
A logic block has a number of binary inputs and produces
a number of binary outputs – the simplest logic block is
composed of a few transistors
A logic block is termed combinational if the output is only
a function of the inputs
A logic block is termed sequential if the block has some
internal memory (state) that also influences the output
A basic logic block is termed a gate (AND, OR, NOT, etc.)
We will only deal with combinational circuits today

## Slide 18
Truth Table
A truth table defines the outputs of a logic block for each
set of inputs
Consider a block with 3 inputs A, B, C and an output E
that is true only if exactly 2 inputs are true
A B C E

## Slide 19
Truth Table
A truth table defines the outputs of a logic block for each
set of inputs
Consider a block with 3 inputs A, B, C and an output E
that is true only if exactly 2 inputs are true
A B C E
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 0
Can be compressed by only
representing cases that
have an output of 1