## Slide 1
Lecture 18: Pipelining
Today’s topics:
  5-stage pipeline
  Hazards
  Data dependence handling with bypassing
  Data dependence examples

## Slide 2
A 5-Stage Pipeline
Source: H&P textbook

## Slide 3
Performance Improvements?
Does it take longer to finish each individual job?
Does it take shorter to finish a series of jobs?
What assumptions were made while answering these
questions?
  No dependences between instructions
  Easy to partition circuits into uniform pipeline stages
  No latch overhead
Is a 10-stage pipeline better than a 5-stage pipeline?

## Slide 4
Quantitative Effects
As a result of pipelining:
  Time in ns per instruction goes up
  Each instruction takes more cycles to execute
  But… average CPI remains roughly the same
  Clock speed goes up
  Total execution time goes down, resulting in lower
  average time per instruction
  Under ideal conditions, speedup
  = ratio of elapsed times between successive instruction
  completions
  = number of pipeline stages = increase in clock speed

## Slide 5
Hazards
Structural hazards: different instructions in different stages
(or the same stage) conflicting for the same resource
Data hazards: an instruction cannot continue because it
needs a value that has not yet been generated by an
earlier instruction
Control hazard: fetch cannot continue because it does
not know the outcome of an earlier branch – special case
of a data hazard – separate category because they are
treated in different ways

## Slide 6
Conflicts/Problems
I-cache and D-cache are accessed in the same cycle – it
helps to implement them separately
Registers are read and written in the same cycle – easy to
deal with if register read/write time equals cycle time/2
Instructions can’t skip the DM stage, else conflict for RW
Consuming instruction may have to wait for producer
Branch target changes only at the end of the second stage
-- what do you do in the meantime?

## Slide 7
Structural Hazards
Example: a unified instruction and data cache 
stage 4 (MEM) and stage 1 (IF) can never coincide
The later instruction and all its successors are delayed
until a cycle is found when the resource is free  these
are pipeline bubbles
Structural hazards are easy to eliminate – increase the
number of resources (for example, implement a separate
instruction and data cache, add more register ports)

## Slide 8
Data Hazards
An instruction produces a value in a given pipeline stage
A subsequent instruction consumes that value in a pipeline
stage
The consumer may have to be delayed so that the time
of consumption is later than the time of production

## Slide 9
Example 1 – No Bypassing
D/R
ALU
DM
RW
IF
CYC-1
D/R
ALU
DM
RW
IF
CYC-2
D/R
ALU
DM
RW
IF
CYC-3
D/R
ALU
DM
RW
IF
CYC-4
D/R
ALU
DM
RW
IF
CYC-5
D/R
ALU
DM
RW
IF
CYC-6
D/R
ALU
DM
RW
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9

## Slide 10
Example 1 – No Bypassing
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I2
ALU
DM
I1
RW
IF
I3
CYC-4
D/R
I2
ALU
DM
RW
I1
IF
I3
CYC-5
D/R
I3
ALU
I2
DM
RW
IF
I4
CYC-6
D/R
I4
ALU
I3
DM
I2
RW
IF
I5
CYC-7
D/R
ALU
DM
I3
RW
I2
IF
CYC-8
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9

## Slide 11
Example 2 – Bypassing
D/R
ALU
DM
RW
IF
CYC-1
D/R
ALU
DM
RW
IF
CYC-2
D/R
ALU
DM
RW
IF
CYC-3
D/R
ALU
DM
RW
IF
CYC-4
D/R
ALU
DM
RW
IF
CYC-5
D/R
ALU
DM
RW
IF
CYC-6
D/R
ALU
DM
RW
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.

## Slide 12
Example 2 – Bypassing
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I3
ALU
I2
DM
I1
RW
IF
I4
CYC-4
D/R
I4
ALU
I3
DM
I2
RW
I1
IF
I5
CYC-5
D/R
ALU
DM
I3
RW
I2
IF
CYC-6
D/R
ALU
DM
RW
I3
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
L3 L3 L4 L3 L5 L3

## Slide 13
Problem 1
add $1, $2, $3
lw $4, 8($1)
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW

## Slide 14
Problem 2
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
lw $4, 8($1)

## Slide 15
Problem 3
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
lw $1, 8($2)
sw $1, 8($3)