## Slide 1
Lecture 22: Out-of-Order, Cache Hierarchies
Today’s topics:
  Out of order processors
  Cache access intro and details

## Slide 2
An Out-of-Order Processor Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 3
An Out-of-Order Processor Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 4
Example Code
Completion times with in-order with ooo
ADD R1, R2, R3 5 5
ADD R4, R1, R2 6 6
LW R5, 8(R4) 7 7
ADD R7, R6, R5 9 9
ADD R8, R7, R5 10 10
LW R9, 16(R4) 11 7
ADD R10, R6, R9 13 9
ADD R11, R10, R9 14 10

## Slide 5
Cache Hierarchies
Data and instructions are stored on DRAM chips – DRAM
is a technology that has high bit density, but relatively poor
latency – an access to data in memory can take as many
as 300 cycles today!
Hence, some data is stored on the processor in a structure
called the cache – caches employ SRAM technology, which
is faster, but has lower bit density
Internet browsers also cache web pages – same concept

## Slide 6
Memory Hierarchy
As you go further, capacity and latency increase
Registers
1KB
1 cycle
L1 data or
instruction
Cache
32KB
2 cycles
L2 cache
2MB
15 cycles
Memory
16GB
300 cycles
Disk
1 TB
10M cycles

## Slide 7
Locality
Why do caches work?
  Temporal locality: if you used some data recently, you
  will likely use it again
  Spatial locality: if you used some data recently, you
  will likely access its neighbors
No hierarchy: average access time for data = 300 cycles
32KB 1-cycle L1 cache that has a hit rate of 95%:
average access time = 0.95 x 1 + 0.05 x (301)
= 16 cycles

## Slide 8
Accessing the Cache

## Slide 9
Accessing the Cache

## Slide 10
Accessing the Cache
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique location in cache
8 words: 3 index bits
Byte address
Data array
Sets
Offset

## Slide 11
The Tag Array
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array

## Slide 12
Example Access Pattern
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 68, 73, 78, 83, 88, 4, 7, 10…

## Slide 13
Increasing Line Size
32-byte cache
line size or
block size
10100000
Byte address
Tag
Data array
Tag array
Offset
A large cache line size  smaller tag array,
fewer misses because of spatial locality

## Slide 14
Associativity
10100000
Byte address
Tag
Data array
Tag array
Set associativity  fewer conflicts; wasted power
because multiple data and tags are read
Way-1
Way-2
Compare

## Slide 15
Associativity
10100000
Byte address
Tag
Data array
Tag array
How many offset/index/tag bits if the cache has
64 sets,
each set has 64 bytes,
4 ways
Way-1
Way-2
Compare

## Slide 16
Example 1
32 KB 4-way set-associative data cache array with 32
byte line sizes
How many sets?
How many index bits, offset bits, tag bits?
How large is the tag array?
Cache size = #sets x #ways x blocksize
Index bits = log2(sets)
Offset bits = log2(blocksize)
Addr width = tag + index + offset

## Slide 17
Example 1
32 KB 4-way set-associative data cache array with 32
byte line sizes
cache size = #sets x #ways x block size
How many sets? 256
How many index bits, offset bits, tag bits?
8 5 19
log2(sets) log2(blksize) addrsize-index-offset
How large is the tag array?
tag array size = #sets x #ways x tag size
= 19 Kb = 2.375 KB