## Slide 1
Lecture 10: Floating Point
Today’s topics:
  IEEE 754 representations

## Slide 2
Floating Point
Normalized scientific notation: single non-zero digit to the
left of the decimal (binary) point – example: 3.5 x 109
1.010001 x 2-5two = (1 + 0 x 2-1 + 1 x 2-2 + … + 1 x 2-6) x 2-5ten
A standard notation enables easy exchange of data between
machines and simplifies hardware algorithms – the
IEEE 754 standard defines how floating point numbers
are represented

## Slide 3
Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
More exponent bits  wider range of numbers (not necessarily more
numbers – recall there are infinite real numbers)
More fraction bits  higher precision
Register value = (-1)S x F x 2E
Since we are only representing normalized numbers, we are
guaranteed that the number is of the form 1.xxxx..
Hence, in IEEE 754 standard, the 1 is implicit
Register value = (-1)S x (1 + F) x 2E

## Slide 4
Exponent Representation
To simplify sort, sign was placed as the first bit
For a similar reason, the representation of the exponent is also
modified: in order to use integer compares, it would be preferable to
have the smallest exponent as 00…0 and the largest exponent as 11…1
This is the biased notation, where a bias is subtracted from the
exponent field to yield the true exponent
IEEE 754 single-precision uses a bias of 127 (since the exponent
must have values between -127 and 128)…double precision uses
a bias of 1023
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)

## Slide 5
Sign and Magnitude Representation
Sign Exponent Fraction
1 bit 8 bits 23 bits
S
E
F
Largest number that can be represented: 2.0 x 2128 = 2.0 x 1038
(not really – see upcoming details)
Smallest number that can be represented: 1.0 x 2-127 = 2.0 x 10-38
(not really – see upcoming details)
Overflow: when representing a number larger than the max;
Underflow: when representing a number smaller than the min
Double precision format: occupies two 32-bit registers:
Largest: Smallest:
Sign Exponent Fraction
1 bit 11 bits 52 bits
S
E
F

## Slide 6
Details
The number “0” has a special code so that the implicit 1 does not
get added: the code is all 0s
(it may seem that this takes up the representation for 1.0, but
given how the exponent is represented, that’s not the case)
(see discussion of denorms in the textbook)
The largest exponent value (with zero fraction) represents +/- infinity
The largest exponent value (with non-zero fraction) represents
NaN (not a number) – for the result of 0/0 or (infinity minus infinity)
Note that these choices impact the smallest and largest numbers
that can be represented

## Slide 7
0 00..0 00…0
Value 0
Value 1
0 127 00…0
Value inf
Value NAN
Highest value ~2 x 2127
0 255 00…0
0 255 xx….x
0 254 11….1
Smallest Norm 1 x 2-126
Largest Denorm ~1 x 2-126
Smallest Denorm ~2-149
0 0..01 00…0
0 0..00 11…1
0 0..00 00…1
Same rules as above, but the sign bit is 1
Same magnitudes as above, but negative numbers
Exponent field < 127, i.e., after
subtracting bias, they are negative
exponents, representing numbers < 1
2 special cases up top that use the
reserved exponent field of 255
Special case with exponent field 0, used to
represent denorms, that help us gradually approach 0.
Denorms don’t have implicit 1. They have exp 2-126

## Slide 8
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
Double: (1 + 11 + 52)
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
Remember:
True exponent Exponent in register
+127
-127

## Slide 9
Examples
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent -0.75ten in single and double-precision formats
Single: (1 + 8 + 23)
1 0111 1110 1000…000
Double: (1 + 11 + 52)
1 0111 1111 110 1000…000
What decimal number is represented by the following
single-precision number?
1 1000 0001 01000…0000
-5.0

## Slide 10
Remember:
True exponent Exponent in register

## Slide 11
Example 2
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
Represent 36.90625ten in single-precision format
36 / 2 = 18 rem 0
18 / 2 = 9 rem 0
9 / 2 = 4 rem 1
4 / 2 = 2 rem 0
2 / 2 = 1 rem 0
1 / 2 = 0 rem 1
36 is 100100
0.90625 x 2 = 1.81250
0.8125 x 2 = 1.6250
0.625 x 2 = 1.250
0.25 x 2 = 0.50
0.5 x 2 = 1.00
0.0 x 2 = 0.0
0.90625 is 0.1110100…0

## Slide 12
Example 2
Final representation: (-1)S x (1 + Fraction) x 2(Exponent – Bias)
We’ve calculated that 36.90625ten = 100100.1110100…0 in binary
Normalized form = 1.001001110100…0 x 25
(had to shift 5 places to get only one bit left of the point)
The sign bit is 0 (positive number)
The fraction field is 001001110100…0 (the 23 bits after the point)
The exponent field is 5 + 127 (have to add the bias) = 132,
which in binary is 10000100
The IEEE 754 format is 0 10000100 001001110100…..0
sign exponent 23 fraction bits

## Slide 13
Remember:
True exponent Exponent in register