## Slide 1
Lecture 16: Basic Pipelining
Today’s topics:
  5-stage pipeline
  Hazards

## Slide 2
Latches and Clocks in a Single-Cycle Design
PC
Instr
Mem
Reg
File
ALU
Data
Memory
Addr
The entire instruction executes in a single cycle
Green blocks are latches
At the rising edge, a new PC is recorded
At the rising edge, the result of the previous cycle is recorded
At the falling edge, the address of LW/SW is recorded so
we can access the data memory in the 2nd half of the cycle

## Slide 3
Multi-Stage Circuit
Instead of executing the entire instruction in a single
cycle (a single stage), let’s break up the execution into
multiple stages, each separated by a latch
PC
Instr
Mem
ALU
Data
Memory
L2
Reg
File
L3
L4
Reg
File
L5

## Slide 4
The Assembly Line
A
Start and finish a job before moving to the next
Time
Jobs
Break the job into smaller stages
B
C
A
B
C
A
B
C
A
B
C
Unpipelined
Pipelined

## Slide 5
Performance Improvements?
Does it take longer to finish each individual job?
Does it take shorter to finish a series of jobs?
What assumptions were made while answering these
questions?
Is a 10-stage pipeline better than a 5-stage pipeline?

## Slide 6
A 5-Stage Pipeline
Source: H&P textbook

## Slide 7
A 5-Stage Pipeline
Use the PC to access the I-cache and increment PC by 4

## Slide 8
A 5-Stage Pipeline
Read registers, compare registers, compute branch target; for now, assume
branches take 2 cyc (there is enough work that branches can easily take more)

## Slide 9
A 5-Stage Pipeline
ALU computation, effective address computation for load/store

## Slide 10
A 5-Stage Pipeline
Memory access to/from data cache, stores finish in 4 cycles

## Slide 11
A 5-Stage Pipeline
Write result of ALU computation or load into register file

## Slide 12
Pipeline Summary
RR ALU DM RW
ADD R1, R2,  R3 Rd R1,R2 R1+R2 -- Wr R3
BEQ R1, R2, 100 Rd R1, R2 -- -- --
Compare, Set PC
LD 8[R3]  R6 Rd R3 R3+8 Get data Wr R6
ST 8[R3]  R6 Rd R3,R6 R3+8 Wr data --

## Slide 13
Performance Improvements?
Does it take longer to finish each individual job?
Does it take shorter to finish a series of jobs?
What assumptions were made while answering these
questions?
  No dependences between instructions
  Easy to partition circuits into uniform pipeline stages
  No latch overhead
Is a 10-stage pipeline better than a 5-stage pipeline?

## Slide 14
Quantitative Effects
As a result of pipelining:
  Time in ns per instruction goes up
  Each instruction takes more cycles to execute
  But… average CPI remains roughly the same
  Clock speed goes up
  Total execution time goes down, resulting in lower
  average time per instruction
  Under ideal conditions, speedup
  = ratio of elapsed times between successive instruction
  completions
  = number of pipeline stages = increase in clock speed

## Slide 15
Conflicts/Problems
I-cache and D-cache are accessed in the same cycle – it
helps to implement them separately
Registers are read and written in the same cycle – easy to
deal with if register read/write time equals cycle time/2
Branch target changes only at the end of the second stage
-- what do you do in the meantime?

## Slide 16
Hazards
Structural hazards: different instructions in different stages
(or the same stage) conflicting for the same resource
Data hazards: an instruction cannot continue because it
needs a value that has not yet been generated by an
earlier instruction
Control hazard: fetch cannot continue because it does
not know the outcome of an earlier branch – special case
of a data hazard – separate category because they are
treated in different ways