## Slide 1
Lecture 22: Cache Examples
Today’s topics:
  Cache access
  Example problems in cache design

## Slide 2
Accessing the Cache

## Slide 3
Accessing the Cache
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique location in cache
8 words: 3 index bits
Byte address
Data array
Sets
Offset

## Slide 4
The Tag Array
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array

## Slide 5
Example Access Pattern
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 68, 73, 78, 83, 88, 4, 7, 10…

## Slide 6
Increasing Line Size
32-byte cache
line size or
block size
10100000
Byte address
Tag
Data array
Tag array
Offset
A large cache line size  smaller tag array,
fewer misses because of spatial locality

## Slide 7
Associativity
10100000
Byte address
Tag
Data array
Tag array
Set associativity  fewer conflicts; wasted power
because multiple data and tags are read
Way-1
Way-2
Compare

## Slide 8
Associativity
10100000
Byte address
Tag
Data array
Tag array
How many offset/index/tag bits if the cache has
64 sets,
each set has 64 bytes,
4 ways
Way-1
Way-2
Compare

## Slide 9
Example 1
32 KB 4-way set-associative data cache array with 32
byte line sizes
How many sets?
How many index bits, offset bits, tag bits?
How large is the tag array?
Cache size = #sets x #ways x blocksize
Index bits = log2(sets)
Offset bits = log2(blocksize)
Addr width = tag + index + offset

## Slide 10
Example 1
32 KB 4-way set-associative data cache array with 32
byte line sizes
cache size = #sets x #ways x block size
How many sets? 256
How many index bits, offset bits, tag bits?
8 5 19
log2(sets) log2(blksize) addrsize-index-offset
How large is the tag array?
tag array size = #sets x #ways x tag size
= 19 Kb = 2.375 KB

## Slide 11
Example 2
Offset = address % 64 (address modulo 64, extract last 6)
Index = address/64 % 16 (shift right by 6, extract last 4)
Tag = address/1024 (shift address right by 10)
32-bit address
22 bits tag 4 bits index 6 bits offset
8: 0 0 8 M
96: 0 1 32 M
32: 0 0 32 H
480: 0 7 32 M
976: 0 15 16 M
1040: 1 0 16 M
1096: 1 1 8 M
Show how the following addresses map to the cache and yield hits or misses.
The cache is direct-mapped, has 16 sets, and a 64-byte block size.
Addresses: 8, 96, 32, 480, 976, 1040, 1096
.
.
.

## Slide 12
Example 3
A pipeline has CPI 1 if all loads/stores are L1 cache hits
40% of all instructions are loads/stores
85% of all loads/stores hit in 1-cycle L1
50% of all (10-cycle) L2 accesses are misses
Memory access takes 100 cycles
What is the CPI?

## Slide 13
Example 3
A pipeline has CPI 1 if all loads/stores are L1 cache hits
40% of all instructions are loads/stores
85% of all loads/stores hit in 1-cycle L1
50% of all (10-cycle) L2 accesses are misses
Memory access takes 100 cycles
What is the CPI?
Start with 1000 instructions
1000 cycles (includes all 400 L1 accesses)
+ 400 (ld/st) x 15% x 10 cycles (the L2 accesses)
+ 400 x 15% x 50% x 100 cycles (the mem accesses)
= 4,600 cycles
CPI = 4.6

## Slide 14
Example 4
00010000
Byte address
Tag
Data array
Tag array
8-byte blocks
Way-1
Way-2
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 24, 36, 4, 48, 64, 4, 36, 64, 4

## Slide 15
Example 4
00010000
Byte address
Tag
Data array
Tag array
8-byte blocks
Way-1
Way-2
Assume that addresses are 8 bits long
How many of the following address requests
are hits/misses?
4, 7, 10, 13, 16, 24, 36, 4, 48, 64, 4, 36, 64, 4
M H M H M M M H M M H M M M