## Slide 1
Lecture 8: Number Crunching
Today’s topics:
  MARS syscall wrap-up
  RISC vs. CISC
  Numerical representations
  Signed/Unsigned

## Slide 2
Example Print Routine
.data
str: .asciiz “the answer is ”
.text
li $v0, 4 # load immediate; 4 is the code for print_string
la $a0, str # the print_string syscall expects the string
# address as the argument; la is the instruction
# to load the address of the operand (str)
syscall # MARS will now invoke syscall-4
li $v0, 1 # syscall-1 corresponds to print_int
li $a0, 5 # print_int expects the integer as its argument
syscall # MARS will now invoke syscall-1

## Slide 3
Example
Write an assembly program to prompt the user for two
numbers and print the sum of the two numbers

## Slide 4
Example
.data
str1: .asciiz “Enter 2 numbers:”
str2: .asciiz “The sum is ”
.text li $v0, 4
la $a0, str1
syscall
li $v0, 5
syscall
add $t0, $v0, $zero
li $v0, 5
syscall
add $t1, $v0, $zero
li $v0, 4
la $a0, str2
syscall
li $v0, 1
add $a0, $t1, $t0
syscall

## Slide 5
IA-32 Instruction Set
Intel’s IA-32 instruction set has evolved over 20 years –
old features are preserved for software compatibility
Numerous complex instructions – complicates hardware
design (Complex Instruction Set Computer – CISC)
Instructions have different sizes, operands can be in
registers or memory, only 8 general-purpose registers,
one of the operands is over-written
RISC instructions are more amenable to high performance
(clock speed and parallelism) – modern Intel processors
convert IA-32 instructions into simpler micro-operations

## Slide 6
Large Constants
Immediate instructions can only specify 16-bit constants
The lui instruction is used to store a 16-bit constant into
the upper 16 bits of a register… combine this with an
OR instruction to specify a 32-bit constant
The destination PC-address in a conditional branch is
specified as a 16-bit constant, relative to the current PC
A jump (j) instruction can specify a 26-bit constant; if more
bits are required, the jump-register (jr) instruction is used
See green sheet!

## Slide 7
Endian-ness
Two major formats for transferring values between registers and memory
Memory: low address 45 7b 87 7f high address
Little-endian register: the first byte read goes in the low end of the register
Register: 7f 87 7b 45
Most-significant bit Least-significant bit (x86)
Big-endian register: the first byte read goes in the big end of the register
Register: 45 7b 87 7f
Most-significant bit Least-significant bit (MIPS, IBM)

## Slide 8
Binary Representation
The binary number
01011000 00010101 00101110 11100111
represents the quantity
0 x 231 + 1 x 230 + 0 x 229 + … + 1 x 20
A 32-bit word can represent 232 numbers between
0 and 232-1
… this is known as the unsigned representation as
we’re assuming that numbers are always positive
Most significant bit
Least significant bit

## Slide 9
ASCII Vs. Binary
Does it make more sense to represent a decimal number
in ASCII?
Hardware to implement arithmetic would be difficult
What are the storage needs? How many bits does it
take to represent the decimal number 1,000,000,000 in
ASCII and in binary?

## Slide 10
ASCII Vs. Binary
Does it make more sense to represent a decimal number
in ASCII?
Hardware to implement arithmetic would be difficult
What are the storage needs? How many bits does it
take to represent the decimal number 1,000,000,000 in
ASCII and in binary?
In binary: 30 bits (230 > 1 billion)
In ASCII: 10 characters, 8 bits per char = 80 bits

## Slide 11
Negative Numbers
32 bits can only represent 232 numbers – if we wish to also represent
negative numbers, we can represent 231 positive numbers (incl zero)
and 231 negative numbers
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
…
0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
1000 0000 0000 0000 0000 0000 0000 0000two = -231
1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
…
1111 1111 1111 1111 1111 1111 1111 1110two = -2
1111 1111 1111 1111 1111 1111 1111 1111two = -1

## Slide 12
2’s Complement
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
…
0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
1000 0000 0000 0000 0000 0000 0000 0000two = -231
1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
…
1111 1111 1111 1111 1111 1111 1111 1110two = -2
1111 1111 1111 1111 1111 1111 1111 1111two = -1
Why is this representation favorable?
Consider the sum of 1 and -2 …. we get -1
Consider the sum of 2 and -1 …. we get +1
This format can directly undergo addition without any conversions!
Each number represents the quantity
x31 -231 + x30 230 + x29 229 + … + x1 21 + x0 20

## Slide 13
2’s Complement
0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
…
0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
1000 0000 0000 0000 0000 0000 0000 0000two = -231
1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
…
1111 1111 1111 1111 1111 1111 1111 1110two = -2
1111 1111 1111 1111 1111 1111 1111 1111two = -1
Note that the sum of a number x and its inverted representation x’ always
equals a string of 1s (-1).
x + x’ = -1
x’ + 1 = -x … hence, can compute the negative of a number by
-x = x’ + 1 inverting all bits and adding 1
Similarly, the sum of x and –x gives us all zeroes, with a carry of 1
In reality, x + (-x) = 2n … hence the name 2’s complement

## Slide 14
Example
Compute the 32-bit 2’s complement representations
for the following decimal numbers:
5, -5, -6

## Slide 15
Example
Compute the 32-bit 2’s complement representations
for the following decimal numbers:
5, -5, -6
5: 0000 0000 0000 0000 0000 0000 0000 0101
-5: 1111 1111 1111 1111 1111 1111 1111 1011
-6: 1111 1111 1111 1111 1111 1111 1111 1010
Given -5, verify that inverting and adding 1 yields the
number 5

## Slide 16
Signed / Unsigned
The hardware recognizes two formats:
unsigned (corresponding to the C declaration unsigned int)
-- all numbers are positive, a 1 in the most significant bit
just means it is a really large number
signed (C declaration is signed int or just int)
-- numbers can be +/- , a 1 in the MSB means the number
is negative
This distinction enables us to represent twice as many
numbers when we’re sure that we don’t need negatives

## Slide 17
MIPS Instructions
Consider a comparison instruction:
slt $t0, $t1, $zero
and $t1 contains the 32-bit number 1111 01…01
What gets stored in $t0?

## Slide 18
MIPS Instructions
Consider a comparison instruction:
slt $t0, $t1, $zero
and $t1 contains the 32-bit number 1111 01…01
What gets stored in $t0?
The result depends on whether $t1 is a signed or unsigned
number – the compiler/programmer must track this and
accordingly use either slt or sltu
slt $t0, $t1, $zero stores 1 in $t0
sltu $t0, $t1, $zero stores 0 in $t0

## Slide 19
Sign Extension
Occasionally, 16-bit signed numbers must be converted
into 32-bit signed numbers – for example, when doing an
add with an immediate operand
The conversion is simple: take the most significant bit and
use it to fill up the additional bits on the left – known as
sign extension
So 210 goes from 0000 0000 0000 0010 to
0000 0000 0000 0000 0000 0000 0000 0010
and -210 goes from 1111 1111 1111 1110 to
1111 1111 1111 1111 1111 1111 1111 1110

## Slide 20
Alternative Representations
The following two (intuitive) representations were discarded
because they required additional conversion steps before
arithmetic could be performed on the numbers
  sign-and-magnitude: the most significant bit represents
  +/- and the remaining bits express the magnitude
  one’s complement: -x is represented by inverting all
  the bits of x
  Both representations above suffer from two zeroes