## Slide 1
Lecture: Pipelining, Static ILP
Topics: wrap-up of pipelining impacts, static ILP approaches,
scheduling, loop unrolling, software pipelines

## Slide 2
Multicycle Instructions

## Slide 3
Effects of Multicycle Instructions
Potentially multiple writes to the register file in a cycle
Frequent RAW hazards
WAW hazards (WAR hazards not possible)
Imprecise exceptions because of o-o-o instr completion
Note: Can also increase the “width” of the processor: handle
multiple instructions at the same time: for example, fetch
two instructions, read registers for both, execute both, etc.

## Slide 4
Precise Exceptions
On an exception:
  must save PC of instruction where program must resume
  all instructions after that PC that might be in the pipeline
  must be converted to NOPs (other instructions continue
  to execute and may raise exceptions of their own)
  temporary program state not in memory (in other words,
  registers) has to be stored in memory
  potential problems if a later instruction has already
  modified memory or registers
A processor that fulfils all the above conditions is said to
provide precise exceptions (useful for debugging and of
course, correctness)

## Slide 5
Dealing with these Effects
Multiple writes to the register file: increase the number of
ports, stall one of the writers during ID, stall one of the
writers during WB (the stall will propagate)
WAW hazards: detect the hazard during ID and stall the
later instruction
Imprecise exceptions: buffer the results if they complete
early or save more pipeline state so that you can return to
exactly the same state that you left at

## Slide 6
Slowdowns from Stalls
Perfect pipelining with no hazards  an instruction
completes every cycle (total cycles ~ num instructions)
 speedup = increase in clock speed = num pipeline stages
With hazards and stalls, some cycles (= stall time) go by
during which no instruction completes, and then the stalled
instruction completes
Total cycles = number of instructions + stall cycles
Slowdown because of stalls = 1/ (1 + stall cycles per instr)

## Slide 7
Pipelining Limits
A
B
C
A
B
C
A
B
C
D
E
F
A
B
C
D
E
F
Assume that there is a dependence where the final result of the
first instruction is required before starting the second instruction
Gap between indep instrs: T + Tovh
Gap between dep instrs: T + Tovh
Gap between indep instrs:
T/3 + Tovh
Gap between dep instrs:
T + 3Tovh
Gap between indep instrs:
T/6 + Tovh
Gap between dep instrs:
T + 6Tovh

## Slide 8
Problem 2
Assume an unpipelined processor where it takes 5ns to
go through the circuits and 0.1ns for the latch overhead.
What is the throughput for 20-stage and 40-stage
pipelines? Assume that the P.O.P and P.O.C in the
unpipelined processor are separated by 2ns. Assume that
half the instructions do not introduce a data hazard and
half the instructions depend on their preceding instruction.

## Slide 9
Problem 2
Assume an unpipelined processor where it takes 5ns to
go through the circuits and 0.1ns for the latch overhead.
What is the throughput for 1-stage, 20-stage and 50-stage
pipelines? Assume that the P.O.P and P.O.C in the
unpipelined processor are separated by 2ns. Assume that
half the instructions do not introduce a data hazard and
half the instructions depend on their preceding instruction.
  1-stage: 1 instr every 5.1ns
  20-stage: first instr takes 0.35ns, the second takes 2.8ns
  50-stage: first instr takes 0.2ns, the second takes 4ns
  Throughputs: 0.20 BIPS, 0.63 BIPS, and 0.48 BIPS

## Slide 10
ILP
Instruction-level parallelism: overlap among instructions:
pipelining or multiple instruction execution
What determines the degree of ILP?
  dependences: property of the program
  hazards: property of the pipeline

## Slide 11
Static vs Dynamic Scheduling
Arguments against dynamic scheduling:
  requires complex structures to identify independent
  instructions (scoreboards, issue queue)
    high power consumption
    low clock speed
    high design and verification effort
  the compiler can “easily” compute instruction latencies
  and dependences – complex software is always
  preferred to complex hardware (?)

## Slide 12
Loop Scheduling
The compiler’s job is to minimize stalls
Focus on loops: account for most cycles, relatively easy
to analyze and optimize

## Slide 13
Assumptions
Load: 2-cycles (1 cycle stall for consumer)
FP ALU: 4-cycles (3 cycle stall for consumer; 2 cycle stall
if the consumer is a store)
One branch delay slot
Int ALU: 1-cycle (no stall for consumer, 1 cycle stall if the
consumer is a branch)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 14
Loop Example
for (i=1000; i>0; i--)
x[i] = x[i] + s;
Loop: L.D F0, 0(R1) ; F0 = array element
ADD.D F4, F0, F2 ; add scalar
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
BNE R1, R2, Loop ; branch if R1 != R2
NOP
Source code
Assembly code
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 15
Loop Example
for (i=1000; i>0; i--)
x[i] = x[i] + s;
Loop: L.D F0, 0(R1) ; F0 = array element
ADD.D F4, F0, F2 ; add scalar
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
BNE R1, R2, Loop ; branch if R1 != R2
NOP
Source code
Assembly code
Loop: L.D F0, 0(R1) ; F0 = array element
stall
ADD.D F4, F0, F2 ; add scalar
stall
stall
S.D F4, 0(R1) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
stall
BNE R1, R2, Loop ; branch if R1 != R2
stall
10-cycle
schedule
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 16
Smart Schedule
By re-ordering instructions, it takes 6 cycles per iteration instead of 10
We were able to violate an anti-dependence easily because an
immediate was involved
Loop overhead (instrs that do book-keeping for the loop): 2
Actual work (the ld, add.d, and s.d): 3 instrs
Can we somehow get execution time to be 3 cycles per iteration?
Loop: L.D F0, 0(R1)
stall
ADD.D F4, F0, F2
stall
stall
S.D F4, 0(R1)
DADDUI R1, R1,# -8
stall
BNE R1, R2, Loop
stall
Loop: L.D F0, 0(R1)
DADDUI R1, R1,# -8
ADD.D F4, F0, F2
stall
BNE R1, R2, Loop
S.D F4, 8(R1)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 17
Problem 1
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many cycles do the default and optimized schedules take?

## Slide 18
Problem 1
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many cycles do the default and optimized schedules take?
Unoptimized: LD 1s MUL 4s SD DA DA BNE 1s -- 12 cycles
Optimized: LD DA MUL DA 2s BNE SD -- 8 cycles

## Slide 19
Loop Unrolling
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
L.D F6, -8(R1)
ADD.D F8, F6, F2
S.D F8, -8(R1)
L.D F10,-16(R1)
ADD.D F12, F10, F2
S.D F12, -16(R1)
L.D F14, -24(R1)
ADD.D F16, F14, F2
S.D F16, -24(R1)
DADDUI R1, R1, #-32
BNE R1,R2, Loop
Loop overhead: 2 instrs; Work: 12 instrs
How long will the above schedule take to complete?

## Slide 20
Scheduled and Unrolled Loop
Loop: L.D F0, 0(R1)
L.D F6, -8(R1)
L.D F10,-16(R1)
L.D F14, -24(R1)
ADD.D F4, F0, F2
ADD.D F8, F6, F2
ADD.D F12, F10, F2
ADD.D F16, F14, F2
S.D F4, 0(R1)
S.D F8, -8(R1)
DADDUI R1, R1, # -32
S.D F12, 16(R1)
BNE R1,R2, Loop
S.D F16, 8(R1)
Execution time: 14 cycles or 3.5 cycles per original iteration
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 21
Loop Unrolling
Increases program size
Requires more registers
To unroll an n-iteration loop by degree k, we will need (n/k)
iterations of the larger loop, followed by (n mod k) iterations
of the original loop

## Slide 22
Automating Loop Unrolling
Determine the dependences across iterations: in the
example, we knew that loads and stores in different iterations
did not conflict and could be re-ordered
Determine if unrolling will help – possible only if iterations
are independent
Determine address offsets for different loads/stores
Dependency analysis to schedule code without introducing
hazards; eliminate name dependences by using additional
registers

## Slide 23
Problem 2
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many unrolls does it take to avoid stall cycles?

## Slide 24
Problem 2
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many unrolls does it take to avoid stall cycles?
Degree 2: LD LD MUL MUL DA DA 1s SD BNE SD
Degree 3: LD LD LD MUL MUL MUL DA DA SD SD BNE SD
– 12 cyc/3 iterations