## Slide 1
Lecture: Out-of-order Processors
Topics: ooo scheduling example, load-store queues,
memory dependences

## Slide 2
The Alpha 21264 Out-of-Order Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Reorder Buffer (ROB)
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
Issue Queue (IQ)
ALU
ALU
ALU
Register File
P1-P64
Results written to
regfile and tags
broadcast to IQ
Speculative
Reg Map
R1P36
R2P34
Committed
Reg Map
R1P1
R2P2

## Slide 3
Problem 3
Show the renamed version of the following code:
Assume that you have 36 physical registers and 32
architected registers. When does each instr leave the IQ?
R1  R2+R3
R1  R1+R5
BEQZ R1
R1  R4 + R5
R4  R1 + R7
R1  R6 + R8
R4  R3 + R1
R1  R5 + R9

## Slide 4
Problem 3
Show the renamed version of the following code:
Assume that you have 36 physical registers and 32
architected registers. When does each instr leave the IQ?
R1  R2+R3 P33  P2+P3
R1  R1+R5 P34  P33+P5
BEQZ R1 BEQZ P34
R1  R4 + R5 P35  P4+P5
R4  R1 + R7 P36  P35+P7
R1  R6 + R8 P1  P6+P8
R4  R3 + R1 P33  P3+P1
R1  R5 + R9 P34  P5+P9

## Slide 5
Problem 3
Show the renamed version of the following code:
Assume that you have 36 physical registers and 32
architected registers. When does each instr leave the IQ?
R1  R2+R3 P33  P2+P3 cycle i
R1  R1+R5 P34  P33+P5 i+1
BEQZ R1 BEQZ P34 i+2
R1  R4 + R5 P35  P4+P5 i
R4  R1 + R7 P36  P35+P7 i+1
R1  R6 + R8 P1  P6+P8 j
R4  R3 + R1 P33  P3+P1 j+1
R1  R5 + R9 P34  P5+P9 j+2
Width is assumed to be 4.
j depends on the #stages between issue and commit.

## Slide 6
OOO Example
Assume there are 36 physical registers and 32 logical
registers, and width is 4
Estimate the issue time, completion time, and commit time
for the sample code
IQ

## Slide 7
Assumptions
Perfect branch prediction, instruction fetch, caches
ADD  dep has no stall; LD  dep has one stall
An instr is placed in the IQ at the end of its 5th stage,
an instr takes 5 more stages after leaving the IQ
(ld/st instrs take 6 more stages after leaving the IQ)
IQ

## Slide 8
OOO Example
Original code Renamed code
ADD R1, R2, R3
LD R2, 8(R1)
ADD R2, R2, 8
ST R1, (R3)
SUB R1, R1, R5
LD R1, 8(R2)
ADD R1, R1, R2
IQ

## Slide 9
OOO Example
Original code Renamed code
ADD R1, R2, R3 ADD P33, P2, P3
LD R2, 8(R1) LD P34, 8(P33)
ADD R2, R2, 8 ADD P35, P34, 8
ST R1, (R3) ST P33, (P3)
SUB R1, R1, R5 SUB P36, P33, P5
LD R1, 8(R2) Must wait
ADD R1, R1, R2
IQ

## Slide 10
OOO Example
Original code Renamed code InQ Iss Comp Comm
ADD R1, R2, R3 ADD P33, P2, P3
LD R2, 8(R1) LD P34, 8(P33)
ADD R2, R2, 8 ADD P35, P34, 8
ST R1, (R3) ST P33, (P3)
SUB R1, R1, R5 SUB P36, P33, P5
LD R1, 8(R2)
ADD R1, R1, R2
IQ

## Slide 11
OOO Example
Original code Renamed code InQ Iss Comp Comm
ADD R1, R2, R3 ADD P33, P2, P3 i i+1 i+6 i+6
LD R2, 8(R1) LD P34, 8(P33) i i+2 i+8 i+8
ADD R2, R2, 8 ADD P35, P34, 8 i i+4 i+9 i+9
ST R1, (R3) ST P33, (P3) i i+2 i+8 i+9
SUB R1, R1, R5 SUB P36, P33, P5 i+1 i+2 i+7 i+9
LD R1, 8(R2)
ADD R1, R1, R2
IQ

## Slide 12
OOO Example
Original code Renamed code InQ Iss Comp Comm
ADD R1, R2, R3 ADD P33, P2, P3 i i+1 i+6 i+6
LD R2, 8(R1) LD P34, 8(P33) i i+2 i+8 i+8
ADD R2, R2, 8 ADD P35, P34, 8 i i+4 i+9 i+9
ST R1, (R3) ST P33, (P3) i i+2 i+8 i+9
SUB R1, R1, R5 SUB P36, P33, P5 i+1 i+2 i+7 i+9
LD R1, 8(R2) LD P1, 8(P35) i+7 i+8 i+14 i+14
ADD R1, R1, R2 ADD P2, P1, P35 i+9 i+10 i+15 i+15
IQ

## Slide 13
OOO Example
Original code Renamed code InQ Iss Comp Comm Prev Map
ADD R1, R2, R3 ADD P33, P2, P3 i i+1 i+6 i+6 P1
LD R2, 8(R1) LD P34, 8(P33) i i+2 i+8 i+8 P2
ADD R2, R2, 8 ADD P35, P34, 8 i i+4 i+9 i+9 P34
ST R1, (R3) ST P33, (P3) i i+2 i+8 i+9
SUB R1, R1, R5 SUB P36, P33, P5 i+1 i+2 i+7 i+9 P33
LD R1, 8(R2) LD P1, 8(P35) i+7 i+8 i+14 i+14 P36
ADD R1, R1, R2 ADD P2, P1, P35 i+9 i+10 i+15 i+15 P1
IQ

## Slide 14
Constraints Worth Remembering
Don’t exceed rename width, issue width, commit width
Make notes about a register’s previous mapping (so you can
release it upon that instruction’s commit)
Stall when out of registers
Delay instructions with data dependences
Factor in 5/6 stages for completion, depending on instr type
InQ and Commit columns must monotonically increase;
Issue and Complete times can be ooo

## Slide 15
Additional Details
When does the decode stage stall? When we either run
out of registers, or ROB entries, or issue queue entries
Issue width: the number of instructions handled by each
stage in a cycle. High issue width  high peak ILP
Window size: the number of in-flight instructions in the
pipeline. Large window size  high ILP
No more WAR and WAW hazards because of rename
registers – must only worry about RAW hazards

## Slide 16
Branch Mispredict Recovery
On a branch mispredict, must roll back the processor state:
throw away IFQ contents, ROB/IQ contents after branch
Committed map table is correct and need not be fixed
The speculative map table needs to go back to an earlier state
To facilitate this spec-map-table rollback, it is checkpointed
at every branch

## Slide 17
Waking Up a Dependent
In an in-order pipeline, an instruction leaves the decode
stage when it is known that the inputs can be correctly
received, not when the inputs are computed
Similarly, an instruction leaves the issue queue before its
inputs are known, i.e., wakeup is speculative based on the
expected latency of the producer instruction

## Slide 18
Out-of-Order Loads/Stores
Ld
R1  [R2]
Ld
St
Ld
Ld
What if the issue queue also had load/store instructions?
Can we continue executing instructions out-of-order?
R3  [R4]
R5  [R6]
R7  [R8]
R9[R10]

## Slide 19
Memory Dependence Checking
Ld
0x abcdef
Ld
St
Ld
Ld
0x abcdef
St
0x abcd00
Ld
0x abc000
Ld
0x abcd00
The issue queue checks for
register dependences and
executes instructions as soon
as registers are ready
Loads/stores access memory
as well – must check for RAW,
WAW, and WAR hazards for
memory as well
Hence, first check for register
dependences to compute
effective addresses; then check
for memory dependences

## Slide 20
Memory Dependence Checking
Ld
0x abcdef
Ld
St
Ld
Ld
0x abcdef
St
0x abcd00
Ld
0x abc000
Ld
0x abcd00
Load and store addresses are
maintained in program order in
the Load/Store Queue (LSQ)
Loads can issue if they are
guaranteed to not have true
dependences with earlier stores
Stores can issue only if we are
ready to modify memory (can not
recover if an earlier instr raises
an exception) – happens at commit

## Slide 21
The Alpha 21264 Out-of-Order Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
LD R4  8[R3]
ST R4  8[R1]
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Instr 7
Reorder Buffer (ROB)
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
P37  8[P35]
P37  8[P36]
Issue Queue (IQ)
ALU
ALU
ALU
Register File
P1-P64
Results written to
regfile and tags
broadcast to IQ
P37  [P35 + 8]
P37  [P36 + 8]
LSQ
ALU
D-Cache
Committed
Reg Map
R1P1
R2P2
Speculative
Reg Map
R1P36
R2P34

## Slide 22
Problem 2
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd
LD R3  [R4] 6 adde
ST R5  [R6] 4 7 abba
LD R7  [R8] 2 abce
ST R9  [R10] 8 3 abba
LD R11  [R12] 1 abba

## Slide 23
Problem 2
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd 4 5
LD R3  [R4] 6 adde 7 8
ST R5  [R6] 4 7 abba 5 commit
LD R7  [R8] 2 abce 3 6
ST R9  [R10] 8 3 abba 9 commit
LD R11  [R12] 1 abba 2 10

## Slide 24
Problem 3
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd
LD R3  [R4] 6 adde
ST R5  [R6] 5 7 abba
LD R7  [R8] 2 abce
ST R9  [R10] 1 4 abba
LD R11  [R12] 2 abba

## Slide 25
Problem 3
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd 4 5
LD R3  [R4] 6 adde 7 8
ST R5  [R6] 5 7 abba 6 commit
LD R7  [R8] 2 abce 3 7
ST R9  [R10] 1 4 abba 2 commit
LD R11  [R12] 2 abba 3 5

## Slide 26
Problem 4
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd
LD R3  [R4] 6 adde
ST R5  [R6] 4 7 abba
LD R7  [R8] 2 abce
ST R9  [R10] 8 3 abba
LD R11  [R12] 1 abba

## Slide 27
Problem 4
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd 4 5
LD R3  [R4] 6 adde 7 8
ST R5  [R6] 4 7 abba 5 commit
LD R7  [R8] 2 abce 3 4
ST R9  [R10] 8 3 abba 9 commit
LD R11  [R12] 1 abba 2 3/10