## Slide 1
Lecture: Cache Hierarchies
Topics: cache access basics/examples

## Slide 2
Out-of-Order Loads/Stores
Ld
R1  [R2]
Ld
St
Ld
Ld
What if the issue queue also had load/store instructions?
Can we continue executing instructions out-of-order?
R3  [R4]
R5  [R6]
R7  [R8]
R9[R10]

## Slide 3
Memory Dependence Checking
Ld
0x abcdef
Ld
St
Ld
Ld
0x abcdef
St
0x abcd00
Ld
0x abc000
Ld
0x abcd00
The issue queue checks for
register dependences and
executes instructions as soon
as registers are ready
Loads/stores access memory
as well – must check for RAW,
WAW, and WAR hazards for
memory as well
Hence, first check for register
dependences to compute
effective addresses; then check
for memory dependences

## Slide 4
Memory Dependence Checking
Ld
0x abcdef
Ld
St
Ld
Ld
0x abcdef
St
0x abcd00
Ld
0x abc000
Ld
0x abcd00
Load and store addresses are
maintained in program order in
the Load/Store Queue (LSQ)
Loads can issue if they are
guaranteed to not have true
dependences with earlier stores
Stores can issue only if we are
ready to modify memory (can not
recover if an earlier instr raises
an exception) – happens at commit

## Slide 5
The Alpha 21264 Out-of-Order Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
LD R4  8[R3]
ST R4  8[R1]
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Instr 7
Reorder Buffer (ROB)
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
P37  8[P35]
P37  8[P36]
Issue Queue (IQ)
ALU
ALU
ALU
Register File
P1-P64
Results written to
regfile and tags
broadcast to IQ
P37  [P35 + 8]
P37  [P36 + 8]
LSQ
ALU
D-Cache
Committed
Reg Map
R1P1
R2P2
Speculative
Reg Map
R1P36
R2P34

## Slide 6
Problem 2
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd
LD R3  [R4] 6 adde
ST R5  [R6] 4 7 abba
LD R7  [R8] 2 abce
ST R9  [R10] 8 3 abba
LD R11  [R12] 1 abba

## Slide 7
Problem 2
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd 4 5
LD R3  [R4] 6 adde 7 8
ST R5  [R6] 4 7 abba 5 commit
LD R7  [R8] 2 abce 3 6
ST R9  [R10] 8 3 abba 9 commit
LD R11  [R12] 1 abba 2 10

## Slide 8
Problem 3
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd
LD R3  [R4] 6 adde
ST R5  [R6] 5 7 abba
LD R7  [R8] 2 abce
ST R9  [R10] 1 4 abba
LD R11  [R12] 2 abba

## Slide 9
Problem 3
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume no
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd 4 5
LD R3  [R4] 6 adde 7 8
ST R5  [R6] 5 7 abba 6 commit
LD R7  [R8] 2 abce 3 7
ST R9  [R10] 1 4 abba 2 commit
LD R11  [R12] 2 abba 3 5

## Slide 10
Problem 4
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd
LD R3  [R4] 6 adde
ST R5  [R6] 4 7 abba
LD R7  [R8] 2 abce
ST R9  [R10] 8 3 abba
LD R11  [R12] 1 abba

## Slide 11
Problem 4
Consider the following LSQ and when operands are
available. Estimate when the address calculation and
memory accesses happen for each ld/st. Assume
memory dependence prediction.
Ad. Op St. Op Ad.Val Ad.Cal Mem.Acc
LD R1  [R2] 3 abcd 4 5
LD R3  [R4] 6 adde 7 8
ST R5  [R6] 4 7 abba 5 commit
LD R7  [R8] 2 abce 3 4
ST R9  [R10] 8 3 abba 9 commit
LD R11  [R12] 1 abba 2 3/10

## Slide 12
The Cache Hierarchy
Core
L1
L2
L3
Off-chip memory

## Slide 13
Problem 1
Memory access time: Assume a program that has cache
access times of 1-cyc (L1), 10-cyc (L2), 30-cyc (L3), and
300-cyc (memory), and MPKIs of 20 (L1), 10 (L2), and 5 (L3).
Should you get rid of the L3?

## Slide 14
Problem 1
Memory access time: Assume a program that has cache
access times of 1-cyc (L1), 10-cyc (L2), 30-cyc (L3), and
300-cyc (memory), and MPKIs of 20 (L1), 10 (L2), and 5 (L3).
Should you get rid of the L3?
With L3: 1000 + 10x20 + 30x10 + 300x5 = 3000
Without L3: 1000 + 10x20 + 10x300 = 4200

## Slide 16
Accessing the Cache
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
8 words: 3 index bits
Byte address
Data array
Sets
Offset

## Slide 17
The Tag Array
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array

## Slide 18
Increasing Line Size
32-byte cache
line size or
block size
10100000
Byte address
Tag
Data array
Tag array
Offset
A large cache line size  smaller tag array,
fewer misses because of spatial locality

## Slide 19
Associativity
10100000
Byte address
Tag
Data array
Tag array
Set associativity  fewer conflicts; wasted power
because multiple data and tags are read
Way-1
Way-2
Compare

## Slide 20
Problem 2
Assume a direct-mapped cache with just 4 sets. Assume
that block A maps to set 0, B to 1, C to 2, D to 3, E to 0, and
so on. For the following access pattern, estimate the hits
and misses:
A B B E C C A D B F A E G C G A

## Slide 21
Problem 2
Assume a direct-mapped cache with just 4 sets. Assume
that block A maps to set 0, B to 1, C to 2, D to 3, E to 0, and
so on. For the following access pattern, estimate the hits
and misses:
A B B E C C A D B F A E G C G A
M MH MM H MM HM HMM M M M

## Slide 22
Problem 3
Assume a 2-way set-associative cache with just 2 sets.
Assume that block A maps to set 0, B to 1, C to 0, D to 1,
E to 0, and so on. For the following access pattern,
estimate the hits and misses:
A B B E C C A D B F A E G C G A

## Slide 23
Problem 3
Assume a 2-way set-associative cache with just 2 sets.
Assume that block A maps to set 0, B to 1, C to 0, D to 1,
E to 0, and so on. For the following access pattern,
estimate the hits and misses:
A B B E C C A D B F A E G C G A
M MH M MH MM HM HMM M H M

## Slide 24
Problem 4
64 KB 16-way set-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets?
How many index bits, offset bits, tag bits?
How large is the tag array?
Equations:
Data array size (cache size) = #sets x #ways x blocksize
Tag array size = #sets x #ways x tagsize
Index bits = log2 (#sets)
Offset bits = log2 (blocksize)
Tag bits + index bits + offset bits = address width

## Slide 25
Problem 4
64 KB 16-way set-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets? 64
How many index bits (6), offset bits (6), tag bits (28)?
How large is the tag array (28 Kb)?

## Slide 26
Problem 5
8 KB fully-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets? How many ways?
How many index bits, offset bits, tag bits?
How large is the tag array?

## Slide 27
Problem 5
8 KB fully-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets (1) ? How many ways (128) ?
How many index bits (0), offset bits (6), tag bits (34) ?
How large is the tag array (544 bytes) ?