## Slide 1
Lecture: Cache Hierarchies
Topics: cache access basics, example problems on cache access

## Slide 3
Accessing the Cache
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
8 words: 3 index bits
Byte address
Data array
Sets
Offset

## Slide 4
The Tag Array
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array

## Slide 5
Increasing Line Size
32-byte cache
line size or
block size
10100000
Byte address
Tag
Data array
Tag array
Offset
A large cache line size  smaller tag array,
fewer misses because of spatial locality

## Slide 6
Associativity
10100000
Byte address
Tag
Data array
Tag array
Set associativity  fewer conflicts; wasted power
because multiple data and tags are read
Way-1
Way-2
Compare

## Slide 7
Problem 2
Assume a direct-mapped cache with just 4 sets. Assume
that block A maps to set 0, B to 1, C to 2, D to 3, E to 0, and
so on. For the following access pattern, estimate the hits
and misses:
A B B E C C A D B F A E G C G A

## Slide 8
Problem 2
Assume a direct-mapped cache with just 4 sets. Assume
that block A maps to set 0, B to 1, C to 2, D to 3, E to 0, and
so on. For the following access pattern, estimate the hits
and misses:
A B B E C C A D B F A E G C G A
M MH MM H MM HM HMM M M M

## Slide 9
Problem 3
Assume a 2-way set-associative cache with just 2 sets.
Assume that block A maps to set 0, B to 1, C to 0, D to 1,
E to 0, and so on. For the following access pattern,
estimate the hits and misses:
A B B E C C A D B F A E G C G A

## Slide 10
Problem 3
Assume a 2-way set-associative cache with just 2 sets.
Assume that block A maps to set 0, B to 1, C to 0, D to 1,
E to 0, and so on. For the following access pattern,
estimate the hits and misses:
A B B E C C A D B F A E G C G A
M MH M MH MM HM HMM M H M

## Slide 11
Problem 4
64 KB 16-way set-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets?
How many index bits, offset bits, tag bits?
How large is the tag array?
Equations:
Data array size (cache size) = #sets x #ways x blocksize
Tag array size = #sets x #ways x tagsize
Index bits = log2 (#sets)
Offset bits = log2 (blocksize)
Tag bits + index bits + offset bits = address width

## Slide 12
Problem 4
64 KB 16-way set-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets? 64
How many index bits (6), offset bits (6), tag bits (28)?
How large is the tag array (28 Kb)?

## Slide 13
Problem 5
8 KB fully-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets? How many ways?
How many index bits, offset bits, tag bits?
How large is the tag array?

## Slide 14
Problem 5
8 KB fully-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets (1) ? How many ways (128) ?
How many index bits (0), offset bits (6), tag bits (34) ?
How large is the tag array (544 bytes) ?
Equations:
Data array size (cache size) = #sets x #ways x blocksize
Tag array size = #sets x #ways x tagsize
Index bits = log2 (#sets)
Offset bits = log2 (blocksize)
Tag bits + index bits + offset bits = address width