## Slide 1
Lecture: Multi-threading
Topics: coherence wrap-up, shared-memory vs. msg-passing,
synchronization primitives

## Slide 2
Directory-Based Example
Request | Cache Hit/Miss | Messages | Dir State | State in C1 | State in C2 | State in C3 | State in C4
 |  |  |  | Inv | Inv | Inv | Inv
P1: Rd X | Miss | Rd-req to Dir. Dir responds. | X: S: 1 | S | Inv | Inv | Inv
P2: Rd X | Miss | Rd-req to Dir. Dir responds. | X: S: 1, 2 | S | S | Inv | Inv
P2: Wr X | Perms Miss | Upgr-req to Dir. Dir sends INV to P1. P1 sends ACK to Dir. Dir grants perms to P2. | X: M: 2 | Inv | M | Inv | Inv
P3: Wr X | Write Miss | Wr-req to Dir. Dir fwds request to P2. P2 sends data to Dir. Dir sends data to P3. | X: M: 3 | Inv | Inv | M | Inv
P3: Rd X | Read Hit | - | - | Inv | Inv | M | Inv
P4: Rd X | Read Miss | Rd-req to Dir. Dir fwds request to P3. P3 sends data to Dir. Memory wrtbk. Dir sends data to P4. | X: S: 3, 4 | Inv | Inv | S | S

## Slide 3
Cache Block States
What are the different states a block of memory can have
within the directory?
Note that we need information for each cache so that
invalidate messages can be sent
The block state is also stored in the cache for efficiency
The directory now serves as the arbitrator: if multiple
write attempts happen simultaneously, the directory
determines the ordering

## Slide 4
Performance Improvements
What determines performance on a multiprocessor:
  What fraction of the program is parallelizable?
  How does memory hierarchy performance change?
New form of cache miss: coherence miss – such a miss
would not have happened if another processor did not
write to the same cache line
False coherence miss: the second processor writes to a
different word in the same cache line – this miss would
not have happened if the line size equaled one word

## Slide 5
Shared-Memory Vs. Message-Passing
Shared-memory:
Well-understood programming model
Communication is implicit and hardware handles protection
Hardware-controlled caching
Message-passing:
No cache coherence  simpler hardware
Explicit communication  easier for the programmer to
restructure code
Sender can initiate data transfer

## Slide 6
Ocean Kernel
Procedure Solve(A)
begin
diff = done = 0;
while (!done) do
diff = 0;
for i  1 to n do
for j  1 to n do
temp = A[i,j];
A[i,j]  0.2 * (A[i,j] + neighbors);
diff += abs(A[i,j] – temp);
end for
end for
if (diff < TOL) then done = 1;
end while
end procedure

## Slide 7
Shared Address Space Model
int n, nprocs;
float **A, diff;
LOCKDEC(diff_lock);
BARDEC(bar1);
main()
begin
read(n); read(nprocs);
A  G_MALLOC();
initialize (A);
CREATE (nprocs,Solve,A);
WAIT_FOR_END (nprocs);
end main
procedure Solve(A)
int i, j, pid, done=0;
float temp, mydiff=0;
int mymin = 1 + (pid * n/procs);
int mymax = mymin + n/nprocs -1;
while (!done) do
mydiff = diff = 0;
BARRIER(bar1,nprocs);
for i  mymin to mymax
for j  1 to n do
…
endfor
endfor
LOCK(diff_lock);
diff += mydiff;
UNLOCK(diff_lock);
BARRIER (bar1, nprocs);
if (diff < TOL) then done = 1;
BARRIER (bar1, nprocs);
endwhile

## Slide 8
Message Passing Model
main()
read(n); read(nprocs);
CREATE (nprocs-1, Solve);
Solve();
WAIT_FOR_END (nprocs-1);
procedure Solve()
int i, j, pid, nn = n/nprocs, done=0;
float temp, tempdiff, mydiff = 0;
myA  malloc(…)
initialize(myA);
while (!done) do
mydiff = 0;
if (pid != 0)
SEND(&myA[1,0], n, pid-1, ROW);
if (pid != nprocs-1)
SEND(&myA[nn,0], n, pid+1, ROW);
if (pid != 0)
RECEIVE(&myA[0,0], n, pid-1, ROW);
if (pid != nprocs-1)
RECEIVE(&myA[nn+1,0], n, pid+1, ROW);
for i  1 to nn do
for j  1 to n do
…
endfor
endfor
if (pid != 0)
SEND(mydiff, 1, 0, DIFF);
RECEIVE(done, 1, 0, DONE);
else
for i  1 to nprocs-1 do
RECEIVE(tempdiff, 1, *, DIFF);
mydiff += tempdiff;
endfor
if (mydiff < TOL) done = 1;
for i  1 to nprocs-1 do
SEND(done, 1, I, DONE);
endfor
endif
endwhile

## Slide 9
Constructing Locks
Applications have phases (consisting of many instructions)
that must be executed atomically, without other parallel
processes modifying the data
A lock surrounding the data/code ensures that only one
program can be in a critical section at a time
The hardware must provide some basic primitives that
allow us to construct locks with different properties
Lock algorithms assume an underlying cache coherence
mechanism – when a process updates a lock, other
processes will eventually see the update

## Slide 10
Synchronization
The simplest hardware primitive that greatly facilitates
synchronization implementations (locks, barriers, etc.)
is an atomic read-modify-write
Atomic exchange: swap contents of register and memory
Special case of atomic exchange: test & set: transfer
memory location into register and write 1 into memory
lock: t&s register, location
bnz register, lock
CS
st location, #0

## Slide 11
Caching Locks
Spin lock: to acquire a lock, a process may enter an infinite
loop that keeps attempting a read-modify till it succeeds
If the lock is in memory, there is heavy bus traffic  other
processes make little forward progress
Locks can be cached:
  cache coherence ensures that a lock update is seen
  by other processors
  the process that acquires the lock in exclusive state
  gets to update the lock first
  spin on a local copy – the external bus sees little traffic

## Slide 12
Coherence Traffic for a Lock
If every process spins on an exchange, every exchange
instruction will attempt a write  many invalidates and
the locked value keeps changing ownership
Hence, each process keeps reading the lock value – a read
does not generate coherence traffic and every process
spins on its locally cached copy
When the lock owner releases the lock by writing a 0, other
copies are invalidated, each spinning process generates a
read miss, acquires a new copy, sees the 0, attempts an
exchange (requires acquiring the block in exclusive state so
the write can happen), first process to acquire the block in
exclusive state acquires the lock, others keep spinning

## Slide 13
Test-and-Test-and-Set
lock: test register, location
bnz register, lock
t&s register, location
bnz register, lock
CS
st location, #0

## Slide 14
Load-Linked and Store Conditional
LL-SC is an implementation of atomic read-modify-write
with very high flexibility
LL: read a value and update a table indicating you have
read this address, then perform any amount of computation
SC: attempt to store a result into the same memory location,
the store will succeed only if the table indicates that no
other process attempted a store since the local LL (success
only if the operation was “effectively” atomic)
SC implementations do not generate bus traffic if the
SC fails – hence, more efficient than test&test&set

## Slide 15
Spin Lock with Low Coherence Traffic
lockit: LL R2, 0(R1) ; load linked, generates no coherence traffic
BNEZ R2, lockit ; not available, keep spinning
DADDUI R2, R0, #1 ; put value 1 in R2
SC R2, 0(R1) ; store-conditional succeeds if no one
; updated the lock since the last LL
BEQZ R2, lockit ; confirm that SC succeeded, else keep trying
If there are i processes waiting for the lock, how many
bus transactions happen?

## Slide 16
Spin Lock with Low Coherence Traffic
lockit: LL R2, 0(R1) ; load linked, generates no coherence traffic
BNEZ R2, lockit ; not available, keep spinning
DADDUI R2, R0, #1 ; put value 1 in R2
SC R2, 0(R1) ; store-conditional succeeds if no one
; updated the lock since the last LL
BEQZ R2, lockit ; confirm that SC succeeded, else keep trying
If there are i processes waiting for the lock, how many
bus transactions happen?
1 write by the releaser + i (or 1) read-miss requests +
i (or 1) responses + 1 write by acquirer + 0 (i-1 failed SCs) +
i-1 (or 1) read-miss requests + i-1 (or 1) responses
(The i/i-1 read misses and responses can be reduced to 1)

## Slide 17
Further Reducing Bandwidth Needs
Ticket lock: every arriving process atomically picks up a
ticket and increments the ticket counter (with an LL-SC),
the process then keeps checking the now-serving
variable to see if its turn has arrived, after finishing its
turn it increments the now-serving variable
Array-Based lock: instead of using a “now-serving”
variable, use a “now-serving” array and each process
waits on a different variable – fair, low latency, low
bandwidth, high scalability, but higher storage
Queueing locks: the directory controller keeps track of
the order in which requests arrived – when the lock is
available, it is passed to the next in line (only one process
sees the invalidate and update)

## Slide 18
Lock Vs. Optimistic Concurrency
lockit: LL R2, 0(R1)
BNEZ R2, lockit
DADDUI R2, R0, #1
SC R2, 0(R1)
BEQZ R2, lockit
Critical Section
ST 0(R1), #0
tryagain: LL R2, 0(R1)
DADDUI R2, R2, R3
SC R2, 0(R1)
BEQZ R2, tryagain
LL-SC is being used to figure out
if we were able to acquire the lock
without anyone interfering – we
then enter the critical section
If the critical section only involves
one memory location, the critical
section can be captured within the
LL-SC – instead of spinning on the
lock acquire, you may now be spinning
trying to atomically execute the CS

## Slide 19
Barriers
Barriers are synchronization primitives that ensure that
some processes do not outrun others – if a process
reaches a barrier, it has to wait until every process
reaches the barrier
When a process reaches a barrier, it acquires a lock and
increments a counter that tracks the number of processes
that have reached the barrier – it then spins on a value that
gets set by the last arriving process
Must also make sure that every process leaves the
spinning state before one of the processes reaches the
next barrier

## Slide 20
Barrier Implementation
LOCK(bar.lock);
if (bar.counter == 0)
bar.flag = 0;
mycount = bar.counter++;
UNLOCK(bar.lock);
if (mycount == p) {
bar.counter = 0;
bar.flag = 1;
}
else
while (bar.flag == 0) { };

## Slide 21
Sense-Reversing Barrier Implementation
local_sense = !(local_sense);
LOCK(bar.lock);
mycount = bar.counter++;
UNLOCK(bar.lock);
if (mycount == p) {
bar.counter = 0;
bar.flag = local_sense;
}
else {
while (bar.flag != local_sense) { };
}