## Slide 1
Lecture: Deep Compression
Topics: pruning, quantization, coding of weights to reduce memory requirements, EIE accelerator
Project ideas on google doc

## Slide 2
Deep Compression
Growing network sizes:
LeNet-5 (1M parameters), Krizhevsky (60M), DeepFace (120M),
AlexNet (60M), VGG-16 (130M), Coates (10B)
Hence, reduce the total storage requirement:
Can fit in cache; eliminates/reduces the memory bottleneck
Results in a small executable (useful for mobile apps)
Reduces the power for inference (esp. useful for mobile)

## Slide 3
Power/Energy Argument
Running a billion parameter network at 20 frames/sec
would consume power = 20 x 1G x 640 = 12.8 W
Would also need a well-provisioned memory system

## Slide 4
Pruning
Remove the weights that are close to zero
Re-train to refine the weights
Walsh, Nature 2013.

## Slide 5
Visualizing the Weights
First FC layer of LeNet-300-100 (MNIST)

## Slide 6
Impact on Accuracy

## Slide 7
Other Notes
Early layers are more sensitive to pruning (need lower
thresholds)
Can prune/re-train one layer at a time (fixing other weights)

## Slide 8
Managing Sparsity

## Slide 9
Quantization and Huffman Encoding

## Slide 10
Quantization and Re-Training

## Slide 11
Centroid Initialization
Linear emerges as the best.

## Slide 12
Outlier Aware Quantization ISCA’18
Use 4-bit precision for small weights and higher precision for large weights (< 3%).

## Slide 13
Huffman Codes
Example for text
Space 7 111
A 4 010
E 4 000
F 3 1101
H 2 1010
I 2 1000
M 2 0111
N 2 0010
S 2 1011
T 2 0110
L 1 11001
O 1 00110
P 1 10011
Can use Huffman codes to reduce the storage needs of the weights and the indices

## Slide 14
Motivation for Huffman Encoding

## Slide 15
Results Summary

## Slide 16
Compression Stats
Note: Weights/indices end up having similar capacities.

## Slide 17
Accuracy Impact

## Slide 18
Impact of Pruning on Performance/Energy
Note: no quantization/coding, no batching.

## Slide 19
Batching
Batching may not be practical for latency-sensitive apps
Batching leads to higher compute-to-memory ratio
CuSparse library overheads are significant; pruning hurts

## Slide 20
Accelerator Motivation
Existing hardware/libraries have little support for managing
sparsity and indirect look-ups
Natural to integrate deep compression into ML accelerators
Also, neuron values exhibit high levels of sparsity
 the EIE accelerator
(Efficient Inference Engine)

## Slide 21
An NFU Operation
DaDianNao operation
Becomes…
EIE operation
Need to:
Identify non-zero activations (Y) and non-zero weights (Xi)
Calculate the weight indices (while looking up the code-book)
Look up the code-book for the weights
Manage load imbalance

## Slide 22
NFU Operation Data Structures
All weights handled by green PE
Weights skipped in that column
Start of each column

## Slide 23
EIE Details
Each PE handles a subset of neurons (data layout determines
broadcast vs. reduction)
Non-zero activations are broadcast along with their id
Based on that id, the column pointer array (32KB SRAM) is accessed
Accordingly, the weight and displacement are accessed – Sparse Matrix
Unit that stores 4-bits for weight and 4-bits for displacement look-ups –
this is an SRAM array that is 64 bits wide (locality) and 128KB in size
One codebook look-up required (Quantization, but no Huffman Encoding)
Each multiplication operation is added to the partial sum for that neuron
(stored in a 64-entry destination activation register, spills into a 2KB
activation SRAM, batching to reduce SRAM reads/writes)
Activation queue in each PE that helps deal with sporadic load imbalance
Central Control Unit receives leading non-zero activations from PEs and
broadcasts them

## Slide 24
EIE Details
4 1.15ns stages to update one activation: codebook look-up and address
accumulation; output activation read and input activation multiply; shift
and add; output activation write
16-entry queue yields ~90% efficiency
Each PE is 9mW and 0.6 mm2 ; SRAMs account for 59% power and 93% area
64 PEs at 800 MHz  102 GOP/s (mult and add)
With 10x weight sparsity and 3x activation sparsity, amounts to 3 TOP/s
About 1-2 orders of magnitude faster than competing CPUs and GPUs
DDN specs for rough comparison:
Throughput = 16 x 500 x 800 MHz = 6.4 TOP/s
Power = 16 W (@ 600 MHz)
Area = 68 mm2 (38.4 mm2 for EIE)
Storage = 36 MB eDRAM (8MB SRAM for EIE) (EIE needs fewer chips)

## Slide 25
EIE Take-Home
EIE better for mobile (fewer chips, lower energy)
DDN better for datacenter (higher throughput, SIMD)
Prior comparison was with peak throughput; note that
zero-weights are more prevalent in FC layers, not in
CONV layers; so, EIE energy benefit may not be that high
Worth pondering a hybrid arch that does DDN in CONV
layers (for high thruput) and EIE in FC layers (for low
energy)

## Slide 26
References
“Learning both Weights and Connections for Efficient Neural Network”,
S. Han et al., Proceedings of NIPS, 2015
“Deep Compression: Compressing Deep Neural Networks with Pruning,
Trained Quantization and Huffman Coding”, S. Han et al., ICLR, 2016
“EIE: Efficient Inference Engine on Compressed Deep Neural Network”,
S. Han et al., Proceedings of ISCA, 2016
“Deep Compression and EIE”, S. Han, talk at GPU Tech Conf, 2016