## Slide 1
Lecture: Deep Compression Accelerators
Topics: EIE accelerator, Cnvlutin, SCNN
Project ideas on google doc

## Slide 2
NFU Operation Data Structures
All weights handled by green PE
Weights skipped in that column
Start of each column

## Slide 3
EIE Details
Each PE handles a subset of neurons (data layout determines
broadcast vs. reduction)
Non-zero activations are broadcast along with their id
Based on that id, the column pointer array (32KB SRAM) is accessed
Accordingly, the weight and displacement are accessed – Sparse Matrix
Unit that stores 4-bits for weight and 4-bits for displacement look-ups –
this is an SRAM array that is 64 bits wide (locality) and 128KB in size
One codebook look-up required (Quantization, but no Huffman Encoding)
Each multiplication operation is added to the partial sum for that neuron
(stored in a 64-entry destination activation register, spills into a 2KB
activation SRAM, batching to reduce SRAM reads/writes)
Activation queue in each PE that helps deal with sporadic load imbalance
Central Control Unit receives leading non-zero activations from PEs and
broadcasts them

## Slide 4
EIE Details
4 1.15ns stages to update one activation: codebook look-up and address
accumulation; output activation read and input activation multiply; shift
and add; output activation write
16-entry queue yields ~90% efficiency
Each PE is 9mW and 0.6 mm2 ; SRAMs account for 59% power and 93% area
64 PEs at 800 MHz  102 GOP/s (mult and add)
With 10x weight sparsity and 3x activation sparsity, amounts to 3 TOP/s
About 1-2 orders of magnitude faster than competing CPUs and GPUs
DDN specs for rough comparison:
Throughput = 16 x 500 x 800 MHz = 6.4 TOP/s
Power = 16 W (@ 600 MHz)
Area = 68 mm2 (38.4 mm2 for EIE)
Storage = 36 MB eDRAM (8MB SRAM for EIE) (EIE needs fewer chips)

## Slide 5
EIE Take-Home
EIE better for mobile (fewer chips, lower energy)
DDN better for datacenter (higher throughput, SIMD)
Prior comparison was with peak throughput; note that
zero-weights are more prevalent in FC layers, not in
CONV layers; so, EIE energy benefit may not be that high
Worth pondering a hybrid arch that does DDN in CONV
layers (for high thruput) and EIE in FC layers (for low
energy)

## Slide 6
Cnvlutin
Only targets sparsity in activations

## Slide 7
Baseline Example

## Slide 8
Cnvlutin Example

## Slide 9
Cnvlutin Results
Inputs are organized as bricks of 16 entries, requiring a 4-bit offset
(25% overhead or 1MB) (4.5% area overhead for the entire chip)
7% lower power than the baseline (lower activity to read SB)
Speedup: 1.37x (1.52x if we can prune neurons sufficiently close to zero)

## Slide 10
Summary
Relatively easy to eliminate zero neurons from a
data-parallel accelerator (Cnvlutin) – relatively small
speedups
Some data-parallelism is lost when eliminating zero
synapses (EIE); but the benefit of dealing with lower
synaptic storage is worth it (the workload fits on a chip)

## Slide 11
SCNN
First work to target sparsity in activations and weights
(Cambricon-X and EIE do sparse weights; Cnvlutin and Eyeriss do sparse activations)

## Slide 12
Loop Nesting
Short-hand:
Do all images
Do all output feature maps
Do all input feature maps
Do all horizontal pixels in output fmap
Do all vertical pixels in output fmap
Do all horizontal pixels in kernel
Do all vertical pixels in kernel

## Slide 13
SCNN Approach
For any architecture, must find the right way to order
these loops and distribute the loops across PEs, such
that reuse is maximized and data movement is minimized
After experimentation, they pick a nesting/dataflow that
is best for exploiting sparsity
(They assume N=1, which may be questionable)
They observe that convs are bigger bottlenecks than FC;
they observe that feature map data movement is the
biggest bottleneck; hence input-stationary
(actually, a combo of input-stationary and row-stationary)

## Slide 14
SCNN Dataflow
Each PE has a matrix of multipliers
This matrix is fed with I inputs and F filter weights
The matrix performs a Cartesian Product – every I is
multiplied with every F
These results are then fed to an array of adders that
keep aggregating partial sums – need a router and an
index generator to make sure each product is sent to
the right adder (multiple pixels may be buffered at adder)
The input stays and a new vector of weights is provided
Once an output feature map entry is computed, it is
written to the output buffer
Then they bring in the next set of input feature map values
Lots of PEs; each handles part of the input feature map;
aggregation required for boundary elements (halos)

## Slide 15
PE Design

## Slide 16
Managing Sparsity
The PE is fed with dense vectors (I and F); each element
also has an index; when multiplications are performed, the
index is also calculated
The product is sent to the appropriate adder (buffered in
case of conflicts); the array vector is twice as large to
reduce conflicts (4x4 mult and 32 adders)
FC layer can only use 4 of the mults in the PE
Overheads: index generation, routed network, more
scatter accumulators

## Slide 17
Chip Details
1 GHz, 2 TOps/s

## Slide 18
Results
About 2.5x speedup
Some inefficiency
because PEs are
underutilized and
because of load
imbalance
Turns out that
DCNN-opt is very
effective at
reducing energy
(DRAM activ. comp
and power-gating
for zero-mults)

## Slide 19
References
“Learning both Weights and Connections for Efficient Neural Network”,
S. Han et al., Proceedings of NIPS, 2015
“Deep Compression: Compressing Deep Neural Networks with Pruning,
Trained Quantization and Huffman Coding”, S. Han et al., ICLR, 2016
“EIE: Efficient Inference Engine on Compressed Deep Neural Network”,
S. Han et al., Proceedings of ISCA, 2016
“Deep Compression and EIE”, S. Han, talk at GPU Tech Conf, 2016
“Cnvlutin: Ineffectual-Neuron-Free Deep Neural Network Computing”,
J. Albericio et al., Proceedings of ISCA, 2016
“SCNN: An Accelerator for Compressed-Sparse Convolutional
Neural Networks,” A. Parashar et al., ISCA 2017