## Slide 1
Lecture: Analog Accelerator
Topics: memristor basics, ISAAC accelerator

## Slide 2
Analog Acceleration
Many electronic phenomena correspond to
multiplication and addition
Analog phenomena are also noisy; perhaps, this is not
an issue when dealing with neural networks

## Slide 3
Wires as ALUs
G1
I1 =V1.G1
V1
G2
I2 =V2.G2
V2
I = I1 + I2 =
V1.G1 + V2.G2

## Slide 4
Crossbar for Vector-Matrix Multiplication
DAC
S&H
S&H
S&H
S&H
DAC
DAC
DAC
ADC

## Slide 5
Physical View
Wordline
Bitline
Memristor cell
Driver circuits in silicon substrate
Physical view of a memristor crossbar array

## Slide 6
Challenge
High ADC/DAC area/energy
  You could stay in analog forever, but then you’d need expensive analog buffering and you’d introduce significant noise that accumulates across network layers
Unfortunately, some ADC overheads increase
exponentially with resolution
Resolution increases with computational density

## Slide 7
1. Input One Bit at a Time
Need a trivial DAC
Must perform multiplication over 16 iterations
Results are aggregated with shift-and-adds

## Slide 8
2. Spread the Weights
A single weight is spread across 8 2-bit cells in a row
The outputs of 8 columns have to be shifted and added
Low bits per cell is good for precision and for ADC efficiency

## Slide 9
3. Few Rows Per Crossbar
Requires us to use many small crossbars
A neuron with many inputs is spread across multiple xbars
Must aggregate partial sums from many xbars

## Slide 10
4. Weight Encoding
If the weights are large, store their “complements”
Reduces ADC resolution by 1 bit
Inputs are provided in 2’s complement form
  The MSb represents -215 -- need a shift-and-subtract
  Irrelevant if we are using ReLU
Weights are stored with a bias: a bias of 215 allows
unsigned integers to represent weights between
-215 and 215 - 1

## Slide 11
Analog Accelerator Challenge
High ADC/DAC area/energy
1-bit input at a time (small v)
2-bit cells (small w)
Few rows per array (small R)
Encoding tricks to produce small numbers
Spread the computation across a single xbar, across
multiple xbars, and across time to reduce ADC size

## Slide 12
ISAAC Architecture

## Slide 13
ISAAC Pipeline
B
B
B
B
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
(a) Example of different layers in action at the same time
Cyc 1 2 3 4 … 17 18 19 20 21 22
eDRAM
Rd + IR
Xbar
1
Xbar
2
Xbar
3
Xbar
16
ADC
S+A
OR wr
S+A
OR wr
s
eDRAM
Wr
…
Tile IMA IMA IMA IMA IMA IMA Tile Tile Tile
(b) Example of one operation in layer i flowing through its pipeline

## Slide 14
Pipeline Variants
Most digital accelerators use “temporal pipelines” – all
units work on 1 layer, then all work on the next layer, etc.
  Good for low latency and cache locality
  A spatial pipeline would give nearly the same throughput, but
  higher latency per inference
Analog accelerators use “spatial pipelines” – parts of the
chip are hard-coded to execute specific layers
  Required by design since weight updates are slow
  Latency impact is small (no batching required and for the most
  part, all layers work on the same image)

## Slide 15
Replication in Early Layers

## Slide 16
The ISAAC Pipeline
Pipelining within an IMA/tile/layer
Pipelining across layers
Network is mapped to avoid hazards; balanced replication
where possible to avoid storage/compute under-utilization
Design space exploration to identify the best use of chip
real estate

## Slide 17
Power/Area Breakdowns

## Slide 18
Power/Area Breakdowns

## Slide 19
Design Space Exploration

## Slide 20
Comparison to DaDianNao
7.5X higher computational density
14.8X higher throughput on CNN benchmarks
5.5X lower energy
The chip has a 3X higher power density

## Slide 21
Throughput on CNNs

## Slide 22
Other Analog Innovations
AN codes for reliability (Feinberg et al., HPCA’18)
Crossbars applied to scientific computing (Feinberg et al.,
ISCA’18)
More efficient ADCs (e.g., PipeLayer, HPCA’17)
Memristor-aided logic (Kvatinsky et al., IEEE Trans. On
Circuits and Systems, 2014) – activate two rows and
ground a third row to perform a NOR operation within the
crossbar

## Slide 23
References
“ISAAC: A Convolutional Neural Network Accelerator with In-Situ
Analog Arithmetic in Crossbars”, A. Shafiee et al., Proceedings of
ISCA, 2016