## Slide 1
Lecture: Spiking Networks Architecture
Topics: TrueNorth design, projects discussion

## Slide 2
The Spiking Approach
Low energy for computation: only adds, no multiplies
Low energy for communication: depends on spikes per signal
Neurons have state, inputs arrive asynchronously, info
in relative timing of spikes, other biological phenomena, …

## Slide 3
IBM TrueNorth
Product of DARPA’s SyNAPSE project
Largest chip made by IBM (5.4 billion transistors)
Based on LLIF neuron model
Lots of on-going projects that use TrueNorth to execute
new apps
Lots of limitations as well – all done purposely to reduce
area/power/complexity

## Slide 4
TrueNorth Core

## Slide 5
TrueNorth Core (Axonal Approach)

## Slide 6
TrueNorth Core (Dendritic Approach)
TrueNorth is designed for very low power per spike. They compress the weights with quantization and axon type sharing. In addition, they use a mix of asynchronous and synchronous circuits. Asynchronous circuits rely on handshakes to “wake up” and perform work when there is an input. They sit idle and do not burn power when there is no work (can also be achieved with clock gating in synchronous circuits). They also use ultra high VT transistors to reduce leakage (this hurts cycle time, but they’re not trying to be super fast anyway). In the figure on the left, we can see the main components. The Router, Scheduler and Token Controller are primarily asynchronous circuits. The Neuron block is synchronous, but dissipates power only when it receives instructions from the Token Controller.
When spikes are received, they are placed in a queue in the Scheduler. An incoming spike may be processed in the next “tick” (a tick is typically 1ms), or in one of the next 16 ticks. So the queue is broken into 16 pieces. Each piece has a bit for one of the 256 axons (rows) in that core. So the incoming spike queue is a 256x16 bit vector. In addition, the scheduler keeps track of the 2-bit type (Str Exc, Exc, Inh, Str Inh) for each axon.

## Slide 7
TrueNorth Core (Dendritic Approach)
In every tick, the Scheduler sends the list of incoming spikes for that tick to the Token Controller (along with the axon types). At the Token Controller, these spikes are processed using a Dendritic Approach. That is, we are going to sequentially walk through every neuron and process all the dendrites (inputs) for that neuron. So the Token Controller first reads all the info for Neuron-1 from the Core SRAM. This is a 410-bit field that stores the 256 1-bit connections for that neuron, its 4 weights, threshold, leak, current potential, stochastic parameters, where the output of this neuron should be sent, etc. The 256 1-bit connections are ANDed with the incoming spike vector to see if this neuron has any input spikes. If it does, the token controller picks out the correct weight and packs off an instruction to the neuron block with all the pertinent arguments. The neuron block does its math. Once the token controller has dealt with all input spikes for that neuron, it sends off a final leak instruction. The leak is added to the potential, a threshold is applied, the generated spike is sent to the router, and the final potential is written back into the Core SRAM. The Token Controller then moves on to the next neuron.

## Slide 8
TrueNorth Core (Dendritic Approach)
This Dendritic approach is more deterministic and leads to fewer SRAM accesses than an Axonic approach. In an Axonic approach, we’d walk through each input axon and increment the potentials of the neurons connected to that axon. This would require us to potentially read a neuron’s data structures multiple times. The first prototype of TrueNorth did use the Axonic approach and they realized that the Dendritic approach was more elegant (even if it requires us to painfully walk through all 256 neurons just to process a very sparse incoming spike train).
TrueNorth has an under-provisioned network, especially when spikes have to be sent off-chip to other TrueNorth chips. If the spike density is high, it’s possible that the spikes won’t be delivered within the next tick. If this is evident during software simulations of the application, TrueNorth is programmed so that all spikes generated by a neuron layer are processed by the next layer (say) 4 ticks later. This is essentially giving all the spikes 4 ticks to traverse the network and reach their destinations.
The subsequent slides have a few more details on TrueNorth.

## Slide 9
Principles
Focus on low power (speed is secondary)
Low power with asynchronous circuits
Low power with high-Vt circuits and SOI process
A dendritic approach leads to fewer SRAM reads/updates
and is more deterministic
Also uses an under-provisioned network (giving rise to
the concept of “future” ticks)

## Slide 10
Receiving Spikes
Spikes arrive at the Scheduler; stored in a 256x16 SRAM
grid to indicate axon and time of the spike
The Token Controller receives spikes in a “tick” (and their
types – exc/inh); it then sequentially walks through 256
neurons – this dendritic approach makes the latency and
SRAM accesses more deterministic
It reads a 410-bit word from SRAM for that neuron (this
word has connectivity info used by Token Controller and
neuron parameters used by Neuron block
Based on connectivity and input spikes, instructions are
sent to Neuron block

## Slide 11
Neuron Block
Neuron computations are performed here (these are
non-trivial because of stochastic behaviors – more later)
A leak is introduced every tick for every neuron
After thresholding, a spike may be triggered
The neuron block uses synchronous circuits, but it is
active only when it receives instructions from the Token
Controller; the Token Controller, Scheduler, and network
Router are all asynchronous to exploit the low power
inherent in spike sparsity

## Slide 12
More Details
The 410 bit word: 256 synaptic connections, 4 9-bit weights,
9-bit leak, 8-bit threshold, 26-bit destination axon, 4-bit
delivery time, 9-bit potential, … (62 more bits)
The network may occasionally not handle a burst of spikes;
if this is likely, then spikes must have a future delivery time;
allows a spike to take multiple ticks to reach its destination
256x256 core; 4K cores; million neurons; 430 mm2;
65 mW on average; 28nm Samsung process; 1ms tick

## Slide 13
Limitations
A neuron can only have 256 inputs (no provision for partial
sums)
A neuron can only have one destination axon output of a
specific type (seen by 256 neurons)
Weight quantization (4 weights per neuron)
TrueNorth does impose some limitations on the network. We’ve already seen the weight quantization restriction before. In addition, a neuron output can be only sent to one other axon anywhere in the TrueNorth network (and this axon has to be one of four types). This axon can be seen by 256 neurons, so this is a non-trivial fan-out, but may not be enough for some really large networks. If we do want a neuron to excite some neurons and inhibit others, we’d have to replicate the neuron and feed it to two different axons in the next layer (where one axon is excitatory and one is inhibitory). Finally, a neuron can only have 256 inputs. It is not possible to aggregate the partial sums from multiple neurons because each neuron applies its own thresholding and can only produce binary spikes as output.

## Slide 14
Measurement Data
Because of the synch/asynch approach, the chip works
correctly even at 0.7V supply voltage (low power!); 0.7-1.05V
42 mW at 0.7V, 0 Hz firing rate, 0 synapses/neuron
323 mW at 1.05V, 200 Hz firing rate, 256 synapses/neuron
At 0.75 V, the max throughput (giga synaptic ops per second)
is 58 GSOP/s, the energy efficiency is 400 GSOP/sW
At 0.75 V, complex recurrent network, 20 Hz avg firing rate,
128 syn/neuron, 65 mW and 46 GSOP/sW
At low activity levels, the ticks can be sped up to 21 KHz

## Slide 15
More Results
We see that the chip is dissipating roughly 65mW in leakage and memory nearly all the time. In addition, depending on the spike rate, we see the computation/communication energy rise linearly. On the previous slide, we see that the super-large TrueNorth chip only has a max throughput of ~60 giga-synaptic ops per second. This is 100 times lower than DaDianNao (that uses maybe 1/10th of the transistors used by TrueNorth). That’s a pretty unfortunate result. But it’s not shocking. TrueNorth has been designed for low energy and it doesn’t have any SIMD-ness… it sequentially walks through updates to every neuron (yes, there is parallelism across the 4K cores). It also has limited wiring.

## Slide 16
Improvements
4K chips on a rack
 4 B neurons, 300 W
for TN chips, plus more for
communication/FPGAs
-- 4 KWs (SC’14)
96 racks  412 B neurons,
1014 synapses (human
brain scale), 29 kW for
TN chips, few hundred kW
overall
Power and time, relative to
the Compass simulator,
running on the BG/Q
supercomputer and a dual-
socket Intel system
TrueNorth looks great, relative to an Intel processor and a supercomputer running a brain simulation. But as discussed on the previous slide, it doesn’t compare favorably to DaDianNao and possibly to a GPU as well.

## Slide 17
Stochastic Neurons
We’ve discussed the basic microarchitecture of TrueNorth. We described the Neuron Core as simply doing the operations for LLIF. Actually, TrueNorth’s neuron model has several other bells and whistles that allow it to emulate many biological neurons. These are all achieved with modest additions to the hardware. These additional features include stochasticity in the input, state, and output. They also include different modes for leak, threshold, and reset. They construct a library of 50+ neuron behaviors that they believe will be useful to application developers. They also demonstrate how the TrueNorth core can be configured to model all 20 Izhikevich neurons (biologically observed neurons) with at most 3 TrueNorth neurons (most just need 1 neuron).

## Slide 18
Stochastic Neurons
The TrueNorth neurons have many stochastic parameters
Helps emulate many biological and non-linear behaviors
Continues to be low cost; applies the RISC argument
Stochasticity in input, state, and output
Different modes for leak, threshold, reset
Helps create a library of 50+ neuron models, including
the 20 defined by Izhikevich (using 1-3 neurons)

## Slide 19
Neuron Parameters
9 bits
256 bits
36 bits
4 bits
1 bit
9 bits
1 bit
8 bits
8 bits
8 bits
9 bits
1 bit
2 bits
8 bits
The cheat sheet for how to configure a TrueNorth neuron. These parameters are stored in the 410-bit field for every neuron.

## Slide 20
Synaptic and Leak Probabilities
If the input is stochastic, the potential change is either
-1, 0, or +1. The probability of the incr/decr is determined
by the synaptic weight (compare the uniformly distributed
pseudorandom number PRN to the |weight|). The
incr/decr is determined by the sign of the weight.
Same for leak
Have to draw many random numbers for each neuron:
threshold, leak, each connected input axon
The potential increments can be done stochastically. For example, in non-stochastic mode, if the weight is 85, every incoming spike will raise the potential by 85. In stochastic mode, if the weight is 85, a pseudorandom number is drawn. If the number is less than 85, then the potential is incremented by 1. So the weight now represents the probability of the potential moving up (exc) or down (inh) by 1. The leak can also be stochastic, using the exact same approach. As a neuron is being processed in a tick, we end up accessing the pseudorandom generator several times.

## Slide 21
Leak Modes
Standard leak operation: constant incr/decr of leak
Leak-Reversal mode: the leak sign flips when the neuron potential flips
No leak at zero potential
Creates a convergent leak and a divergent leak
There are four leak modes. In the first two, the leak value does not change over time – if the leak is positive, it forces the potential to rise constantly (fig 1) – if the leak is negative, it forces the potential to drop constantly (fig 2).

## Slide 22
Leak Modes
Standard leak operation: constant incr/decr of leak
Leak-Reversal mode: the leak sign flips when the neuron potential flips
No leak at zero potential
Creates a convergent leak and a divergent leak
The fourth leak mode is what we had described before. The leak is moving the potential towards the zero resting potential (convergent leak). So the leak is negative when the potential is positive, and positive when the potential is negative.

## Slide 23
Leak Modes
Standard leak operation: constant incr/decr of leak
Leak-Reversal mode: the leak sign flips when the neuron potential flips
No leak at zero potential
Creates a convergent leak and a divergent leak
The third leak mode is divergent, i.e., it moves the potential away from the resting potential. So the leak is positive when the potential is positive, and negative when the potential is negative. The third and fourth modes also have zero leak when the potential is zero.

## Slide 24
Negative Threshold
Crossing the positive threshold always produces a spike
There’s also a negative threshold that does not produce a spike
The negative threshold may either act as a floor, or as a “bounce”
to the negative reset voltage
The bounce allows us to create a neuron ON-OFF pair; they mirror
each other
In addition to the typical positive threshold for spikes, they also have a negative threshold. When this is reached, you can either stay at that floor, or you can bounce to the negative reset voltage. The latter option allows you to mirror a typical neuron without producing a spike. This is useful in creating a neuron ON-OFF pair, where one neuron produces a spike when it sees a strong stimulus and the other spikes when it sees the opposite stimulus.

## Slide 25
Stochastic Threshold and Reset
Can grow the threshold by a random number
Can set the max of this delta with a mask parameter
Three reset modes:
  Normal: after firing, the new potential = reset voltage
  (residual is discarded)
  Linear: after firing, the new potential = residual voltage
  (reset voltage is not used)
  Non-reset mode: no reset. Relies on leak and –ve synapses to
  lower the potential
A commonly used feature is the stochastic threshold, i.e., the threshold can be increased by a random number. The user can define the max increase.
They also have three different reset modes, described above.
All of these modes described in the previous slides give the TrueNorth neuron incredible flexibility.

## Slide 26
Synthetic Functions
Library of 50+ synthetic neuron behaviors (compatible with many
coding techniques)
Example: various arithmetic ops, rate store neuron
Rate store neuron: acts as a memory that is constantly being read (e.g.,
a state holding recurrent neuron); output freq a potential;
uses a stochastic threshold and non-reset mode;
The next slide shows how we can emulate various arithmetic ops. Here is an example of a neuron that is used to remember state. Depending on the value of that state, the neuron produces a proportionate amount of spikes. The threshold is chosen randomly between 0 and 1. So the neuron produces a spike if its potential happens to be above this random threshold. The higher the potential, the higher the probability of a spike. There is no leak so you can remember your state. Incoming spikes will grow/shrink the potential.

## Slide 27
Arithmetic Ops
This slide shows a number of arithmetic ops. The green and black lines show the input values (y-axis) in each experiment (x-axis) and the blue line shows the output result. The stochastic options can be used to generate the non-linear curves such as the sigmoid.

## Slide 28
Izhikevich Neuron Models
Can also model the 20 Izhikevich neurons. Neuron L is the basic integrator neuron that we typically use for most SNNs. The paper shows how to set up each neuron to produce these output behaviors. The next 2 slides will go through 2 examples.

## Slide 29
Neuron Model
Need 924 gates for neuron computation and 348 for PRNG
This figure shows that there’s a good deal of muxing in the neuron circuit to consider the many modes and the stochasticity.

## Slide 30
TrueNorth Networks
Could use rate coding and STDP/back-prop to implement
networks on TrueNorth (most early TrueNorth papers)
Many hardware constraints; must therefore use either
train-then-constrain or constrain-then-train (the latter is
usually better)
  Only 4 synaptic weights
  A neuron can only receive 256 inputs (narrow receptive field)
  A neuron can only have one destination axon/type (narrow
  projective field, although one can replicate a neuron to fix this)
We’ll next see a few different strategies to run applications on TrueNorth with high accuracy. Recall that TrueNorth imposes several constraints (see summary on next slide). The TrueNorth folks (and others) have generally concluded that it is better to integrate the hardware constraints during training (referred to as constrain-then-train). Most early papers on TrueNorth used rate coding for inputs and STDP for training. Like we’ve pointed out before, rate coding makes a spiking neuron act very much like an artificial neuron. This means that back-prop can also be used effectively to compute weights for an SNN. We’ll soon see how this can be implemented.

## Slide 31
MNIST – NeurIPS’15
Spikes are discrete, but the probability of spiking is a
continuous function learnable through back-prop
Limited connectivity in each layer, but over a few layers,
a neuron can see every input
Inputs are provided in a single tick (spike with a probability
that corresponds to the input value)
With an ensemble of networks, the outputs correspond to
the expected value; accuracy of 99.42% on MNIST
This TrueNorth paper shows how you can apply back-prop in an SNN to get very high accuracy.
Back-prop only works when the activation functions are differentiable. Spikes are a step function, so their differential is either 0 or inf. So to get over this hurdle, they take a network and replicate it 64 times to get an ensemble of networks. Each network is identical, i.e., it has the same set of weights. But they use TrueNorth’s stochastic features, so the output neuron in one network may spike while same neuron in another network may not spike. The output for that neuron is the sum of spikes across the 64 networks – let’s say that that neuron spiked in 50 of the 64 networks. If we tweak the weights a little, that neuron may spike in 51 of the 64 networks. So unlike a single network, where a weight tweak may change the output from 0 to 1 (non-differentiable), in this ensemble, a small weight tweak changes the neuron output from 50 to 51 (differentiable). Back-prop therefore works and after a number of iterations, they determine the network weights.

## Slide 32
Implementing CNNs on TrueNorth
Small kernels: a neuron can only have 256 inputs
Conv layer has to replicate the shared weights
Can’t have more than 256 kernels
They use ternary weights and activations
A single spike (or not) for every pixel in every feature map
We can use TrueNorth with ternary weights (-1, 0, +1). The input image is converted into a number of input feature maps (e.g., one of the feature maps could use +1 for a pixel if its R component is greater than 128). Note that we are not using spike trains; an input is represented by a single binary value (spike or not). Next, we have to deal with the many constraints imposed by TrueNorth. First (see next slide), unlike DaDianNao and ISAAC, TrueNorth is spatially expanded, i.e., every neuron in the network maps directly to a TrueNorth neuron. So while convolutions are designed with weight sharing, every TrueNorth neuron in a convolution has to replicate the same set of weights (lots of wasted space!).

## Slide 33
Results
Most are with 8 TN chips
On relatively simple workloads (typically small input sizes of 32x32), this approach (lots of constraints, ternary weights, binary activations) gives us nearly state-of-the-art accuracy.

## Slide 34
References
“Cognitive Computing Building Block”, A. Cassidy et al., IJCNN’13
“A Digital Neurosynaptic Core Using Embedded Crossbar Memory
with 45 pJ per Spike in 45nm”, P. Merolla et al., CICC, 2011
“TrueNorth: Design and Tool Flow of a 65mW 1 Million Neuron
Programmable Neurosynaptic Chip”, F. Akopyan et al.,
IEEE TCAD, 2015
“Real-Time Scalable Cortical Computing…”, A. Cassidy et al., SC’14
“Spiking Neuron Models”, W. Gerstner and W. Kistler, Cambridge
University Press, 2002