## Slide 1
Lecture: Spiking Networks Architecture
Topics: TrueNorth design, projects discussion

## Slide 2
The Spiking Approach
Low energy for computation: only adds, no multiplies
Low energy for communication: depends on spikes per signal
Neurons have state, inputs arrive asynchronously, info
in relative timing of spikes, other biological phenomena, …

## Slide 3
IBM TrueNorth
Product of DARPA’s SyNAPSE project
Largest chip made by IBM (5.4 billion transistors)
Based on LLIF neuron model
Lots of on-going projects that use TrueNorth to execute
new apps
Lots of limitations as well – all done purposely to reduce
area/power/complexity

## Slide 4
TrueNorth Core

## Slide 5
TrueNorth Core (Axonal Approach)

## Slide 6
TrueNorth Core (Dendritic Approach)

## Slide 7
Principles
Focus on low power (speed is secondary)
Low power with asynchronous circuits
Low power with high-Vt circuits and SOI process
A dendritic approach leads to fewer SRAM reads/updates
and is more deterministic
Also uses an under-provisioned network (giving rise to
the concept of “future” ticks)

## Slide 8
Receiving Spikes
Spikes arrive at the Scheduler; stored in a 256x16 SRAM
grid to indicate axon and time of the spike
The Token Controller receives spikes in a “tick” (and their
types – exc/inh); it then sequentially walks through 256
neurons – this dendritic approach makes the latency and
SRAM accesses more deterministic
It reads a 410-bit word from SRAM for that neuron (this
word has connectivity info used by Token Controller and
neuron parameters used by Neuron block
Based on connectivity and input spikes, instructions are
sent to Neuron block

## Slide 9
Neuron Block
Neuron computations are performed here (these are
non-trivial because of stochastic behaviors – more later)
A leak is introduced every tick for every neuron
After thresholding, a spike may be triggered
The neuron block uses synchronous circuits, but it is
active only when it receives instructions from the Token
Controller; the Token Controller, Scheduler, and network
Router are all asynchronous to exploit the low power
inherent in spike sparsity

## Slide 10
More Details
The 410 bit word: 256 synaptic connections, 4 9-bit weights,
9-bit leak, 8-bit threshold, 26-bit destination axon, 4-bit
delivery time, 9-bit potential, … (62 more bits)
The network may occasionally not handle a burst of spikes;
if this is likely, then spikes must have a future delivery time;
allows a spike to take multiple ticks to reach its destination
256x256 core; 4K cores; million neurons; 430 mm2;
65 mW on average; 28nm Samsung process; 1ms tick

## Slide 11
Limitations
A neuron can only have 256 inputs (no provision for partial
sums)
A neuron can only have one destination axon output of a
specific type (seen by 256 neurons)
Weight quantization (4 weights per neuron)

## Slide 12
Measurement Data
Because of the synch/asynch approach, the chip works
correctly even at 0.7V supply voltage (low power!); 0.7-1.05V
42 mW at 0.7V, 0 Hz firing rate, 0 synapses/neuron
323 mW at 1.05V, 200 Hz firing rate, 256 synapses/neuron
At 0.75 V, the max throughput (giga synaptic ops per second)
is 58 GSOP/s, the energy efficiency is 400 GSOP/sW
At 0.75 V, complex recurrent network, 20 Hz avg firing rate,
128 syn/neuron, 65 mW and 46 GSOP/sW
At low activity levels, the ticks can be sped up to 21 KHz

## Slide 13
More Results

## Slide 14
Improvements
4K chips on a rack
 4 B neurons, 300 W
for TN chips, plus more for
communication/FPGAs
-- 4 KWs (SC’14)
96 racks  412 B neurons,
1014 synapses (human
brain scale), 29 kW for
TN chips, few hundred kW
overall
Power and time, relative to
the Compass simulator,
running on the BG/Q
supercomputer and a dual-
socket Intel system

## Slide 15
Stochastic Neurons
The TrueNorth neurons have many stochastic parameters
Helps emulate many biological and non-linear behaviors
Continues to be low cost; applies the RISC argument
Stochasticity in input, state, and output
Different modes for leak, threshold, reset
Helps create a library of 50+ neuron models, including
the 20 defined by Izhikevich (using 1-3 neurons)

## Slide 16
Neuron Parameters
9 bits
256 bits
36 bits
4 bits
1 bit
9 bits
1 bit
8 bits
8 bits
8 bits
9 bits
1 bit
2 bits
8 bits

## Slide 17
Synaptic and Leak Probabilities
If the input is stochastic, the potential change is either
-1, 0, or +1. The probability of the incr/decr is determined
by the synaptic weight (compare the uniformly distributed
pseudorandom number PRN to the |weight|). The
incr/decr is determined by the sign of the weight.
Same for leak
Have to draw many random numbers for each neuron:
threshold, leak, each connected input axon

## Slide 18
Leak Modes
Standard leak operation: constant incr/decr of leak
Leak-Reversal mode: the leak sign flips when the neuron potential flips
No leak at zero potential
Creates a convergent leak and a divergent leak

## Slide 19
Negative Threshold
Crossing the positive threshold always produces a spike
There’s also a negative threshold that does not produce a spike
The negative threshold may either act as a floor, or as a “bounce”
to the negative reset voltage
The bounce allows us to create a neuron ON-OFF pair; they mirror
each other

## Slide 20
Stochastic Threshold and Reset
Can grow the threshold by a random number
Can set the max of this delta with a mask parameter
Three reset modes:
  Normal: after firing, the new potential = reset voltage
  (residual is discarded)
  Linear: after firing, the new potential = residual voltage
  (reset voltage is not used)
  Non-reset mode: no reset. Relies on leak and –ve synapses to
  lower the potential

## Slide 21
Synthetic Functions
Library of 50+ synthetic neuron behaviors (compatible with many
coding techniques)
Example: various arithmetic ops, rate store neuron
Rate store neuron: acts as a memory that is constantly being read (e.g.,
a state holding recurrent neuron); output freq a potential;
uses a stochastic threshold and non-reset mode;

## Slide 22
Arithmetic Ops

## Slide 23
Izhikevich Neuron Models

## Slide 24
Neuron Model
Need 924 gates for neuron computation and 348 for PRNG

## Slide 25
TrueNorth Networks
Could use rate coding and STDP/back-prop to implement
networks on TrueNorth (most early TrueNorth papers)
Many hardware constraints; must therefore use either
train-then-constrain or constrain-then-train (the latter is
usually better)
  Only 4 synaptic weights
  A neuron can only receive 256 inputs (narrow receptive field)
  A neuron can only have one destination axon/type (narrow
  projective field, although one can replicate a neuron to fix this)

## Slide 26
MNIST – NeurIPS’15
Spikes are discrete, but the probability of spiking is a
continuous function learnable through back-prop
Limited connectivity in each layer, but over a few layers,
a neuron can see every input
Inputs are provided in a single tick (spike with a probability
that corresponds to the input value)
With an ensemble of networks, the outputs correspond to
the expected value; accuracy of 99.42% on MNIST

## Slide 27
Implementing CNNs on TrueNorth
Small kernels: a neuron can only have 256 inputs
Conv layer has to replicate the shared weights
Can’t have more than 256 kernels
They use ternary weights and activations
A single spike (or not) for every pixel in every feature map

## Slide 28
Results
Most are with 8 TN chips

## Slide 29
References
“Cognitive Computing Building Block”, A. Cassidy et al., IJCNN’13
“A Digital Neurosynaptic Core Using Embedded Crossbar Memory
with 45 pJ per Spike in 45nm”, P. Merolla et al., CICC, 2011
“TrueNorth: Design and Tool Flow of a 65mW 1 Million Neuron
Programmable Neurosynaptic Chip”, F. Akopyan et al.,
IEEE TCAD, 2015
“Real-Time Scalable Cortical Computing…”, A. Cassidy et al., SC’14
“Spiking Neuron Models”, W. Gerstner and W. Kistler, Cambridge
University Press, 2002