## Slide 1
Lecture: SNN vs. MLP
Topics: comparing SNNs and MLPs in terms of
accuracy and hardware efficiency, SpinalFlow

## Slide 2
RISC vs. CISC, ML vs. Neuroscience
Questions answered in the MICRO’15 paper by Du et al.:
1. Can the neuroscience-inspired approach (SNN + STDP) achieve the
same accuracy as the machine learning inspired approach (MLP + BP)?
2. Is the cost of hardware SNN lower than that of hardware MLP?
3. When should a designer use hardware SNN or MLP?

## Slide 3
Workloads
Most of the paper focuses on small networks for MNIST
One small section on two other even smaller networks:
MPEG-7 object recognition
Spoken Arabic Digits for speech recognition

## Slide 4
SNN Set-Up
One layer with 300 neurons
Each neuron receives inputs from all 784 pixels
An image is shown; this results in spike trains for the next
500 cycles; 0-10 spikes in each train corresponding to
pixel values 0-255; spike intervals are drawn from a
Gaussian distribution
Weights end up being 8b or 12b
The winning neuron is the one with highest potential;
could also use first-to-spike or most spikes
Trained with STDP

## Slide 5
MLP Set-Up
8b fixed-point weights, inputs, operators
784 input neurons, 100 neuron hidden layer, 10 neurons
in output layer
Larger networks had marginally higher accuracies
Sigmoid activation function
Training with back-propagation

## Slide 6
Accuracies on MNIST
CNNs/DNNs have achieved accuracies of 99.21% and 99.77%
(60M+ synapses)
MLP with 800 hidden neurons: 98.4% (related work)
In this work, they focus on an MLP with 100 hidden neurons: 97.65%
SNN+STDP: prior works have achieved 93.5% (300 neurons) and 95%
(6400 neurons)
In this work, they achieve 91.82% with 300 neurons
They also introduce a simplified SNNwot model with accuracy 90.85%
SNNwot: SNN-without-time: send the number of spikes in a 500-cycle
window, ignore leak, much better in terms of speed (500x
better), 1% worse in terms of accuracy

## Slide 7
Bridging the Accuracy Gap
Starting with SNN+STDP, 91.82%
… they instead use back-propagation to train 95.40%
(using SNN computations, but computing the
error function and applying gradient descent)
MLP+BP with a step activation function 97.2%
MLP+BP with a sigmoid activation function 97.65%
(going from 32b fl-pt to 8b fx-pt takes accuracy to 96.65%)
Note that a TrueNorth paper achieved 99.42% accuracy
on MNIST by using BP and an ensemble of networks

## Slide 8
Potential Extensions
Are we handicapped by only using 10 spikes to encode
the input pixel?
By introducing stochasticity, can augment SNN so it has
a sigmoid activation function
Even better, can augment SNN to use ReLU
Can also make the network deeper/smaller

## Slide 9
MLP Implementation
Expanded design, i.e., there is a dedicated ALU/register for every neuron
and synapse (since the MLP is small enough)

## Slide 10
SNN Implementation
Expanded design. Input pixels are converted to 4-bit inputs. Using
4-bit multipliers in SNNwot. Using counters/accumulation in SNNwt.
Using MAX circuit to decide output (max of potential or spikes).

## Slide 11
Expanded Design Comparison

## Slide 12
Expanded Design Results
The 4x12 multiplier (SNNwot) is 8x cheaper than the 8x8 multiplier (MLP)
The SNN needs 3x more ALUs and storage than MLP
The SNN takes 3x less area for ALUs, but 3x more area for storage
All put together, SNN takes ~2x less area than MLP
SNNwt takes less area than SNNwot because it has simpler adders
A 15-10-neuron MLP has the same accuracy as the SNN – it also consumes
3x less area than SNN
For a small-scale design, they also evaluate delay and power

## Slide 13
Spatially Folded Designs
For a spatially folded MLP, each neuron is assumed to
have only ni inputs; must compute multiple partial sums;
need an SRAM buffer to store all weights and feed ALUs
They do not consider folding where multiple neurons
share a set of ALUs
Same approach for SNNs as well

## Slide 14
Spatially Folded Comparison

## Slide 15
Spatially Folded Results
Need more cycles to process all inputs, but the clock is faster
Small ni is very area-efficient and has high clock speeds
High ni is very energy-efficient because the task finishes sooner
SNNwt is not competitive in terms of time because we have to
sequence through 500 cycles (at least); but it consumes less
area because it uses adders instead of multipliers
Each SNNwt neuron has roughly the same area as an MLP neuron
(because of the SRAM, the multiplier complexities are less pronounced);
therefore, SNNwt consumes 3x more area because it uses 3x more
neurons
Bottomline: not much hw difference between an SNN neuron and an
MLP neuron; differences are because of #neurons needed
for high accuracy
Their conclusion: SNNs may be better when expanded (small networks)
or when on-line learning (STDP) is required

## Slide 16
Adding Features for On-Line Training
STDP: more counters, comparators, SRAM updates
Counters for refractory and inhibitory periods
Homeostasis: change the threshold so every neuron
has a roughly equal firing rate
Adding these features increases area by 1.3-1.9x, and
energy by <1.5x

## Slide 17
Other Benchmarks
MPEG-7 object recognition
MLP 15-10 99.7% accuracy
SNN 90 92% accuracy
Spoken Arabic Digits speech recognition
MLP 60-10 91.35% accuracy
SNN 90 74.7% accuracy

## Slide 18
Main Conclusions
MLP has an advantage in accuracy
Some of the gap can be bridged with BP, sigmoid,
better input encoding, etc.
For time-multiplexed hardware units, the neuron model
may not matter much
SNN has an advantage in on-line learning and for
spatially expanded designs

## Slide 19
Limitations of this Study
Small-scale workloads
4-bit rate coding (and no thorough evaluation of other codes)
Modeling other activation functions in SNNs (ReLU, sigmoid)(not MAX)
Considering the impact of stochasticity on SNN accuracy/cost
Considering the impact of the many TrueNorth modes on acc/cost
Finding the right balance of ALUs/storage/SIMD-ness
Need a much better analysis/breakdown for tiled large-scale designs
What about the SRAM overheads for neuron potential (Conv and FC)?

## Slide 20
Eyeriss vs. Spiking Eyeriss
Slowdown of 16x for a 16-tick input interval
Rate-coded energy results:

## Slide 21
Eyeriss vs. Spiking Eyeriss
Crossover points: 3bSp90 (rate) and 3bSp60 (temp)
Temporal coding energy results:

## Slide 22
SpinalFlow

## Slide 23
SpinalFlow Energy

## Slide 24
Accuracy Comparison

## Slide 25
References
“Neuromorphic Accelerators: A Comparison Between Neuroscience
and Machine Learning Approaches”, Z. Du et al., MICRO 2015
“SpinalFlow”, under review.