## Slide 1
Lecture: Self-Driving Cars
Topics: System analysis for two systems: with and
without LIDAR
Email me to communicate team/project and set up
meeting times
The next two slides show the major companies pursuing various levels of autonomy and the definitions for level 2-5 autonomy. In terms of hardware, we’ve already discussed the Tesla FSD chip, Audi has a new board, and NVIDIA has a Xavier SoC.
Some companies (Waymo) seem to be investing in LIDAR sensors, while others (Tesla especially) have committed to vision-based LIDAR-free solutions. LIDAR sends lasers and estimates object locations based on the reflections, thus producing a point cloud. LIDAR is known to be very expensive ($75K), but one can expect steady cost reductions. Waymo announced a 10x reduction in cost in early 2019; a short-range LIDAR may cost around $5K.

## Slide 2
Self-Driving Cars Intro
Several players: Waymo, Tesla, Mobileye, Uber, NVIDIA
Xavier SoC, Audi zFAS board
Level 2 autonomy: car handles steering/accel in limited
conditions, (alert) driver handles rest (hands-off)
Level 3 autonomy: car handles everything in limited
conditions, driver serves as back-up (eyes-off)
Level 4 autonomy: driver helps only when entering
unmapped areas or during severe weather (mind-off)
Level 5 autonomy: no steering wheel

## Slide 3
LIDAR vs. No-LIDAR
LIDAR is very expensive ($75K); hence, Tesla and Mobileye
are focusing on vision-based solutions
Recent announcements claim that top-of-the-line LIDAR
may cost $7,500, with short-range LIDAR being under $5K
https://techcrunch.com/2019/03/06/waymo-to-start-selling-standalone-lidar-sensors/
As we’ll see, LIDAR has other latency problems

## Slide 4
Self-Driving Car Pipeline
Need decimeter-level accuracy for localization; GPS fails; localizer
gives them centimeter-level accuracy
Need a locally stored map (41 TB for USA)
Three main bottlenecks in the pipeline. The detector and tracker use well-known DNNs. The localizer is the new and unintuitive step.

## Slide 5
Self-Driving Car Pipeline
Need decimeter-level accuracy for localization; GPS fails; localizer
gives them centimeter-level accuracy
Need a locally stored map (41 TB for USA)
Actually identifying landmarks and using trig equations to pinpoint where you are at cm resolution. Impressive! But needs a local map.

## Slide 6
Metrics
99.99th percentile tail latency of 100ms would be faster
than fastest human reaction times (target supported by
industry, but will likely be a moving target); 10 frames/sec
Power and cooling (need cooling because the computers
will be inside the cabin); 77W cooling for every 100W
dissipated; a 400W computer reduces MPG by 1; a
CPU+3GPU system (~1000W) lowers driving range by 6%
(and 11.5% once you add storage+cooling)
Also need high storage and reliability (recall that Tesla FSD
executes every computation twice)
The paper identifies important metrics. Not surprisingly, predictably low response times and power are the most important. The impact of these computers on driving range is clearly non-trivial.

## Slide 7
Algorithms
Object detection: YOLO; DNN based
Object tracker: GOTURN; DNN based and a few
book-keeping tables
Localization: ORB-Slam; lots of trigonometric calculations
Motion and Mission planning: MOTPLAN and MISPLAN
from Autoware
Of these algorithms, the localization one is new. But they aren’t very clear about what the feature extraction algorithm does (the blog post linked at the end has more details). The trig calculations are simplified with look-up tables.

## Slide 8
Bottleneck Analysis
DNNs implemented with Eyeriss and EIE
The CPU solution is clearly sub-optimal. This also shows that most of the time is in those three phases, with much of it spent in DNNs.

## Slide 9
Localization

## Slide 10
Feature Extraction
Ops in feature detector
not clear (a blog post
that may be helpful is
listed on the last slide)
Rest are trig ops that
are implemented with
LUTs

## Slide 11
Results
Power for a single camera
(Tesla has 8)
For the whole system, GPU
lowers driving range by 12%
and ASICs by 2%
They do much better with ASICs. The GPU does great too, but consumes too much power. The FPGA is fine if an ASIC is not possible. The overall latency is close to the 100ms target.

## Slide 12
Scalability Results
VGG accuracy improves from 80% to 87% when resolution is doubled
Not clear how the bottlenecks change (compute, memory, reuse patterns)
The accuracy improvement with higher resolution is compelling. But they show that latency is too high. Can probably do it with multiple ASICs. The system will also scale up along other axes: more cameras, higher resolution, more redundancy, larger networks.

## Slide 13
Summary
Detection, Localization, Tracking, Planning are major steps
The first three take up 94% of compute
Contributions: a pipeline with publicly available frameworks,
bottleneck analysis, acceleration with GPU/FPGA/ASIC
GPUs and ASIC offer two orders of magnitude speedup,
but GPUs consume too much power
More work remains – lower latency, lower power, higher
resolution, feature extraction, other bottlenecks

## Slide 14
LIDAR-based Approach [Zhao et al.]
Joint work with Pony.AI; characterization based on several
hours of driving on their test fleet over 3 months
They rely on LIDAR and their software pipeline has
relatively little DNN
The second paper considers a LIDAR-based pipeline. It does have a limited amount of DNN computation. But as shown in the next slide, 65% of the computation is LIDAR based perception. This last computation is itself spread across several functions, of which Segmentation is the largest (the computations that identify/separate major objects from the background). This makes it harder to create an accelerator that improves all the functions. It turns out that LIDAR perception has varying latency based on the nature of the point cloud. Scenes with more nearby objects take longer to analyze; this is especially problematic since those are the scenes that need speedy resolution.

## Slide 15
Software Pipeline

## Slide 16
LIDAR Pipeline
Several steps, with segmentation
being a major overhead
Segmentation extracts useful
semantic info (relevant objects)
from the background
The latency is worse when there
are more nearby objects, since
there are more reflected points
to deal with
This leads to high variance,
especially when collisions are
more likely

## Slide 17
LIDAR Perception Latency
Max time is a relevant metric because it disproportionately
impacts safety
They observe that long LIDAR perception latency also
disproportionately impacts overall latency
(The LIDAR sampling rate is 100ms)
The authors show that if LIDAR perception latency exceeds the LIDAR sampling rate (100ms), the impact on other stages of the software pipeline is even higher.

## Slide 18
Safety Score
They compute a safety score that factors in the response
time along with velocity/acceleration
They design a predictor to estimate response time based
on the count/proximity of objects in the scene and how
hardware resources (CPU/GPU) are allocated to each part
of the software pipeline
To improve performance, they first predict if the point cloud will take longer to analyze, if yes, then they re-allocate CPU/GPU resources across the many software functions. The impact is evaluated with a safety score that shows how the response latency ultimately impacts safety. The equation factors the sampling rate, vehicle acceleration and velocity.

## Slide 19
References
“The Architectural Implications of Autonomous Driving: Constraints
and Acceleration”, S.-C. Lin et al., ASPLOS 2018
“Towards Safety Aware Computing System Design in Autonomous
Vehicles”, Zhao et al., Arxiv, 2019
“Driving into the Memory Wall”, Jung et al., MemSys 2018
ORB-Slam details:
https://medium.com/software-incubator/introduction-to-orb-oriented-fast-and-rotated-brief-4220e8ec40cf