## Slide 1
Lecture: In-Memory Processing
Topics: in-SRAM (Neural Cache) and in-DRAM (DRISA)
processing for DNNs, discussion for projects

## Slide 2
Compute Cache and Neural Cache
Key enablers: most of the processor die is occupied by large
caches; new circuits show how the cache can also perform
simple bit-wise operations (AND, NOR)

## Slide 3
Addition
Words are placed in transpose fashion, bit-serial addition
Need a latch for Cin, result is placed back in SRAM
Takes N steps (2N reads, N writes) to process N-bit addition

## Slide 4
Circuits
Must operate at a lower voltage to avoid disruption.
Hence slower, clock goes from 4GHz to 2.5GHz.

## Slide 5
Details
While addition requires N cycles/reads/writes, there is
massive parallelism – a million parallel ops in a 35MB cache
Each op is a single cycle (baseline cache access is 30 cycles)
This is an easy way to “neurify” an existing CPU
Area overhead of 7% per 8KB subarray and 2% for the chip
Bit-Serial is also useful for variable precision accelerators
The read and write overhead are similar to the baseline,
but no ability to reuse data through registers,
but no long-range data movement on the H-Tree,
and avoids a million latch/AND/NOR circuits.
But, we haven’t yet talked about multiplication …
Also note that analog crossbars handled many more inputs

## Slide 6
Multiplication
For each bit of the multiplier, add the multiplicand to the psum
Each addition takes N+1 cycles
Total operation takes N2 + 5N -2 cycles (O(N2) subarray rd/wr)
Still beats CPU and GPU by 18x and 8x on DNN workloads

## Slide 7
Circuit with Multiplication

## Slide 8
Reduction
Requires a copy/move circuit in the periphery

## Slide 9
DRISA
Many more bitlines available in DRAM
2 major challenges: destructive reads, cost-sensitive chips
Must therefore copy a row before computing on it
Different circuit: when 3 rows are activated, the result is
the majority value, can set/reset the third row to
implement either AND/OR
Multiple different implementations: NOR-capable 3T1C
or AND/OR-capable 1T1C with additional peripheral logic
Multiplications are the bottleneck again
1.2x energy efficiency and 9x performance over DaDianNao
ComputeDRAM: shows that such capabilities can be
emulated on off-the-shelf DRAM by violating timing params

## Slide 10
References
“Neural Cache: Bit-Serial In-Cache Acceleration of Deep Neural
Networks”, C. Eckert et al., ISCA 2018
“DRISA: A DRAM-Based Reconfigurable In-Situ Accelerator”, S. Li et al.,
MICRO 2017
“ComputeDRAM: In-Memory Compute Using Off-the-Shelf DRAMs”,
F. Gao et al., MICRO 2019