## Slide 1
Lecture: 3D CNNs, Gradient Compression
Topics: Diffy, Morph, Gradient Compression

## Slide 2
3D CNNs
Used for video processing
Examining a series of F images in one step
T is typically 3
Note that F reduces as we advance (also because of pooling)

## Slide 3
Overheads
The 3D aspect greatly increases the amount of compute
required for convolutional stages; also ifmap sizes
3D CNNs exhibit a new dimension of reuse
Variable behavior across layers

## Slide 4
Variability across Layers
Different ways to parallelize, tile, loop order
Figures below show the impact of different orders for the
outer and inner (tiled) loops
Different sized buffers for each layer

## Slide 5
Buffer Hierarchy
Because of the impact of data management and tiling, need
a deeper hierarchy (more so than in the 2D case)
They argue for a 3-level buffer hierarchy
New ideas: allocated per layer: banks per structure, order
and tiling, broadcast/multicast to PEs, NoC

## Slide 6
Diffy
Key observation: a feature map has many similar pixels, it
is more efficient to represent pixels as deltas
Bit-serial architectures can exploit this to finish the task
sooner and use less memory to store feature maps
This notion of differential convolution applies more to
image processing kernels than to DNNs; such image
processing kernels aren’t doing feature extraction but just
doing pixel-by-pixel predictions (e.g., de-noising)
The activation functions in DNNs reduce pixel similarity
or make it zero (zeroes can be exploited in other ways);
therefore, mostly effective in early layers of DNNs
7.1x better than value-agnostic accel (1.4x over zero-aware)
DNNs: 1.16x better (2x in early layers) than zero-aware

## Slide 7
Entropy
Effectual terms with diff vs. raw can be higher or lower for each element; it’s usually lower; on average, effectual terms are 1.9 and 3.6; sparsity is 48% and 43%

## Slide 8
Computation Structure
For each row, we do the first conv with raw values and other convs with diffs; the results are then added (not required if no activation function or if the next layer can accept diffs as well)

## Slide 9
Mapping to Bit Serial Architectures
Note that the baseline has many parallel bit-serial MACs
Generally limited by the slowest MAC (longest inputs)
Best to do the raw computation for each filter in parallel
(slow); followed by faster diff computations in parallel
Can apply a similar concept to 3D CNNs with temporal
locality (see ISCA’19 paper)

## Slide 10
Distributed Training
Training is typically distributed across several GPUs/TPUs
Two primary forms of parallelism:
  Data parallelism: full model on each GPU; each GPU handles a different image; gradients are aggregated before starting the next mini-batch; best for convolutions (exchange: gradients, no fmaps)
  Model parallelism: full image on each GPU; each GPU handles a subset of the model & neurons; best for FC (fmaps are exchanged)
Data parallelism is more common; must reduce gradient
exchange; also useful for federated learning

## Slide 11
Deep Gradient Compression
Store gradient changes locally; only transmit the ones
that exceed a threshold; akin to selective batch size;
enables higher threshold and even higher compression
Also attempting a number of other ML tricks: momentum
correction, local gradient clipping, momentum factor
masking, warm-up training (less aggressive DGC at first)
Able to reduce gradient exchange by 270-600x; from
100s of MB to < 1MB

## Slide 12
References
“Deep Gradient Compression: Reducing the Communication Bandwidth
for Distributed Training”, Y. Lin et al., ICLR 2018
“Diffy: a Déjà vu-Free Differential Deep Neural Network Accelerator”,
M. Mahmoud et al., MICRO 2018
“Morph: Flexible Acceleration for 3D CNN-based Video Understanding”,
K. Hegde et al., MICRO 2018
“Learning Spatiotemporal Features with 3D Convolutional Networks”,
D. Tran et al., ICCV 2015