## Slide 1
Lecture: Molecular Dynamics
Topics: sequence alignment wrap-up, Anton for moldyn

## Slide 2
Precision Medicine

## Slide 3
Burrows-Wheeler Transform
A data transformation that is reversible and amenable to compression
Transformation |  |  |  | 
Input | All rotations | Sorted into lexical order | Taking last column | Output last column
^BANANA¦ | ^BANANA¦ ¦^BANANA A¦^BANAN NA¦^BANA ANA¦^BAN NANA¦^BA ANANA¦^B BANANA¦^ | ANANA¦^B ANA¦^BAN A¦^BANAN BANANA¦^ NANA¦^BA NA¦^BANA ^BANANA¦ ¦^BANANA | ANANA¦^B ANA¦^BAN A¦^BANAN BANANA¦^ NANA¦^BA NA¦^BANA ^BANANA¦ ¦^BANANA | BNN^AA¦A
When applied to text, you’ll see many consecutive occurrences as below.
Note that the last column is highly compressible.
he dog … T
he object … T

## Slide 4
BWT Applied to Sequence Alignment

## Slide 5
Burrows Wheeler Alignment
The trie structure reduces the storage requirement; strings with common
suffixes share a portion of the trie
Because the strings are sorted, each node must only store two
numbers to capture the many possible matching locations
In addition to the above “compression”, the many matching locations
are determined in O(w) time, where w is the string length; this is
true for perfect matches (see example for GO on previous slide)
For approximate matches, you may have to navigate a significant
portion of the trie (see example for LOL on previous slide)
Note that memory access pattern is quite random, but capacity is low

## Slide 6
Molecular Interactions
DNA and RNA eventually produce the protein (a sequence
of amino acids) – these proteins fold into a particular 3D
structure that determines their behavior – gene mutations
result in potentially incorrect protein expressions that can
result in functionally incorrect folds
Drug delivery – does it bind to carriers in the blood – does
it bind to the appropriate receptors

## Slide 7
Anton
Research supercomputer by DE Shaw Research to accelerate molecular
dynamics simulations; Anton in 2008; Anton 2 in 2013; a “microscope”
for biochemistry; specialization before it was cost-effective

## Slide 8
Scale of Mol Dyn
Simulations are performed in time steps; each time step
is a few femto-seconds (10-15 seconds)
Interesting interactions happen at the scale of milli-seconds;
must therefore simulate 1012 steps
Anton introduces a 1000x speedup, enabling milli-second
simulations in a couple of months
Anton 2 introduces an additional 5x speedup
42 kW/rack; 190 W Anton 2 chip; 408 mm2 chip

## Slide 9
Anton Goals
Trying to do one step involving 10s of thousands of atoms
in 1000s of cycles
New hardware, new algorithms for higher parallelism and
lower inter- and intra-chip communication
Low latency compute and communication
Can’t use speculation because each step depends on
the previous step
Related: Folding@home explores many parallel
trajectories on very short time scales

## Slide 10
Biochem Background
Modeling a small (repeating) volume of protein, solvent,
and other chemicals
Two significant steps: force calculation and integration;
integration applies Newton’s laws and is also non-trivial
Forces are of two types: bonded and non-bonded
Bonded: force between an atom and other atoms that
share a covalent bond – an atom is typically bonded to
<4 atoms, so calculating these forces takes linear time
Non-bonded forces: van der Waals and electrostatic

## Slide 11
Biochem Background
Non-bonded forces are the bottleneck because there are
a quadratic number of interactions
van der Waals: weak forces among atoms because of
varying electron positions within the atom; these are weak
enough that we can ignore them beyond a cutoff radius
Electrostatic forces cannot be ignored, but we can
approximate some of the long-range interactions
Within a small radius, the pairwise interactions (vdw and es)
are calculated; at long-range, they use FFT-based
techniques to compute the es forces (charges are mapped
to a mesh)

## Slide 12
Parallelization
The space is partitioned into smaller boxes; each
computational “node” is responsible for its home box
They use a “neutral territory (NT)” method where a node
computes close-range interactions for its home box and
parts of two neighboring boxes
The particles in a node are split into “tower” (home box and
one neighbor box) and “plate” (home box and the other
neighbor box) groups; every element of tower is interacted
with every element of plate
This is the key step that requires the most time and hw

## Slide 13
Amdahl’s Law Analysis
Must target everything to get 1000x

## Slide 14
Contributions
Specialized pipeline for non-bonded nearby interactions
Programmable processor with custom ISA for all other
operations
Accumulation at the memory system; little on-chip storage
Network support for m-cast and compressed sparse packets
Synchronization and push-based communication

## Slide 15
Architecture
512-node torus; a node has a chip, attached DRAM, and 6 ports;
4 nodes per board; 32 boards per rack; 4 racks

## Slide 16
Anton Chip

## Slide 17
HTIS – Hi-Thruput Interaction Subsystem

## Slide 18
HTIS – Hi-Thruput Interaction Subsystem

## Slide 19
HTIS – Hi-Thruput Interaction Subsystem
Particles are received through push-communication from neighbors
ICB buffers these and controls the systolic array computations
32 PPIMs store parts of the tower particles; the plates are replicated
four times and are streamed to each of the rows
At each step, 8 matches are performed to identify the pairs that must be
processed; these are then sent thru the rest of the pipeline
26-stage PPIM pipeline at 800 MHz; rest of the chip operates at 400 MHz;
the pipeline is fixed-function and uses variable precision
Each PPIM stores the forces collected for the tower; the plates carry
their forces as they move to the right; the forces from the four rows are
merged at the end and sent to the appropriate buffers; at the end, the
tower forces are streamed out as well
DRAM is only used when spilling very large simulations; on-chip cache
is enough to handle most working sets

## Slide 20
Flexible Subsystem
Responsible for several complex operations; the GP cores handle
control flow; the remote access units have scratchpads and take
care of data movement; the geometry cores take care of SIMD
calculations; the racetrack is used for intra-node communication

## Slide 21
Speedups

## Slide 22
Anton 2
Power: 75 W 190 W
Size: 300 mm2 408 mm2

## Slide 24
References
Anton papers and presentations at: ISCA’07, HotChips’08, SC’09
Anton 2 papers at: HotChips’14, SC’14

## Slide 25
Title
Bullet