## Slide 1
Lecture: Systolic Arrays II
Topics: algorithms for addition/multiplication, solving a
system of linear equations, graph algorithms, sort
Schedule for next week:
  Tuesday:
  Thursday:

## Slide 2
Motivation
How can accelerator computations be performed
efficiently?
  Basic adds, multiplies, convolutions
  While you may not directly use the algorithm as shown, it might
  inspire other applications of the same technique
Broaden our knowledge beyond dot products
Last class: using arrays of simple processors (systolic
arrays) to perform sorting and matrix multiplication
This class: algorithms for addition and multiplication on
linear arrays/trees, solving a system of linear equations,
graph algorithms

## Slide 3
Adding Two N-bit Numbers
Propagating the carry takes N steps – can we do better?
Recall the generate, propagate, and stop signals
a = 1010
b = 0011
c = 0010
psgp
s g p p g p s s p p s g p p p s
Carry =
Each carry depends on the leftmost non-p bit to the right

## Slide 4
Using a Tree – Log(N)
Carry Lookahead
s
s s
s g s s
s p g s p s p s
s g p p g p s s p p s g p p p s
Propagate to the root: is the sub-tree generating a carry?
node = value of its leftmost non-p child
or p if both children are p

## Slide 5
Using a Tree – Log(N)
Carry Lookahead
s
s s
s g s s
s p g s p s p s
s g p p g p s s p p s g p p p s
Leaves: remember the first non-p value you’re going to see
Remember: s g g s s s g s

## Slide 6
Using a Tree – Log(N)
Carry Lookahead
s
s s
g g s s
p p s s s s s s
g g p p p p s s p p g g p p s s
As values are propagated to the root, copy the right
child to the left child
Remember: s g g s s s g s s

## Slide 7
Using a Tree – Log(N)
Carry Lookahead
s
s s
g g s s
p p s s s s s s
g g p p p p s s p p g g p p s s
The root is the carry of the final sum. We’ll swap it out
with s (since there is no carry-in from the right
non-existent subtree)
Remember: s g g s s s g s s

## Slide 8
Using a Tree – Log(N)
Carry Lookahead
s
s s
g g s s
p p s s s s s s
g g p p p p s s p p g g p p s s
Start pushing a node to its children. Note that leaves
are remembering the first non-p value they see.
Remember: s g g g g s s s s s s g s s s s

## Slide 9
Adding N k-bit Numbers
Can build a tree of adders (DaDianNao); logN additions;
each addition is O(logk); therefore O(logN * logk)
Instead, we’ll do it in O(logN + logk) – called a Wallace
Tree – used in the SNN vs. ANN study (MICRO’15)
Based on the insight that adding 3 bits gives us 2 bits, i.e.,
we can add 3 numbers to produce two numbers.
A: 1 0 1 1 0 0 0 1
A’: 0 1 1 0 1 1 0 1
A’’: 1 0 1 0 0 1 0 0
D: 0 1 1 1 1 0 0 0
C: 1 0 1 0 0 1 0 1

## Slide 10
Wallace Tree
Each level shrinks 3 inputs to 2 inputs in a single cycle;
log3/2N levels; adding the last 2 numbers takes logk

## Slide 11
Multiplication of Two N-bit Numbers
See typical multiplication example on next slide
Essentially, adding N 2N-bit numbers – we know that’s
do-able in O(logN) time, but requires more than O(N)
hardware (O(N2) work)
We’ll try to do it with O(N) hardware in O(N) time (4N-1 steps)

## Slide 12
Multiplication Example
Multiplying 7x6 = 42
1 1 1
1 1 0
0 0 0
1 1 1
1 1 1
1 0 1 0 1 0
b3 b2 b1
a3 a2 a1
a1b3 a1b2 a1b1
a2b3 a2b2 a2b1
a3b3 a3b2 a3b1
p6 p5 p4 p3 p2 p1
This is the definition of a 1D conv.

## Slide 13
1D Convolution
Need 2N processing elements to multiply 2 N-bit numbers
Inputs are fed from left and right with gaps (why gaps?)
Each processing element accumulates the corresponding
bit of the product
The generated carry has to also move leftward

## Slide 14
Example
Convolution of
5 (101) and 7 (111)

## Slide 15
Analysis
4N-1 steps because a 2N input has to go across 2N PEs
But every PE is idle in alternate cycles – can improve
efficiency by interleaving two multiplications or by
wrapping the linear array into two rows
This is also one approach for computing a 1D convolution;
extending to 2D and 3D convolutions is not straightforward

## Slide 16
Solving Systems of Equations
Given an N x N lower triangular matrix A and an N-vector
b, solve for x, where Ax = b (assume solution exists)
a11x1 = b1
a21x1 + a22x2 = b2 , and so on…

## Slide 17
Equation Solver

## Slide 18
Equation Solver Example
When an x, b, and a meet at a cell, ax is subtracted from b
When b and a meet at cell 1, b is divided by a to become x

## Slide 19
Complexity
Time steps = 2N – 1
Speedup = O(N), efficiency = O(1)
Note that half the processors are idle every time step –
can improve efficiency by solving two interleaved
equation systems simultaneously or by wrapping the
linear array

## Slide 20
Inverting Triangular Matrices
Finding X, such that AX = I, where A is a lower triangular
matrix
For each row j, A xj = ej , where ej is the jth unit vector
(0,…, 0, 1, 0,…, 0) and xj is the jth row of matrix X
Simple extension of the earlier algorithm – it can be
applied to compute each row individually

## Slide 21
Inverting Triangular Matrices

## Slide 22
Gaussian Elimination
Solving for x, where Ax=b and A is a nonsingular matrix
Note that A-1Ax = A-1b = x ; keep applying transformations
to A such that A becomes I ; the same transformations
applied to b will result in the solution for x
Sequential algorithm steps:
  Pick a row where the first (ith) element is non-zero and
  normalize the row so that the first (ith) element is 1
  Subtract a multiple of this row from all other rows so
  that their first (ith) element is zero
  Repeat for all i

## Slide 23
Sequential Example
2 4 -7 x1 3
3 6 -10 x2 = 4
-1 3 -4 x3 6
1 2 -7/2 x1 3/2
3 6 -10 x2 = 4
-1 3 -4 x3 6
1 2 -7/2 x1 3/2
0 0 1/2 x2 = -1/2
-1 3 -4 x3 6
1 2 -7/2 x1 3/2
0 0 1/2 x2 = -1/2
0 5 -15/2 x3 15/2
1 2 -7/2 x1 3/2
0 5 -15/2 x2 = 15/2
0 0 1/2 x3 -1/2
1 2 -7/2 x1 3/2
0 1 -3/2 x2 = 3/2
0 0 1/2 x3 -1/2
1 0 -1/2 x1 -3/2
0 1 -3/2 x2 = 3/2
0 0 1/2 x3 -1/2
1 0 -1/2 x1 -3/2
0 1 -3/2 x2 = 3/2
0 0 1 x3 -1
1 0 0 x1 -2
0 1 0 x2 = 0
0 0 1 x3 -1

## Slide 24
Algorithm Implementation
The matrix is input in staggered form
The first cell discards inputs until it finds
a non-zero element (the pivot row)
The inverse r of the non-zero
element is now sent rightward
r arrives at each cell at the same
time as the corresponding
element of the pivot row

## Slide 25
Algorithm Implementation
Each cell stores di = r ak,I – the value for the normalized pivot row
This value is used when subtracting a multiple of the pivot row from other rows
What is the multiple? It is aj,1
How does each cell receive aj,1 ? It is passed rightward by the first cell
Each cell now outputs the new values for each row
The first cell only outputs zeroes and these outputs are no longer needed

## Slide 26
Algorithm Implementation
The outputs of all but the first cell must now go through the remaining
algorithm steps
A triangular matrix of processors efficiently implements the flow of data
Number of time steps?
Can be extended to compute the inverse of a matrix

## Slide 27
Graph Algorithms

## Slide 28
Floyd Warshall Algorithm

## Slide 29
Implementation on 2d Processor Array
Row 3
Row 2
Row 1
Row 1
Row 3
Row 2
Row 1/2
Row 3
Row 1/3
Row 2
Row 1
Row 2/3
Row 2/1
Row 3
Row 2
Row 3/1
Row 3/2
Row 1
Row 3
Row 2
Row 1
Row 3
Row 2
Row 1

## Slide 30
Algorithm Implementation
Diagonal elements of the processor array can broadcast
to the entire row in one time step (if this assumption is not
made, inputs will have to be staggered)
A row sifts down until it finds an empty row – it sifts down
again after all other rows have passed over it
When a row passes over the 1st row, the value of ai1 is
broadcast to the entire row – aij is set to 1 if ai1 = a1j = 1
– in other words, the row is now the ith row of A(1)
By the time the kth row finds its empty slot, it has already
become the kth row of A(k-1)

## Slide 31
When the ith row starts moving again, it travels over
rows ak (k > i) and gets updated depending on
whether there is a path from i to j via vertices < k (and
including k)
Algorithm Implementation

## Slide 32
Shortest Paths
Given a graph and edges with weights, compute the
weight of the shortest path between pairs of vertices
Can the transitive closure algorithm be applied here?

## Slide 33
Shortest Paths Algorithm
The above equation is very similar to that in transitive closure

## Slide 34
References
“Introduction to Parallel Algorithms and Architectures,” Leighton
Figure credits: Mitsu Ogihara